## Slide 1: PowerPoint 5: Know the different types of structures in the built environment
PowerPoint presentation
Unit 101: Introduction to the built environment

## Slide 2: Transport infrastructure
People and goods are transported around the country and the rest of the world using a range of interlinking networks.
Roads: link local and national locations, towns, cities, airports, docks etc.
Rail: links major towns and cities to docks and airports.
Air: airports link regional and internal destinations, carrying people and goods.
Water: canals were traditionally used to transport goods before the railways were built but are now mainly used for leisure. Modern ports are all deep water to accommodate large ships and tankers transporting raw materials and goods internationally.

## Slide 3: Highways
Types of highways in the UK include:
Motorways: A network of major roads, normally three lanes wide, connecting all parts of the UK and
avoiding built-up areas.
A/Trunk roads: Major roads between towns and cities that can be both single and dual carriageways. There are over 28,000 miles of A roads in the UK.

## Slide 4: Highways (continued)
B and unclassified roads: Minor roads often serving smaller towns and villages, ranging in size from dual carriageways to single lane with passing points.
Cycle paths: A UK-wide network of paths and routes for walking and cycling. These can run alongside an A/B road or be an altogether separate path.

## Slide 5: Bridges
A bridge is a structure that crosses an obstacle such as a river, valley or another road, without impacting on the obstacle. Bridges can be built using one of five main construction methods, or by a mix of these.
2. Beam bridge – e.g. road bridge in Cardigan
1. Arch bridge – e.g. Inigo Jones bridge, Llanrwst, North Wales

## Slide 6: Bridges
3. Truss bridge – e.g. Ballachulish Bridge, Glencoe
5. Suspension bridge – e.g. Menai Suspension Bridge
4. Cantilever bridge – e.g. The Forth Bridge

## Slide 7: Viaducts and aqueducts
A viaduct is a long bridge-like structure consisting of a series of arches that carries a road or railway across a valley or gorge.
An aqueduct carries water from a source to a distribution point. Canals often have aqueducts to cross valleys or low-lying areas in much the same way as a viaduct.
Pontcysyllte aqueduct
Chirk and Cefn Mawr viaduct

## Slide 8: Tunnels
Tunnels are artificial underground passages built to go through an obstacle, such as a hill, or under buildings, roads or a body of water.
Types of tunnels
Cut and covered: A simple method of constructing a shallow tunnel, where the ground is excavated, and a supporting overhead structure is installed then back-filled.
Bored: This involves drilling through a solid land mass or under a body of water and then lining the tube.
Immersed tube: A concrete structure is prefabricated on land and floated out to its final location, where it is sunk, joined together and then the water is pumped out to leave a dry tunnel.

## Slide 9: Example of a bored tunnel
Notes: data:image/jpeg;base64,/9j/4AAQSkZJRgABAQAAAQABAAD/2wCEAAkGBxMSEhUSExMVFhUVFxcXFxYYFxgXGBcaFxcWFxoXFRcYHSggGBolGxUXITEhJSkrLi4uFx8zODMsNygtLisBCgoKDg0OGg8QGi0eHSUvLS0tLS4tLS0tLS0rLjctLS0tLS0vMy0rLSsrKy01Ky0tKy0tLS0rListLS8tLSstLf/AABEIALcBEwMBIgACEQEDEQH/xAAbAAABBQEBAAAAAAAAAAAAAAAAAQIDBAUGB//EAEMQAAEDAQQGBQoEBgEEAwAAAAEAAhEDBBIhMQUTQVFh8AYicYGRFBYyQlKSobHR4WJywfEVI1OCotLCc4OTsgczQ//EABoBAQEBAQEBAQAAAAAAAAAAAAABAgMEBQb/xAAsEQEAAQMCBQIGAgMAAAAAAAAAAQIREwMSBCExQVEiUjJxgZGh8GGxIyRC/9oADAMBAAIRAxEAPwDm0LW83q34fe+yXzerfh977L9Vvp8vx+OrwyFctDAKNIwJLqsnaYuRPifFW/N2tub732U9XQlY02MhvULzN7O9d4fhWZri8c/2zdNE2nl+3YKFr+blf8HvfZL5uV9zfe+y1vp8sbKvDHSrX826+5nvfZL5tV9zPe+yb6fJsq8MdC2fNmvuZ732R5sV9zPe+yZKfJsq8MZb1n6PB9nbVFQ33U31BThhm5U1d0de/jnN2BBkqMdF7RuZ732V6no23Np6prwGQRAcBg43iL129BJOErnqVTMRsmIddKIiZ3xdUPRO0B112rb6IkuIEufqw3KZvEDKMQZIxUY6M2iGOLWi/kJMjqucCQAZkMODZOWGIWg/R9vJkvbMtOBaJLXXw4w3E3sZzJzlKNH2/DrsMSMbhkEOaWulvXbD3C66QA4wue7V90OltL2yrt6KuAdrKtNjm62Rjhq6bKkk7GkPGyRhvgVKOgnF9dj3tY6gGk7b157WdUj84PeBtkaVTR1vcHA1GkPm8JbjLBTPq4SxoGG4Jg0Rbb73323qgh5vDrDDMRHqjwSKq+9UExp9qZQ1OiNbWOawse0FwD5w6tQ07roGDpHYN8Jmiejjq9J72uh7KrKdwjO8QHOmcLsyeAKsWmhbqTXPL5AvOIF1/pOvuddLYm91pzGyFm6HdaXk06DnDNxxgCWlhJPFriO9X/LNM+qP3yn+KKo9Mr1t6J1WufqyH02uAa49UvkMJMYgAawZmcDAMFRU+i1dzwxppkkYEOJEh7qZbIGBDmkE5cVeOjrec6jTJBklpIIu+ibstHUZIGBuiZTqNh0gz0ajc73qmDec+8JaYN57jOfWKzu1bfFDUxpTN9ssqy6IaawpvqXBqmVZN0El9NjwwFzg1pN8AFxHjgrNp6LuE3ajcHVARU/llrabGPL3YkRDxkTmCCZU1LQ9ta/WBzb1wMJkEFgAaGFpbDmw1ogjYE+po23uDgagIeXF3WGN5oYdmALQBAwgDcFZqrvyqhIjTtzplSp9GqtzWOLQ0sc4OByhrXdaQMIdm2du0Qs3Sti1FapRvB2rcW3hkY4bOxdC/R1vLS01GwRBxaJF0M6xDZcbrQJOOAVS1dHrXUeXvLHOdiTeAJMRJgZ4LVFdV/VVDOpTRMemJu55C3fNS0bme99knmraNzPe+y7ZKfLhjq8MNC3PNS0bme99keato3M977Jkp8myrwxFbLB5PegTrYnbFyY8Voeato3M977KfzdtGq1cM9O/N/8ADdjJZqrp5WlqmiefJzqRbnmraNzPe+yPNa0bme99lrJT5Z2VeGGlW35rWjcz3vsk81rRuZ732TJT5NlXhipFuea1o3M977ITJT5Nk+HZ6pApLU1HBLqOC+dkfRxyy9Unapaeo4JdRwUyGKWZqeCXVcFpajgl8n4JkXFLN1PBLqlpahLqFMhhZupS6krR1CXUpkXCzdUUuqK0dQjUKZDCztUUuqK0NSl1KZFws7VpdWtDUo1KZDCz7ihsthZTBDGBoJJMbSVrakJdSEyGFn3EXFoagI8nCZFwyz7iLi0PJwjycJkMMs64i4tHycJPJwmSDDLPuJNWtHUJNQmRMLP1aTVrR1CNSmQws7Vo1a0dSk1PBMiYmfq0ataGoSGgrkMShcSXFoahJqEyQmKVC4hXtQhN5ild1aNWtC5wS3OC8mR9HEztUlFJaIZwTrn4VMhiZ2pSijxWjc/ClufhUyNYoZ4ocUvk60QzgluLOSVxM8WZL5Mr9xLcTJK4oUPJ0eTK/cRcUyLjhQ8mR5MFfuIuJkMUKHk/BLqOCvXEtxMhjhQ1PBGqG5X7iLimQxwoaobkuqG5XriLibzGo6oeyjVD2VeuIuJvXGo6obkakbleuJLibzGpakbijUjcrtxF1XemNS1HBGoG5XbiLibzGpajgk1HBXdWjVpvMal5PwSGzq7q0apN5jhRNnSGzq9qe1IaHFXImOFDyZCvahCuRMS1CW6vOrLpq0033zVNRowNNxABnjGBxzWo7psGu61CpdjEgtJnDAAwIzxncvnRxVH/AHen5/tnpnl2djdS3VnWDStGsAWVWyQDdJAcOBbmCtALvFUVReJuFhF1KhVSQi6lQgSEQlQgSEQlQgSEEJUiCF9pYL0uAuRex9GcRO5ShZlr0UXuebwAfMiM4Y0NnscJ70N0Y68SXSC6e0Xr0HsGG3uyW7U26uO6u/wtJ7gBJyCjqWhjSGlwBMQO0wPE4LNdop/tD0bs4zF0iMt+OfdtVq12NznhwIHoicQcCTkMHAzkcktT5N9dvhXGuBEgyEgqCYkTu7p+RWY3RRDY6uTQN0Bzid8SCNhyT7Jo5zS0uIcWnjlca3D3Z70tT5Irr5elpwiEqFh2JdRdSoQJdRdSoQJCISoQJCISlRms0YFw8QpcPhEKG0WynTF572MBwBc4NBO4Elc3bOn1kZkXvguButw6piZJAIMYEdqxVq0U/FNk5OqhJdVDR+nLPWANOswmA67eF4A+0MwVafbKYxL2DtcAtRXTMXiVS3UKidOWYYa+l77fqhZzUe6PunJ57BTh8E1pTpXndkT6LDmAtPRulqtBoYw9UeqcRjxzVAJYUimKZvEc0tDbf0prn0dUO1rj8Q8fJVz0rtmxtnPYH/q5ZQcgnmCu9OvVHaJc6tGKu8x8paPnhbBnRp9zXH5PTvPO1DOi33Kn1WbCJ2yuscVHeiHCeFq7aktLz5q7W0x3OH6p7em9TdT/AMvqsy8ePimlgOYB7RPzW44nT70flieG1u2p+GyOmj91P4/VOHTJ+6n8fqsA2ZhzYzuAHyUJ0dTPqkdjnfVbjiNCetMuc6HFR0qif35OnHTJ25nx+qd54u3M5/uXLfw2nud7xUZ0Ww5OqDscD82rUa3Dz5YnS4yO8T9XXeeJ3N5/uSeeJ3N5/uXHO0YP6lQdsfZV36POyse9uHiHLUV8NPf+2Ko42O35h3HnkdzOe9HnmdzPj9V5++wVf6jPF/8Aqm+Q1dtVn+f+q3/r+6HLfxvtl6D55ncz4/VMPTR25ngf9lwJsh21j3MB+bgjycbX1P8AEfVZmvho7/23FPHT2/MO6d02fuZ7rv8AZRnpzU9lnuu/2XDGi3fUP9zR/wAEoa0erP5nOPyhZnW4eP5ajR42e9vq7Y9PKvs0/dd/smnp9V9mn4O/2XGGqdgaP7G/qEeUv9qOwAfJc54jS7UO0cNxHfUdk3p7WJhtNhPBrj8nId04tP8ASpjtBHzeuHq13nAucRuJJCqP38VmeIp7UQ6Rw2p31Jd67p/aBmLOO0k/Bryfgonf/JNUerTd2Mc0e858/wCK4Qjn7Jplc6taZ6REO1Gjt61TP1dTpTp3aqzXMljGuBBDRjHa7nFc6bY/f8Bj8FCecUc/Jeeqimqb1Rd2tCx5Y/ePAfRJ5a/f8GqABLHas4dP2x9ktCbyx59buw+iPKn+0e6AoYlL488/BMWn7Y+y2hJ5Q72neJQmgneha2U+IHagnd8TPglBG9EonYstlnn6puMft90s7AgZfSEConnBNOHelHOXjggUHakEzsj4oDUsIG3ezwSzP7EIkbEsT+/0QNEZ71QtdGrrA+mXEAAFt4gHrtnqEhs3L/7wtAc/sqFtsL3PDg4XbsXDIBl9N0EiRBDCCY27VYFYNtkDFkwScG4ODHQBwL7sncpaLbQagL4uguEC7EF1OCBPWF0OxMEYp9jstVhZeqzESJ9IAOB2ZyWHuO9QNsldrWjWtAEDMn2RMlu3EXeOcwiNRwULiqdWzV5wqCIyJxOJmSG45jHZd4qCjYqodfc+ThMEmerTDsC3D0XH+5FXH88/dROUzlDU4oInKFxUrionFBE5NTiE1xhWEJKjcnk8/eE0qojlQvUplRVFREUkoPOfO5EIhUD5IlHP2+SA8OxKDzz3Jo8fH6J4Y7cfA70UwlOaeHMbE9tmf7Dz2Nd27lLTsFY5UqnuO+iCuQd6FdGiq/8ASqe45CDrvLH5B7MfwU0028zGspzhhcZOJIGzeCFns0PTG1xxvSSJxc12YG9g+KZ/BKcAS/D8uMBzcerBwcR38FhWu20vOIcw/wDbYf0TRa35Xm/+Nn0UNCiGANGQ5x4qWEupzrW8CbrH8CwCRwuwrVkqUKwyuHdMhU+BVGu0sdeGR+BSJHQVdEkYgyFUfZXDYn6N0oRtW1SrsfmraJHOGmRsKbK6SpYwclTq2Dgm0ZCoWvR7nuLhULZAERIwIOMnLAiBvK3Kli7VTqlo9b9fkp0GT/CHzOtPDAyM8Qb2cEY/hGaWnotwImqXQ5rsQfVcxwjrZm7iYxnILTG+D4IDkuWRlQv7lO5QvUELlDUCmfzyVC7eghKiKleFG9UROTSrDLM92Qw3nAKdminHMx2AlIRmymlbdLRdPJz3fIfZadn0NTzDQeJx+atyzjyCcgTwCkZoys7KmeEwP/Zd9Q0eBkIV2lYQrzLQ4Cz9FqzjiWt8StWydCgfSe49kAfGV17ixnFZlv0oYgYBBRdoSx0BLm3iNhJd88Asa39IBTN2jRpNH5Z58FFpbSBg49i50knEmT+31QbR6T19lwdjG/RMd0ltPtx2NAWPHPO1Kql2oekFp/qu7kx2mrQc6z/ErOS8/BC67/E639V/ifqhVQ3iPihLDtRhyN6VLKFzaNBE/dOCCUkn7oAJHMkQcinApIQZrSWOjwO8LVslrVe1UL44jJUrPVhWJHW2a28VcqWxjWlzzAGZ52rmbPXVTSmkR1nOxp0o6ux9Q5A8MD3Ard0T6Y0yIvPkNOLKTYvvHtOOTW8fAHNcraNPWpxIpRRbj6AAO/Gq/EnsI7FFbNISL7zee4nbnkAPjAA3di57SOla7JAe9rXYENwJG6ZGGOW+dkLVNKTLRdpa0TPllaf+s/6wum6K6UtDrQKNqdrGODgC8AuDmi9hUbjkHYErzJtMwHNktJz4mZByIO3PZtXR6L0laQ5rjUcbhF0klxHAEzhsA38AVvl3R6bbbO0OLWOkgFxYfSDRgXD2mgkYjKRKz37vgsXSOmXV2U67OpVoOBvtIggksOH5oBGIx7lt07Q2rTbWaAA7BzRk17YvNHDEOHAhca6bdGonygO3JQ1MlM5QvWVQuV+y2FoGsqmGjhOPstHrO+A2pujqF50kwBJJ3ACSe4Kva7driCBDB1Wt9jbDvxbTv7FqijckzYaT029o/kNDI9YgPee9whvcO9URpiuSSa1X0SfTcPgCr1DR5fhvSWDRV6WlpvAlnol2e+Bhkuuxi6vT03XBALi9sYioA8bMJdiO4rW0ZpQOP8vqP/pkyx/BhOIPA9xWfatFOYTI/YfeVnVaZWZpIl6XYNIsqNkCHDBzTm0pLTbFx1h0gSNb67IbU/Gw4Bx4jI9y1q1pnEbVluElqtaxLZasySpLTWXP6StMy0bM+1Z6qhtNa+Se4KGOYSJeC0yVIefmkP1/ZOhEA5+CUDZ+nf4Jv7pQPh9EDpHP7ISXRzKEHcjtSHn7IhC5tgHn7JbyQDGeec0oQBKEkJN6B0qhb6WN8d/1V/nNNDp47N+xBn0q0Cd2KwdPVTq6Td4dUPEuddHwZ/kti2UrkjYQY8MljaZp3mU3RgaYHeHPW6eqS5rTFWnTqtbUNSboaA1rSOsBMy4YEncclXtFvLbpDDdEtv8AtgEmXA4CRhh4rp7XoqzWio81WVDUaGuZdMS1zGOBjbiVxLW1HOeyQ0SWbi6JwwzEb16tLr/LlXHLn0SNrS5zyfWBicCJIj5eCu2PSTg0uLZYZkwBtx9HZB3bNsrIpUpY4RjIGeEycBzsKsubUvBpeHNDC2TJIAui60k4CIIicoVjnTN+hPWLOl6P6Rp1Kjmay+0gsMAtAa8QDiBEGTH4QtjoTbi4VqRIPVbUHAscGmO1tT4Bczo2wUrOalx7nC4XuvAYNYyodg7PFafQQRVeYOFB/Zi6m35kLhMRZ07uweoXFSuyUTlxaTVagZZ3TgHlrJxgDF5kgGBLW+KzrPZ3SHNh0gRiMRGR2H5haRBdREOukVB3y3D/ANSqdGzODvSA2yBEz8D916NOPS51dW1ZLYaLAX04kQHSIkYfMKjXFS+XmpGsEm6JE5RiR1sst5VttnvMAYKhLSZMgCAdk4TABUllszcDMwZiJju2Htw/TrKH6Dddq06VcX6dSWsdJEYls75kEEHJU+kmidVUc0GQDgfiOeC1rNT19ek1uTHmo92Ybg0RIzMMBPEntUHSu0B9VxBzPwAjeszCuW0a6KobsqSw/wBwj5we5XbNXOrE7JHgqVjb/Np/naT4gpKdeGE7JJXCvq1SNIWmBAzOSxz4p9WpeJJ/ZN4c96zEEyQt5570oHP6/NAPP6JAefoqhePP7ZoA2oEoJ5/UoAcPslA557vBCUc8EC4bvgEIA5hCDuYSBIUELm2AEADntUVqtLKYvPMDATBzOQwUjXgiZGIB3Z9qBwCE2+N4w4qNtqYYAcOtJHEAgEjvIQS5xz8UQJ5+Sa94AJJECcczhmiQBs44gCeP2QMr0g4XSeztxWDUaTSfQI6zHhwwxumRhtiSD3ro2ztVDSdlcSKtMfzGbMw4bWnx+KsTYcvUsAiKzKjq9EgBnqVqb3Xg01GOkkdYgt9oDZjyOlqRDqnVcwCS0DHAFwIkDGCHCeC7fSFHWUzVp1Aw02wb+Gqa0CLxGJAIz3RkuatGn3SadSjTtJaYq1QwF7sIGIAMwIBwnCZK66VVU3mXTXoopttm91SzvL67aJphtEkDWwcGmP5l/bnOfxW7S0aGVC24BfIaC2Sy6260kB7nEXsOqSeu8DItXMUasvADKwbfEDVCQJwnr/GF1lnttZ1WrSY1tK7JbaSCXBreq917EtkAi9EwMCISq+63ZKaaZov1m/4Rafm5Ua260VLnVDLphhl4z6suDXZn0CtXolZLlC9trER/02Tj3un3E9nRylRdUZVc+pRLabqTg8XqpcA8BxxJHWExEnHPBbNCkcyADAAaMA1ogBoGwAALnFU2tLevFEVRs8R9w+dyhIjep3Dn7qFyjidQF4OpTF8CD+JpkZb8R3qJthjNzjwkx3hMf8efBXaNoFXA4P2j2uLeO8Lrp1dpZqhcsFtuYZDcrxqUX4vaJWC7OAmueYXdh0FXSrabblMBoO7PvXNW20lxPFLVM5qIMgEuIAGbvpvPBZmRGHXGufti638zhGHYJKzqrsA3YPmpq9fWERIY30R2+seJVd5XCZvN20JTSrlfR9VoY9zDdfF2IM3heGAylskTnCqmdx5/TiiADn5pvPPO1SPaRMgiM5GXA7ipKNne5wa1jiSWiI2ugNHCTETwQQXecUqlNB4AddMXrsxtADss5uwUlOk4kAAycRkJzxBOzBBEU4c/RBaRszxxH12Z/JK089yBQRuCE0uPP7oQd0EJBzCVc21e2UQ9t0mBLTMx6Lg/afwrNq6DYZl5MggYM6odrIPdrXY8Fct2jWVXNc/1YjAH12P277kdhKpU+jzQQdYeq1rBLQQbuqi8Mnf/AFDdmeEVDDoikXSHHBwa4DDrS50uiOt18zuVuroprrgvehIGDTINRjyR7JmmBIykqKroGmfWIMEEgNGYpjYB/TwH4ipKOhGNqCoCcDIbkB6XogQB6RmQZS4o1LBZm3mOq43KjMgIF0Mc7KC5oGLt5xUNtsFB4Ip1mBzw8G9AyFR73XbplwFoB2GLuIlav8JBBaXZi0NEbq7rxmRmFXd0cYSCXuzJwgDEUw4DDJzad0/nKXGrZ7S2oLzHBwwxHEBwPeHA96lJ5zVPRtg1IImR1ADwYxjMeMg/BXYUVQtmjA832ksf7Q2/mG1YdfQjh/8AkMz16NwHHPqPaQJzMNC6oJVYqmBxbtDNJBu2i8Mzq6WOcYXLo2YxOHctSw2B7GlrKQYHGXF10Xjvcym1rXf3NK6BAKszdbyo0rGG9Ykud7R2dg2J7lO9QPWUQvHMqNxUr1C9BA4TmoarfhtGxTuPYonFUK23PHpAP4nB3e7b3yippFpEFlQdkH6KJxTCFqKpZmE1TSRPo0u9x/QQqdUueZqOmMgPRHYBgpU0q3uInFQvU7lC4INenpa0FofcJpMYKRANzFtMMkPHWvwc8Yvbipj0otF2dWz03PDrpOIeKpBEzduuu/lcc81S0Xpt9ANaGhwa8vgkxJNE5f8AaHvFWKPSmo0NlodDS0kuMukUQb0g/wBFu444EHFauiLTGlazi1jmXdW/WXYz6tNovgABwAp7vWKv2bpFWBD20C7WOJbLnvvFpD3ReOQvA9WMDtzUI6V1ceoMZAxkibogXger1chnOYVep0iealKpcxpFzovOxvta1wb7DergBlKXE9DpTUBEUxgIxJc6Ja4dZ04ywY7jGGBVWrpyo40nGmJpNI24gtDNmwBuHhMQBPR6SvYG3WAEFhJvO61zUDuBFnaCPxOTqXSuo0EXW5QJMwLtNoiQQG/ypI23jiEuKOnLfUquDarbrm3jEnDWXXRmYEQR2rOB555wU9utGtqF7hEhogZdVrWf8R4qELIUE8/uhEnZCEHbl0eKUoQubZAgmEIQJgQljCPohCAnnnsQUiEDgEhQhAAIPDnxQhAJCY2IQgY4889qiehCCF3OSichCIgeVC4zj4IQgjcmpULUCMuTShCqI3ujNROSoVEDkQkQiHBJOSRCBxwSIQgXYgH5lCEDweCEIQf/2Q==

## Slide 10: Example of an immersed tunnel being lowered into position
Notes: data:image/jpeg;base64,/9j/4AAQSkZJRgABAQAAAQABAAD/2wCEAAkGBxAQEA8PDw8QDRAPDxAQDw8NDxAQDw8OFRUWFhYVFhUYHSggGRolGxUVITEhJSkrLi4uGB8zODMtNyktLisBCgoKDg0OGhAQGislHSAvLS0tLSstLSstLS0tKystLS0tLS0tLy0tKy0rKystLS0tLS0tLS0tLS0tLS0tLS0tLf/AABEIALUBFwMBEQACEQEDEQH/xAAbAAEBAAMBAQEAAAAAAAAAAAAAAQMEBQIGB//EAEsQAAECBAMBCQ0FBQYHAAAAAAEAAgMREhMEITEFBhQiMkFRYZHRFSNSU2JjcXOBkqGy0jNCk7HBdIKis8IWVHKEo8MHJENkg+Hw/8QAGgEBAQADAQEAAAAAAAAAAAAAAAECAwQFBv/EADwRAAEDAQMGDAYCAQUBAAAAAAABAhEDBCExEhVBUaHhBRMiMlJhcYGxwdHwFBZTYpGSM3KyBiNCgsLx/9oADAMBAAIRAxEAPwDctr3z5cW1QLagFtCC2hRbQC2gFtALaAW0AtoQW0AoSQKFZBaEkpKEkChJIKEkChSQKEkChJAoSQKEkChJAtoUW0AtoBbQC2gFtALaAW0AtqgW1ALaA2raxkotpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIgW0kQS2kgttJAtpIFCSBQkiBbSQLaSIFtJEChJEC2kiBbSRAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpIFtJAtpINq2sJMoFtJEC2kiBbSRAtpIgW0kQLaSIFtJEC2kiBbSRAtpIgttJEEtpIgCGrIgW0kgtpJYKYaEg821JLBbasiBbSRAtpIgW1JEFtqyIFtJEEtqSIFtJEC2kiBbSRAtpIgW0kQLaSIFtJEC2kiBbSRAtpIg2zDWEmcEtpIgttJEC2kiBbSRAtqyIFtSRAtqyIFtSRAtpIgUJIgUKyIFtSRBr42AXQ3NaA4mQkTKYnnn6JqOVVS4ypwjkVTRh7Lcb8QYcEQYIiPFyHMNFw5ZZngnqC5XvyFvbt3HdTpcY252HVvMOCwpqYGwpGG+bnF7JU1PYZADyXdQ51sbM4bdxpfkwvKW/q3nbtrok5YFCkiCiGrIgW1JEC2kiCW0kQW2rIgUJIgghqSILbSRAtpIgW0kQLaSIFtJEC2kiBbSRBLaSILbSRAtpIg2yxYSZwS2rIgtCSIJbUksFtpJIFCSIFCSIFCSIIGJIgttWRBLaSIPLpAgEgF05DnlmVMqCo1VvPVtJJBLasgrGyZj+CT/yRzEpDgx9c559AOnIuS0c5D0LJzF7Tm7Ohd9jmlzdc3Om09/j6CZl1Bb24r70qcj+anvQh0XNAzOmXxyWcmtGltqyIFtSSQAxWSwW2pIgGGkkgltWRB5hycA5pBB0IzBUR0lVqosKehDSSQKEkQKEkQKEkQLaSIFtJLAoSSQLasiC20kQS2pIgUJJYNq2sJM4I5gHtyHpSRBbasiBbUkQLasiAYaSIFtSSwLaSIFtWSQLaSXJFtJJkmviWAOhE5Cp8ydOI7VRVvQya25fek4m0NpYoRIogCCYbQ2kxA6sEw6s5H259GS8m28Kts9TIXVO2PQ9OycHJWp5S6zu4N4iMa7U0tqlzkTy1yXqo6TzFZCwIgAZjgagTgTKQdLi4jWQlzSmtFbnIddmTkr2mjsmGLkcTiOkM7jXAfbYjQkAH2Lc1bzmelye9CGbbTQIQLi9rRGgVmG5zXBhiNDpSz0msKz0axXKtyEZDVl2BxsZi8IWR7WJxhiUmyDGjyqpGvt51yfFU1uRy7TalWldhf1bj6e3LLPLLnXoSaIIYfQkkgtCSIObtvFPhtaIFBiGIxsog4MjPLXUgHTmXNa7UlnpLUXBDpslm46ojdZg2Hjo0Rz24gQ2nvdFrThBxkZmecsvaOha7FbUtLVcmhYNltsfEKiJpSTo7PZOFCMtWNXY1bjkqJylNgw1lJjAtqSIIIaSIFtJLBbaskgltJLAtqSILbSRAtpJIBhpIgW0kQbRYBrl0lYybMk5O3YkMb3rxDsNDOIlEiQi0uAtRHDItd95rOTlWLspbm3qbaSNReXgedg4hj7hbin4loEHhRaAWvLJvAk1vKUTLbz0gtVGKvIwOyGDUEEdGYWUmrJFtJJAoSRAtpIgW1JLBzsTtnCwnFkSPDY4AEtJnKfoWKvRNJklJy4Icrb26bDtgl0CJCjvrZ3twcQWzzyCwqVYbLb1LxT0SYPnTuyfMHe+GEjPKG/PLlzXP8TU6BMmp0V/Jr4rdY95aaMNDLZkSYdTLORd0LU61uXRCmLaqtWFacrfkObZQcJIEEzhAz405mrlq/hbzLji56X8rrvS6Ll0a+06s4PlvIw23zfd3dh0Nnbo7FQZCwpaSSGlgk0mU5SOmWnSV0UKzqTUbjGvH2vu40VrStR2Vkx2f/D6jc7te/htpvNphZhHgMhgBrwGR3TMyTlV1LobVWokqhvs7lVq3e7j5XA7rXh0WQwsQOYGiTRweHFM5h2vC/JYraXJ/xOZ73IiclfcdRsY/dW6MwsMLDMmWmpjTPIg+F0LXVtC1GKyMTU5yqkQvvuOQMY0FxAgzdrMTHKchVzkrlRFlMbjGVuxu96juP3ZuOkHCDMHJp5CD4S7vjHdE2cYupffcU7s3mXecIJGfFOeREjwun4KfGO6I4xdXv8D+2j5g2cLkCJSMs5eV0fFPjHdEZa6l99xzMZtgRnmJEhYVxkWtBhghgJLss88yuWu5azkVZSFRYTBepdaLpOmlbHU2qiMxSN+GgxYXaAhlrmwsMHtBFYhgEgtDSDn0dbjoqx2RUV6aYu0XTo65vDra5zMlWa+3w0HUwm6t0NjWCDhnymAXNcScyfC/+kuptrdgjTTluetzV/O49ndfEplvfDzDZB1D6py111WfxNSOYX/cnmr77j7OFugwZaCcTCBIBIq0PKuvLTWXiXajewOMgxpmDEZFpMjQZyOv6hVHIuBirFTFDZMNWTGBbVkQLSSWBbSSQLaSINHbRLIERwiGDTSbjQ0loqbMycCNJ8ixWdBmxEyr8DnbKjNdiGth4+JjG28S57XNgSbRFYyGZtY05tcTqo1KiLy0VO1DbVSnHIj8nftrOTng+K3Y7tt7xYcJmGbHhlrItUZ5hze15mymkzAk0z8pc1eo6mqIqHqWGyNtLVc12F2G9D5DbO7HfMK1vOFB78YtbIkzmHCniDwvgtbLZkrzdu47HcEKuD1/G88bH3X72huh70hxqorIlT4kiKXAylQcjL4o+2ZUcnDr79QbwQqYvX8bz6jczu9dFjPh7xkx5MUjDxGucyTGMya4NBzaOUarKjVWo6EQ5bbYW2emj3P6r07etT7B26LDDJxiQz5cJ4APNVKR9hXVkuTQeYjmLgplG2oHnPw3K5D9RjxlPWO7MDzn4TuxOLfqHGU9ZW7ZgeX+E/sTIfqHGU9Z+UYqZiOIJAqdUJa8L0elca4npJgeSB5XW5AY4k8pVAcuRzGXR6VAfc7htoQ4cCKHh4JxDiJQ3OyohjkHOCuik1ypKIcloe1HIiqdfH7Xgl+GIrk2MSZwomlqIObnIWTmOlLjBlRkOv0eaG53agec/Cidiz4t+ow4xnSML8YIgxjmB5a7Bhn2T5l4Ec+wCoci0VWqjoU6qD2qxVRTT2btNgixXPJpc1oZTBiT+1xDs9eR45BqtqU3zgc7qtOEv93HS7tQPOfhROxZZD9RhxrOkBtqB5z8GJ2Jxb9Q4xnSHdrD+c/BidiZD9Q4xmsd2oHnPwYnYmQ/UONZrHdqB5z8GJ2JkP1DjGdI8RtswKXZxOKf+lE5vQorH6ipUZPONfY21oAw2GDq5tw8IEWohzDBPkUax2SlxnUqMR636VPkN2uKZExQcyqVhgzhubnU/nC01UVFvOmg5HMuU4NQ5j7h7FrNp5e6YMpg8hpPYgQ7m4jENh4oOiVZQogJEN5z4PMFnSaquuNVdyI28/QO7OH53/gRvpXTkP1HFxlPWhhZugwpMg95I1FmNMfwrGHKZKrUSVUyd28MBMucANSYMUS/hVyH6iZbF0mI7o8NIll6NLkhwImfoc4Bp60RrlwQquYmKofn+1v+IIdEjsfs5hNL4DbsUFzJF4qlbMjmMgeTVcT7RCqioe1R4NymNej8YXA0tobu4cVsZo2bBhGLDYwObEBLC1znVDvQzNUuTRRlqyXI7JwM3cEqrVTL2L6mhsXdUMPEc92EZiQYbmBsR8gCS01ZsPgy9q31+EeNROTh17jVS4FVk8vYvqfo+4/dYzE4eqLCdAMNwhNDbkYRA1jeFMMEsycuhZ0FdUbKIcFtpMs9TIV3XqNPH7Ngx6b0JsWmdNXJPXT0BdtSkypzkk8uhaatCeLcqTian9msF/dofW7tWv4Sj0TozrbPqKX+zWC/u0P+LtT4Sj0RnS2fUXYbOB2XAgFxgwmwy6VRbOZA5M1sp0WU+akGiva61eEqOVYNtbDmMRwrNQKDrNhLJnplr7VMlDPKUlt40eHdERon1tlLqKl6CWroAiuHGhkc5Ya2j8nfBXKXSghNC+R8ZEiNL3SP3iZaHXm1Xkrip7zcEChQhT6Tc19k71p+Vq9CyczvPJt38idnmpuYzjwPWn+W9bH85vb5KaaXNf2f+kNkLYaTq7K+wxmU+9HMnTgRJLitH8ie9J6Vj/id70HDww4TsgOCMxy8J+uS624nA/BE94IZ1lJgVAJIAgCoPMQZH0FRcCtxMOA+yheqZ8oWFLmN7E8DZX/lf2r4nA3SDvw9W383LjtXP7j0bD/F3+hzJLmOsiFOhufjNEbn727JgLjqOQZrfZl5fccltT/b7z6QRXniw5dMRwHtk2fxkvQldCHkwmlfwQYc5kvlPW20Nq9JMz1SUyS5XtT03DMBnKpw0c8l7h7TMqo1CK9xlVMTl4vc7hIr3RIkEF7pFxDntmdJyBlNaH2Wk92UqXnfR4StVJiMY+ETDD0MR3K4LxH+pF+pY/B0ej4mzO9s+psT0B3KYLxH+pF+pPg6PR8SZ3tnT2J6HTweFhwWNhwm22NnICfKZnXpW9jGsbktS44a1apWer3rKqZisjAAICoAqQKAIUIAEIfLxdhxiTNrCJk5uBXnrZnyeu22UkRMTx3Aj8lI9D5jqOinw1QvxtL2gGw8SOSG79+ntT4aoPjaPX+DrbHYYLHNitcwl5IMqmyk0TqbMDTlkuqg1WNhxxWl6VHZTdRkxeMhl8CmJDcLpmREb4Dh7dZ+xV7kymxr8lMaTHZL5TR5objY7CQA9pJIAAe2ZJ0Gq2K9qJKqam03OXJRMTr7OjwRCxUnQ3SgkVOe0iI6l85Zzp5BLUCfKvOqqrnIq6dh69HJaxUbo2nJLoQ4THtofMtm8Fwkc2O6QT7QQeVdtJ6XouKHnV6aoqObzV2dRN8M8NnvBbZTWc8LqG+Ifhs94JKaxkrqLvhnhs94JKaxkrqJeZ4bPeCSghdRbrfDb7wSUGSp4jR2hrjU3JriBUM8lHKkKVrVykMOBxcMQoIc9gNpkgHtJPB5Of2LCm5MhvYhsrtdxr4TSvicza2DixoodDYS2gCb+9iczyOkeXmWitSc98tQ6rNWZSZDlvntNPuHiTyMHQ17Ses9i1fDVDo+No69gO5+NytDvS9pHVonw1QfG0tew6GxdmxYUSpzQG0EZOBzJHIFuoUXsdKnNarTTqMyWrpO4uw88KFIgCAIAhCoCFAEAQFQoQgQoQBUgQEUKJoBNAegUIcB2JawQ2mZc8SaANZCZz0GQOq8OvWZSlzvd+8+jo03PREaYTtHyPv2+MONOXNouTOFKcFwnRqnWdHwj9aA7R45tzoIaeFqSGnLLygmcKcoiIt/Z19fUX4V996XEftAgxBbHAY154ZkQatOD5J61inCNNURclb1jR1dfWVbI6+/AyQ8cJhrmlpcKgQQ4ATAz0OpHIt1G2U6qxELMefka6lnexJDNoQzlJwyccxyNBJ+UrY20UnLCLsUwWjURJVDwdpaFsPIxDD4bqSHAuB0B8Erndb6aKqIirdPh6m5LK+Jkh2keEbY4ERsMyfq51InxdOGOoqJwhTuSFvSdGievqC2V+tCxdoUiITDnbbUZO1Ep5ZKt4QpuVqQvK7PULZXpN6XHrfwqLTDMw0OMi05EkdHMjeEKKoi33rAWyVE1G1gorXugvZmHOcQZEEi2/kOa9Wyqi1EVOs8y2oqUlnq8TsL0zxiTUKVCQRAVAEKEBFSFUKAqQIAoUhwx8a7qh/SvEzhW6j6BeDKHX+dw3q7xr+qH9KucavUTNlHr/O4hgPGj6jzPAAPtaMvisqfCL55SJBjU4Lp5PIVUXrvPLIgJkZtdytdrLn6R0jJenSrMqpLVPIrUH0XQ9PQyLaaSICoRQUKhAoUFCFCoKgPk8X9phf3v5b18twpzV7/APJp9XYfTwUwu4v+a/3F5SY/9PI79Hf5kfpiPWw/khI3Gn2L4uC4O7fJD1H42J9Qz/dWLObT/sv/AJK7F3Z6nuXfIY83/XDXVYv5E/sv+LjTaeYvZ5oa2HOf/jjH2SiD9QttmYqVFnQl/wCDCq5MhOtU8TIzRn7VF+eKuJcV/qng06EwTtXxUsQcGL+0QvmhI3nN/qvg4LgvanihMXxMV6v+gpS51Lt8w/B3Z5GSIO+v9QPmetbf407fJDJed3G9sE8DC+35Ii+rsGKd/mfPcI8x3d5HfXrniBAVCEQoQFQBAQqkPAeXZMFRnImcmNPMTz9A+Gq5a9rZSuxXUdtnsVStfgmtfLWZW4d3K/0yYAPzXn5xq6kPSzXR1rs9AcO7w/4QmcaupPfeXNdHWv53De7vD/gCmcaupBmqjrX8p6HupcB6IqUKKlSHiK0OEnCfNyEHnBGiya5zVykW8j2NemS5JQwmpus4g5wOGPSBr7OperQ4QRbqn5PGtHBipfS/Hoe2uBAIIIOhC9JFRUlDyVRWrC4lSAEBZIAgCECok+UxfHwvoP8ALcvleFOb+f8AJp9ZYfTwUw/d/wA0f5q8rT/08jv0d/mSIMsR61nyQkbjT7F8XBcHdvkh7xAzxPqG/lFWLMKf9l/8lXF3Z6mRv20L1Y+di6rF/In9l/xU02nmL2eaGrgzxz/28f5nLro/y1e80VOYzuMkPis/aov8yKvLXFf6p4NOxME7V8VEU8F/7RB+eEq3nN/qvg4LgvankTGcTFer/oSnzqfb5h2DuzyM0Qd8f6ofM5YJ/Gn9vJDJecvZ6m5sPiYb0u+SIvqrBi3v8z57hHmO7vI+gXrniBARCBChAFSHiJFDZTzJ0aM3H0D9VrqVGsTKctxspUn1XZLElSCGXcfgjwGnUeUf0HWV5Fe3udcy5Nu49yzcGsZyql67N5sNIGQEgNAMgPYvPPRLUqUVoCVIQw1KAtSFFSAVKyAXoDE9mc2mh3OMwf8AE3l/PpW+haH0luW7Uc1ezU6ycpL9ekMjyMniknIH7rj0Hn6D8V7NC1sq3YLqPCtFhqUb8U1p5mYLpOQqAiAqENbHB5aKKp1CdBANMjznnktVXKyeTib6GRl/7mBzYmBqoJgxJsnTJwEspeFnkV51SxrUue2T1WW2mzmujuX0PI2YJStRONXx/vTnPjc61Ztb0NEd35M85J09m4HZg4XeonCILuHqQAPC8kdSJwa27kYde/rGck6ezcU7NBqnCicJoa7h6tE/K6T1onBrUjkYX47+oZyTp7NxW7Pk4OtRJgSBLp5TnpV0BZM4PyFlrPf5I7hBrkhX7Nx4h7LDZygxM2uaQXzFLjM6u6VkliVFVUbiRbcxURFdh2+g7ljIWouTi8cP7xJJPG53HrWvNjeh1e7+ozzknT2bh3LGYtRM3Bx4f3gQQeN5I6kza3odXu/rGck6ezcV2ywagYcQ1iTuHqJS8LmRODWpEMw695M5J09m4p2dmTbiTIkeHyZ+V0lTNjYjI27zLOSY5ezcem4Z7GBsOHEaWA2yCJgyI1J6TquplCqzmpBzvtFGpc9Z/J2l6Z44UAVIJKKUjnAAkmQGZJyAHSmAxwNcxXO4vBHhuGf7rf1PUV59fhBreSy9dh6dm4Nc/lVLk1adxkhMDdNTq45ud6T+i8l9Rz1lyntU6bKbclqQhkqWs2HmpUha0KK0IKlAYakAqQCpCipCEqQCpUBxBEjmDkQdCEB4a4t4vCb4JOYHkn9D8F30Le9lz702nm2jg5lS+ncuzcbEKM12hzGoOTh6QvXp1W1ElqyeJVovpOyXpB7Ww1hQEQp6QBARAJoAgLJARAEIUICFAJqlE1AEBUBgiYgAybwnDUA5D/EeT0a9C561qZSxvXUdVnsdStelyazERMgvNZBmORrT0D9SvGr2qpVxuTUe7Z7JTo4Xrr94GSpcx1AuQCpUhKlAKkAqQCpAYakKKkAqQgqQoqQCtCCpCipCEdIy1BGhBkR6Cs2VHMXKasKYvptqJkuSUPTMU8GTqSPDz+IH5j4LtfwrUYyUp5S9Sx5KeW/glqu5LoTsk3RBeQCDDIImCCSCF5y/6oaly0l/bcMz/fs3lsRPI63difNLfpL+24Zn+/ZvLYieR1u7E+aW/SX9twzP9+zeLETyOt3YnzS36S/tuGZ/v2bxYieR1u7E+aW/SX9twzP9+zeLMTyOt3YnzS36S/tuGZ/v2bxZieR1nsT5pb9Jf23DM69PZvJZieR1u7E+aW/SX9twzP8Afs3izE831u7E+aW/SX9twzP9+zeLETzfW7sT5pb9Jf23EzP9+zeDBieb63difNLfpL+24Zn+/ZvJZieb953YnzS36S/tuLmf79m8WIvm/ed2J80s+kv7bhmf79m8tiL5v3ndivzQz6S/lPQZo+/ZvMcZzmCbzDA5OE4knmApmVspf6k412Syiqr2p6EXghU/57N5qOjPfr3seC103EdLuT0DrXZV4Re5IakbTbR4MpsWXrPgGkDIZAaAaBefpPTgVIC1oBWgJUgFSAVIC1IBUgMFSoFSAVIBUgFSAVKAVoBWhBUhRWqBCiubxHFk+QSInzyOU+lc9azUqt72yv48AZN+RfGu92F9K05vs/R2r6llRvuL453uwvpVzfZ+jtX1JKjfcXxzvdhfSmb7P0dq+olRvuL453uwvpTN9n6O1fUSo35F8a73YX0pm+z9HavqJUb7i+Nd7sL6UzfZ+jtX1EqN9xfHO92F9KZvs/R2r6iVG+4vjne7C+lM32fo7V9RKjfkXxrvdhfSmb7P0dq+olRvyL40+7C+lM32fo7V9RKl35F8afdh/Smb7P0dq+pZUb8i+Nd7sL6VM32bo7V9RKk35F8a73YX0K5vs/R2r6iVMRfnMkucdXOzP/odAyXTTptptyWJCELWswSpUFrQCtQCpUCpQCpUCpAKkAqQGvWoQVoBWhRWhC1oBWgJWhS1oBWhBUhRUgFSAlaELWgFaAVoBWgFaAlSAVIBUgLWgFaFFSAVIBWgFaEJWgLWhRWhCVoBWgFaAVoBWgMNSFFSAVIBUgFSAVIBUgFSoFSgFaAVoC1oCVoBUgFSAVIBUgFaAVoBWgFSAVIBUgFSAVoBUgFSAVIBUgFSAVIBUgFSoFSAVIDBWoBWgFaAVoBWgFaAVoBWgFaAVoBWqBWgFSgFSAVIBWgFSAVIBUgFSAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAwVKgVIBUgFSAVIBUgFSAVIBUgLUgFSAVIBUoBUgFSoJUgLUgFSgFSAVKglSAVKAVIC1IBUqCVIC1KAVICVKgVIBUgFSAtSgFSAVIDBWqBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAVqAVoBWqBWgFaAVoBWgFaAVoBWgFaAVoBWgFaAwzQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQCaATQH/2Q==

## Slide 11: Service distribution
Services are transported across the country via a network of underground or overground pipes and cables that carry gas, electricity, water and telecommunications to both homes and businesses.
Pylons carry high voltage electricity (often exceeding 765,000 volts) from power stations to local substations before been stepped down to 240 volts for use in domestic properties.
Electricity and phone cables usually cross the country on overground poles, while water and gas are usually piped underground.
Notes: https://upload.wikimedia.org/wikipedia/commons/b/bf/Overhead_power_lines_in_Dnipro%2C_Ukraine.jpg

## Slide 12: Towers
Mobile phone towers: These act as though they are large antennae, transmitting and receiving radio waves to a radio base station. From here, the call is either sent via a fibre optic cable or forwarded to another base station via a satellite link.
Notes: https://mattata30.files.wordpress.com/2012/12/gsm.png
https://image.slidesharecdn.com/cdocumentsandsettingss05299219desktop2mobilephonesstrengthweaknesses-100220003926-phpapp02/95/test-3-728.jpg?cb=1266626404

## Slide 13: Flood management and coastal defences
Flood management and protection of Wales’s coasts is increasingly important with the pressures of climate change and weather unpredictability.
Dams: Designed to regulate the flow of water and to form reservoirs for domestic and commercial use, as well as to generate hydroelectricity.
Temporary catchment area: To prevent flooding caused by run-off, all new developments must have included in their planning catchment areas that hold back water to allow a slower release into main water courses.
The Craig Goch Dam, Elan Valley Reservoirs in Mid-Wales
Notes: https://www.elanvalley.org.uk/sites/default/files/fileman/claerwen.png

## Slide 14: Flood management
River defences: Rivers are regularly dredged to maintain flow. Levees, bunds and weirs assist in regulating water flow and reducing the risk of erosion and flooding.
Flood plains: These are natural low-lying areas that naturally flood when rivers burst their banks after heavy rainfall. When houses are built on flood plains, they are at an increased risk of flooding should the levees break.
Notes: https://i.pinimg.com/564x/2e/47/15/2e47159ab31d89dd3859ef7443ee99e1.jpg

## Slide 15: Weirs, bunds, levees, floodgates and barriers
A weir is a small dam designed to regulate the flow of water to help prevent erosion.
A bund is a wall built of stone or soil formed into an embankment that holds back water.
A levee is like a bund but is normally formed naturally by the river.
Floodgates are designed to control water levels in flood barriers, reservoirs, rivers and levee systems.
A temporary flood barrier in Ironbridge
The weir on the Afon Twrch
Notes: https://i.pinimg.com/originals/bb/81/99/bb8199587af52ada4f5b6adcdbc06361.jpg
https://www.southwalesargus.co.uk/resources/images/11077271.jpg?display=1&htype=0&type=responsive-gallery

## Slide 16: Coastal defences
To prevent land being eroded by the sea a number of techniques have been adopted dependent on the location.
In seaside towns and areas that are prone to the full force of storm surges, sea walls often form part of the promenade and protect the land from erosion.
Storm Ciara, Porthcawl in South Wales

## Slide 17: Coastal defences
Groynes are low walls or barriers built out into the sea to help stop erosion and prevent beaches from drifting or washing away.
Gabions are a versatile form of erosion protection. They are cages filled with bricks or stones and placed in areas prone to erosion, as the contents allow water to flow through them and so they prevent erosion by decreasing the velocity of the water.
Revetments are sloping structures made from timber, rocks, concrete blocks or paving that are built along shorelines, cliffs and sea walls to absorb the energy from waves, preventing erosion.
Notes: https://lh3.googleusercontent.com/proxy/JtkevScYsHV3yKFFBB1nCCrnhgfZLQA9VbWbanxY9DTovUv5LOUW1g7wBEpnKhQ66ehs9EtEUAss7aTWQfuyHLmccWu52DOX_VtJKmRZ4c1QDmV3PFZsZlDAs4SqVbcVMJntcgCPbvmCdWPNX7yfwP1wNWQ
https://ichef.bbci.co.uk/images/ic/320xn/p033wrp3.jpg

## Slide 18: Canal and waterway structures
With the construction of canals, goods and building materials could be cheaply transported across the border and so coal from South Wales powered the industrial cities of England.
On canals, locks are used to raise and lower boats between stretches of water at different levels, allowing a barge to travel over obstacles.
Notes: https://lh3.googleusercontent.com/proxy/JtkevScYsHV3yKFFBB1nCCrnhgfZLQA9VbWbanxY9DTovUv5LOUW1g7wBEpnKhQ66ehs9EtEUAss7aTWQfuyHLmccWu52DOX_VtJKmRZ4c1QDmV3PFZsZlDAs4SqVbcVMJntcgCPbvmCdWPNX7yfwP1wNWQ
https://i.pinimg.com/originals/c0/7a/40/c07a409ccb70923f126bcfa6ea9e9fc4.jpg

## Slide 19: Quays, docks and piers
Quays are stone or metal platforms that are built alongside or project over the water, allowing ships to dock while loading and unloading cargo.
Docks are man-made, enclosed structures normally surrounded by warehouses where ships dock to load and unload cargo.
Dry docks are man-made structures where a ship sails into a dock that is then drained so that work on the ship can be undertaken. The dock is re-flooded so the ship can sail out again.
Piers are raised structures that usually extend from the shore into the sea. These were traditionally used for boarding boats at sea but most are now used for recreational purposes.
Notes: https://encrypted-tbn0.gstatic.com/images?q=tbn%3AANd9GcSE-5DyddP1rhY5kcXm98UqZv_oZjidCl5THw&usqp=CAU
https://lh3.googleusercontent.com/proxy/D4O7-WMxrWMXVPXRDUTyiVmS7SnoOctKrNy2dbljVZPZUE7TVU5ZnBCOZMB3ItdjkkFfEx1fOYOrb9NR3nlTCIc2v0pfjuEekrKuU9d3rSJL_91kbYqp-8MTAghMAl2eRDgvesT9f86ZU2q2
http://www.simplonpc.co.uk/Piers-Wales/Tenby-01_b.jpg

## Slide 20: Renewable energy
With the rise of global warming and the depletion of fossil fuels, the production of energy from renewable sources is becoming more and more important. The following are the most common ways of producing energy which feeds into the National Grid:
Wind farms produce clean electricity from wind turbines.
Tidal movement is being harvested to produce electricity.
Solar farms produce electricity from sunlight.
Industrial biomass boilers using wood pellets or timber are being used to replace fossil fuels to produce sustainable electricity.

## Slide 21: Renewable energy continued
Renewable energy generation is a major design feature in new buildings. Buildings can be heated and generate electricity from renewable sources. These technologies include:
Solar water heating which directly absorbs the heat of the sun and circulates it through a heat exchanger into the hot water storage tank of the building.
Domestic biomass boilers, fueled with wood pellets or timber that can be used to heat a building and hot water.
Air source heat pumps transfer heat from the air outside a building using a refrigerant system.

## Slide 22: Renewable energy continued
Ground source heat pumps use a ground heat exchange loop placed underground. Water is naturally heated underground and is pumped back to the surface where it is used to run heating systems and produce hot water.
Photovoltaic cells can be positioned on a roof or on the ground and supply electricity to a building. Any excess electricity is then fed into the National Grid.

## Slide 23: Air source heat pump
Notes: https://www.staticwhich.co.uk/media/images/trusted-trader/desktop-main/air-source-heat-pumps-465255.jpg

## Slide 24: Ground source heat pump

## Slide 25
Any questions?