## Slide 1: PowerPoint 4: Traditional building materials
PowerPoint presentation
Unit 102: Introduction to the trades in the construction and built environment sector

## Slide 2: Traditional building materials
Before modern transport infrastructure was in place, most traditional houses were built using locally sourced materials. This resulted in a range of properties across the length and breadth of Wales which were made of local stone, slate, timber or clom (a natural building material made from subsoil, water, straw and sometimes lime). Thatch, slate or stone were used as roofing materials.

## Slide 3: Lime
Traditional built properties used a lime-based mortar to bed the bricks or stone used to construct the external superstructure. External render and internal plaster was also lime-based.
The main benefit of using a lime mortar over gypsum or cement-based mortar is that is breathable. Breathability means that the wall is ‘vapour permeable’ and allows water to enter and exit the wall easily. Water does not get trapped behind a lime mortar, so the walls do not stay damp and cause timbers to rot.
Conservation plastering using lime-based plaster

## Slide 4: Lime (continued)
Notes: https://www.wtbf.co.uk/images/old-building-information/Wall-Diagram.jpg

## Slide 5: Lime (continued)
Traditional buildings are not waterproof. They rely on the thickness of the wall to prevent water reaching the inside. Lime renders and plasters protect the wall structure. Other benefits of using a lime-based mortar over a cement-based mortar are that lime:
attracts water – so it actively draws water out of stone and timbers
is relatively flexible and self-healing, making it less likely to crack
has a lower carbon footprint than cement and is therefore a more environmentally friendly material; it is burnt at a lower temperature and re-absorbs CO2 as it cures.

## Slide 6: Timber
Traditional timber framed houses are most common in the east of Wales. These tend to use oak, which grows well in the area, where the climate is less wet and windy.
Modern construction uses timber framing methods, although the timber is usually faster grown pine and offers less structural strength. More timbers are therefore usually required to provide the overall building strength.

## Slide 7: Timber building components
Non-load bearing partitions were traditionally constructed using locally sourced timber and covered in thin timber laths, with a gap between each to allow lime-based plaster mixed with horsehair to adhere to them.
Modern partitions are constructed using either timber or metal studs covered in plasterboard.
Timber is traditionally used as lintels, floor joists and boards in traditional buildings, and while it is used in modern construction, other materials such as concrete and composite timber boards are also commonly used.
Notes: A section of a lathed wall with plaster removed. Image courtesy of Museum Resources
Rear of a lath wall showing the lime lips adhering the plaster to the laths. Tywi Centre photo.

## Slide 8: Traditional timber windows
Traditionally the majority of windows and doors were made from locally sourced timber. They ranged in style, design and material depending upon when they were made and where they were installed.
Modern windows are constructed largely using aluminum, steel or uPVC.
Notes: Historic Windows – Tywi Centre
https://www.litehausuk.com/aluminium-windows/
https://www.lycawindows.co.uk/windows/upvc-windows-london/modern-upvc-window-house/

## Slide 9: Stone and slate
It is used for external walls, internal load bearing walls and as a roofing material. The colour and structure of the stone can give a region its distinctive look.
A row of traditional stone built Welsh terraced cottages, Bala, Wales
A natural building material which varies widely in use and appearance from area to area. Stone may be cut to a uniform size before use or used in its quarried state.

## Slide 10: Stone and slate (continued)
Slate can be used as a roof covering but is also used to build external walls.
Pile of Bangor Blue slate roof tiles after they have been removed from the roof of a building being refurbished.
A slate wall at the entrance to the main University building, Bangor, Gwynedd.

## Slide 11: Copper
Copper mining and smelting was a huge industry in Wales right up until the mid-20th century, when resources ran low and cheap imports took over. Traditionally, copper was widely used as a roof covering in public and industrial buildings. It turns a distinctive green colour as it oxidises over time. Copper is still used in construction today.
Copper-clad Humanities Building, Plymouth, England
Green Verdigris dome made of copper, Foel Tower, intake of Garreg-ddu Reservoir, Elan Valley, Powys

## Slide 12: Lead
Early plumbing used lead pipes before it was discovered that lead dissolves in water and is poisonous.
Copper or plastic piping is now largely used in domestic plumbing. Lead is still widely used for roof flashings and coverings.

## Slide 13
Any questions?