## Slide 1: PowerPoint 3: Traditional skills used in the construction and building services
PowerPoint presentation
Unit 102: Introduction to the trades in the construction and built environment sector

## Slide 2: Traditional skills required
All construction and building services tradespeople need to be able to measure, mark out, cut, install and finish to a standard that is accurate and with a finish that is aesthetically pleasing.
People working in the construction and building services trades today will need to use traditional hand skills to complete many maintenance and repair tasks.
You will need to measure carefully and cut accurately to ensure a good-quality finish.

## Slide 3: Measuring
For every job you work on, you will be working to a given size. This will generally have a tolerance, e.g. a door frame is required to be 900mm wide with a tolerance of +/− 2mm, which means it is acceptable the door frame is between 898mm and 902mm.
It is important that when measuring or checking a measurement you ensure the rule you are using is accurate and that you are using it correctly to obtain the most accurate measurement possible.
Measure twice, cut once

## Slide 4: Measuring: Units
Traditionally materials were all supplied in imperial measurements. Most are now sourced in metric measurements.
Units for measuring | Metric units | Imperial units
Length | millimetre (mm) metre (m) kilometre (km) | inch (in) or " e.g. 6" (6 inches) foot (ft) or ' e.g 8' (8 foot)
Liquid | millilitre (ml) litre (l) | pint (pt)
Weight | gramme (g) kilogramme (kg) tonne (t) | pound (lb)

## Slide 5: Calculations
Numeracy skills are essential for carrying out daily tasks such as calculating measurements, linear metres, areas and volumes of materials required, and air and liquid flow volumes; working with formulas to true dimensions; and calculating electrical loads and voltage resistance to ensure the correct cabling and fuses are selected.

## Slide 6: Calculating linear metres
Linear metres are the total of an individual component’s measurements added together. Linear means how long a number of items would measure from end-to-end if laid in a straight line. Examples of things that are calculated in linear measurements are:
skirting board
lengths of timber
DPC
building line
wallpaper.
For example: 4 pieces @ 3.3m = 13.2m

## Slide 7: Calculating area
To find out how much material is required to cover a surface such as a floor or wall you need to calculate its area. Area is the measurement of a two-dimensional surface, e.g. the surface of a floor, wall, glass window or a roof. For example, you would need to calculate the area of cavity walls in order to work out how many bricks and blocks you need.
To find the area of a surface you need to multiply its length by its width (L × W), or multiply one side by the other. This will give you an answer which is expressed in square units (²). For example, mm², m² or km².
For example: 3.3m × 3.3m = 10.89m2

## Slide 8: Calculating volume
The volume of an object is the total space it takes up, e.g. the amount of paint in a tin, a foundation for a wall or the capacity of a concrete mixer. Volume is shown as m³ (cubic metres). To find the volume of an object you must multiply length by width by height.
volume = length × width × height
For example: 3.3m × 3.3m × 3.3m = 35.937 m3

## Slide 9: Measuring: Drawings
It is important to be able to interpret information from a drawing correctly in order to ensure you have all the measurements you need before starting work.

## Slide 10: Measuring: Levels
Levels on a building site refer to a point known as an ordnance benchmark, or OBM, which is a permanent reference point. From the OBM a temporary benchmark or TBM is set up on-site.
A level can then be transferred from the TBM to datum points around the site. A laser level can be used to transfer levels over long distances.
Ordnance benchmark symbol
Temporary
benchmark

## Slide 11: Examples of traditional skills used in bricklaying
Measuring and setting out
Cutting
Installing masonry
Finishing – jointing and pointing

## Slide 12: Examples of traditional skills used in BSE trades
Measuring and marking out
Cutting pipes
Installing electrical components
Installing plumbing components

## Slide 13: Examples of traditional skills used in plastering
Measuring and marking out
Cutting plasterboard and components
Installing cornice/beads
Finishing floor screeds and plaster

## Slide 14: Examples of traditional skills used in carpentry and joinery
Marking out
Cutting
Fixing timber

## Slide 15: Measuring and marking out tools
Measuring tools are used either to transfer measurements from one component to another or to check known measurements. Many tasks will involve measuring, marking out and checking using some of the tools below.
Tape measure
Rule
Folding rule
Spirit level
Being able to measure accurately will mean you can make the most economic use of materials and therefore reduce waste.

## Slide 16: Measuring and marking out tools (continued)
The term ‘marking tools’ refers to the tools used to mark the required measurements, such as string or chalk lines.
Gauges can also be used for measuring and marking out components.
Squares are used for marking out and checking angles and corners.

## Slide 17: Cutting and finishing tools and equipment
Hand tools used for cutting and shaping materials include, for example:
chisels
bolsters
pipe cutters
hand saws.
Finishing tools that you may need to use include:
trowels
spatulas
paint brushes
jointers.

## Slide 18: Using tools
It is important to ensure the highest standards of safety when using, maintaining and storing hand tools. Using the right tools for the job will produce the fastest and most accurate results.
Always make sure you are using the appropriate PPE for the task you are doing (safety glasses or goggles, gloves, etc.).

## Slide 19
Any questions?