## Slide 1: PowerPoint 3: Understanding the stages of construction and the installation of services
PowerPoint presentation
Unit 103: Introduction to the built environment life cycle

## Slide 2: Building structure
A building is split into three distinct parts:
Substructure: Anything below ground level is classed as been part of the substructure.
Superstructure: Everything structural above ground level is classed as been part of the superstructure.
Internal components: Everything that goes into a building that is nonstructural is classed as an internal component.

## Slide 3: Parts of the substructure: Foundations
The type of foundation used will depend on the type of building and the ground conditions. The most common types are:
Brick pillar
Pad foundation
Steel column
Traditional strip foundation
Pad foundation
Pad foundation with bolts

## Slide 4: Parts of the substructure: Foundations (continued)
The type of foundation used will depend on the type of building and the ground conditions. The most common types are:
Hardcore
Foundation concrete
Raft foundation
A cylindrical pile foundation

## Slide 5: Examples of a typical domestic building's substructure

## Slide 6: Parts of the superstructure
The superstructure is best described as any part of the building above ground level that bears a live load. This includes:
External walls: These are constructed using either brick, block or stone outer leave with lintels and cills forming openings, an inner leave of brick, block or timber frame is secured using brick ties, the cavity between these is filled with insulation.
Decorative finish
Floor
Inner leaf
Wall tie
Insulation
Outer leaf

## Slide 7: Common brick bonds
Stretcher brick bond is the most common bond. It is easy to lay with little waste and is made up of stretcher set in rows, with each course been offset by half a brick.
English brick bond is made up of alternating courses of stretchers and headers.
Flemish brick bond is an alternating layer of heads and stretchers on a single course, with the next course laid with the header in the centre of the stretcher.

## Slide 8: Load-bearing internal walls
Any internal wall that supports the overall structure is known as a load-bearing wall; they normally carry the ends of the upper floor joists. They are normally constructed using block work; however, bricks and timber framed construction are also used.
Head
Sole plate
Noggins
Studs
Head plate
Timber stud wall
Puncheon

## Slide 9: Solid ground floors
Types of floors include: solid ground, block and beam, suspended timber ground, upper timber.
Early solid ground floors built in the 1930s to the 1950s had issues with rising damp as many did not have any damp proof membranes fitted. Modern solid floors include a damp proof membrane and a layer of insulation.
Screed
Insulation
Concrete DPM
Sand blinding
Hardcore
Concrete floor

## Slide 10: Suspended timber floors
The principle has remained the same: timber joists span the width of the building with intermediate supports (honeycombed dwarf walls) ever 1.2m, allowing for small timber section sizes to be used.
Suspended timber floor construction has only changed slightly over the years with the introduction of proprietary fixings and modern insulation and ventilation regulations.
Honeycombed sleeper wall
Joist supported on hangers
Slab on hardcore or blinding
DPC min 150mm
above ground level
Suspended wood floor

## Slide 11: Timber upper floors
Timber upper floors need to span the full distance of the room below without any intermediate support, the timber sections need to be able to span this distance and take any loads without failing so are usually a much thicker section size (the building regulations give the sizes to be used).
More modern methods include I beams and metal web (posi- joists); these are lightweight engineered alternatives.
Posi-joist
I-beam

## Slide 12: Roofs
Roofs can be either traditionally cut and erected using sections of timber or constructed using prefabricated trusses. There are various types of roof design and coverings from the simple to the complex, each serving the purpose of providing protection from the elements and providing insulation.
Collar roof
Loads imposed are spread to preventing collapse

## Slide 13: Traditional cut roof components
LEVEL 2 DIPLOMA IN SITE CARPENTRY AND BENCH JOINERY
305
Gable end
Gable end
Eaves
Eaves
Jack rafter
Wall plate Crown rafter
Hipped end
Hip rafter
Purlin
Verge
Valley rafter
Cripple jack rafter
Ridge board
Common rafter

## Slide 14: Truss roofs
Trusses are available in many formats to suit the end user, the span and the loads imposed.
Fan
Attic
Mono
Girder
King post
Fink

## Slide 15: Truss roofs (continued)
The safest way to erect a roof. These are constructed at ground level and craned into place.
Crane
Spreader bar
Slinging from joists
Manually lifting trusses
Mechanically lifting trusses

## Slide 16: Roof coverings
Roof covers are available in a wide range of material. Traditional locally available materials were used in the past, but today many man-made materials are used, such as clay tiles, slate, concrete tiles, thatch, interlocking metal sheets, fiberglass, and so on.
Slate
Cement fibre slate
Roof tiles

## Slide 17: Stairs
Stairs are designed to allow access between floors. They come in different styles and layouts to fit available space. However, all types must be compliant with Building regulation K.

## Slide 18: Stair strings
Each flight of stairs has two strings in the image:
the right-hand string has been cut to follow the treads and risers; this is known as a cut string
the left-hand string has an equal width down the full length that encloses the treads and risers; this is known as a closed string.
The stair string or stringer is the section of timber that is housed to accommodate the treads and risers.

## Slide 19: Internal components
Any component that can be removed without affecting the integrity of the structure is classed as an internal component. These include:
non-load-bearing partition wall
plasterboards and plaster
second fix carpentry: doors, windows, frames, mouldings, fitted units (kitchen, bedroom)
second fix sanitary ware: toilets, baths, showers, basins, sinks and drainage
decorative finishes: paint and wall coverings.

## Slide 20: Superstructure
External walls: brick bonds, stone, block, lintels (traditional, modern), cills, insulation, brick ties.
Cladding materials: timber, metal, plastic.
Floors: solid ground floor, suspended timber floors, upper timber floors, block and beam.
Roofs: flat, gable, hips and valleys, traditional and trussed, roof coverings.
Straight flight and with turns stairs: quarter-turn, half-turn, winders, closed and cut string.

## Slide 21: Internal components
Internal components are applied or fitted after completion of the superstructure these can be classed as either first or second fix
First fix is anything prior to plastering, i.e. partition walls, door frames and linings, plumbing and electrical runs.
Second fix is everything after plastering, i.e. hanging doors, decorative mouldings, sanitary fittings and drainage, fitting units and kitchens, electrical sockets and appliances.
Final finishing includes tiling, painting and decorating.

## Slide 22: Sequencing of works
Before building work can commence, you need to plan the work activities to ensure work is completed to the client’s requirements and within the timescale agreed. Planning any construction or building services project starts well before any personnel arrives on site, and includes:
writing the of Programme of Works
writing method statements
carrying out risk assessments
planning site layout
organising suppliers, sub contractors, welfare facilities plant and equipment hire etc.

## Slide 23: Sequencing of works (continued)
Remember the 6 Ps:
Proper Planning and Preparation Prevents Poor Performance

## Slide 24: Critical path analysis
Critical path analysis (CPA) is a method used to sequence the tasks required to complete a project. It shows what must be completed in an orderly sequence and what can be completed simultaneously to achieve the planned outcome in a timely manner.

## Slide 25: Gantt chart
A Gantt chart (named after its inventor Henry Gantt) lists all the tasks needed on the vertical axis and the time intervals on the horizontal axis in hours, days or weeks (dependent on the size of the project).
Labour plant and equipment can also be shown, allowing for effective planning and ordering of materials.
Designated time for each task is added during the planning process and the actual times taken during the construction process can be added later. This allows for the necessary actions to be implemented at the right time and any changes can be mitigated to diminish the impact of any delays on the overall project.

## Slide 26: Example of a basic Gantt chart
Green planned time
Red actual time

## Slide 27: Site communication
What is communication and how is it achieved?
Communication is the process or tool which people use to exchange or pass on information.
How do we exchange or pass on information?
There are many ways to communicate.

## Slide 28: Importance of communication
Good communication is important, as it can help to:
increase work productivity and so time management
ensure smooth day-to-day running of the site
reduce unseen costs – storage, damage, returned deliveries, slow work progress
enhance morale and working relationships between all team members
encourage quick and accurate relaying of information between members of the workforce.
ensure a safe working environment is maintained.

## Slide 29: Communication methods
There are many ways to communicate.
Verbal or oral communication (talking) is an example. This includes:
group discussions
meetings, lectures etc
face-to-face, one-on-one
telephone conversations, video links.

## Slide 30: Verbal communication
Verbal communication is the quickest and most common method of communicating.
We use speech in two ways:
Informally – general conversations with your friends and family etc; chatting to people.
Formally – at work, during interviews, on the telephone to customers.

## Slide 31: Written communication
Letters – personal and official.
Memos and notes – short and precise.
Timesheets – various forms.
Invoices – used to bill customers.
Drawings and sketches.
Specifications.
Schedules – lists of building components.
Graphs and charts – used to display data.

## Slide 32: Electronic communication
Involves using electronic equipment, including:
telephone and video calling equipment
fax machines
television and radio
computers – email and the internet.

## Slide 33: Signs and notices
Signs and notices are designed to communicate information in a visual format.
They can cross language barriers through the use of symbols.
RAG rated.
Show safe exit and escape routes.
Are placed in prominent positions and are usually associated with specific H&S issues.

## Slide 34: Communication channels: Examples
From | To | Method
Architect | Directors / Clerk of works / Site managers | verbal, electronic, written
Directors / Clerk of works | Site managers | verbal, electronic, written
Site managers | Trade personal | verbal, electronic
Site managers | Builders merchants | verbal, electronic, written
Trade personal | Operatives | verbal, electronic
Operatives | Trade personal | verbal, electronic

## Slide 35: Other forms of communication
Body language: A non-verbal method that can show an individual’s mood and feelings.
Sign language and gestures: Another non-verbal method of communicating often used to communicate between drivers and banks persons.

## Slide 36
Any questions?