## Slide 1: PowerPoint 7: Know the process for demolition and destruction of buildings and structures
PowerPoint presentation
Unit 103: Introduction to the built environment life cycle

## Slide 2: The main requirements in decommissioning
Eventually most buildings will need to be demolished because they have come to the end of their viable life cycle or are in the way of a new development.
Planning permission is not required if a building is less than 50 cubic metres, but is required for most other buildings. It is also required for unlisted buildings in a conservation area in Wales only.
A detailed sequence of work needs to be drawn up before any demolishing can commence and must include:
isolation of all services
risk assessments and method statements.

## Slide 3: Environment impact and health and safety
Isolation of services: Gas, electricity, water supply and telecommunications all need to be isolated. Failure to do so can result in the release of toxic and explosive gases into the atmosphere, the risk of electrocution to operatives, and flooding leading to contamination of the waterways and land.
Risk assessments and method statements: These must include any specific risks and hazards associated with the removal and demolition of a property, cover the materials involved and preventing any debris and contamination leaving the location, so protecting the general public and the local environment from work undertaken.
For further information visit the HSE website https://www.hse.gov.uk/construction/safetytopics/demolition.htm

## Slide 4: Selecting the demolition method to use
Appropriate measures need to be in place to prevent any dangerous dusts such as asbestos leaving the site. It is common practice for this to be manually removed before any other work commences.
Gas supplies must be safely disconnected to reduce the chance of an explosion or fire, electricity disconnected to reduce the chances of electrocutions and water turned off to prevent flooding and leaching of containments.
Before any demolition can begin, the environmental impact needs to be considered, as well as access to the site.

## Slide 5: Risks associated with the demolition process
Entrapment
Crushing
Falling objects
Explosion
Asbestosis – caused by exposure to asbestos
Contact with chemicals
Manual handling injuries
Inhalation of gases and dusts

## Slide 6: Types of demolition
Dismantling/Deconstruction
This is the process of taking down a structure carefully and methodically, often in a reverse process of the one that was used to initially construct it.
It is mainly used if the building is of historical importance, and is to be rebuilt in another location, or is in a location that does not allow any other method of demolition to take place.

## Slide 7: Types of demolition (continued)
Interior demolition Interior demolition is the taking apart of interior portions of a structure while preserving the exterior, usually in preparation for a renovation project. This usually includes the removal of walls, ceilings, pipes, etc.
Selective demolition A selective demolition project involves the removal of specific interior or exterior portions of a building while protecting the remaining structure and nearby structures.
Total demolition Total demolition is the demolition of an entire structure.

## Slide 8: Crane and wrecking ball
Less widely used today as modern methods are more accurate and faster.
Wrecking balls range from 1,000 to 12,000 pounds in weight and are made from forged steel (an alloy of carbon and iron).
They are round so they do not get trapped in a buildings structure when they are slammed into it – like a giant sledgehammer or when dropped from a height by a crane.
Link to video showing wrecking ball in action:
https://www.dailymotion.com/video/x61zll3

## Slide 9: Implosion
Implosion uses a series of explosives to destroy the buildings vertical supports, causing the building to collapse into itself. Implosion is most often used to bring down large structures, such as chimneys, cooling towers, tower blocks, etc.
Video link showing implosion of three tower blocks:
https://youtu.be/uMIiQGkLQo8

## Slide 10: Mechanical demolition
Mechanical demolition uses a high-reach arm machine fitted with either a crusher, shears, hammer or bucket to break and remove sections of a building starting at the top and working down.
Shears
Crusher
Bucket

## Slide 11: Stages involved in removing demolition waste
Planning: Ensures all permissions, plant, equipment policies and procedures are in place.
Site security: Protect the general public from work activities.
Isolation of services: Protect operatives and the environment.
Removal of hazardous waste: Protect operatives and the environment, including reduced land fill.

## Slide 12: Stages involved in removing demolition waste (continued)
Architectural salvage: Removal of specific items of value for reuse
On-site processing of aggregates: Can be reused on-site or shipped out ready processed.
Recycling metal waste: Reduced carbon footprint.

## Slide 13
Any questions?