## Slide 1: PowerPoint 2: Health and safety regulations
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Session aims
In this session you will gain an understanding of the different safety rules and regulations. These will include:
The Health and Safety at Work Act (HASAWA)
Reporting Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Control of Substances Hazardous to Health (COSHH)
Provision and use of Work Equipment Regulations (PUWER)
Manual Handling Regulations
Personal Protective Equipment (PPE) at Work Regulations

## Slide 3: Session aims cont…..
Work at Height Regulations
Control of Noise at Work Regulations
Control of Vibration at Work Regulations
Electricity at Work Regulations
Lifting Operations and Lifting Equipment Regulations (LOLER)
Construction (Design and Management) Regulations (CDM)
Approved Code of Practice (ACOP)
HSE information.

## Slide 4: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
The RIDDOR Regulations are all about reporting accidents. They cover:
    deaths and major injuries
    incapacity to work for more than 3 days
    specified diseases
    dangerous occurrences or near misses.
  Any of the above occurrences must be reported to the HSE using the prescribed form.
  This is also available on the web at www.riddor.gov.uk

## Slide 5: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
It is vital that accurate records are kept of any incident. For example, records may be kept by:
  keeping copies of report forms in a filing system
  recording the details on a computer
  keeping a written log in a notebook.

## Slide 6: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
If you choose to report the incident by telephone or through the website, the Incident Contact Centre will post you back a copy of the record held.
You will be able to make amendments to the record if you feel the report is not fully accurate.

## Slide 7: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
The RIDDOR Regulations include the following personnel:
    employers
    employees
    self-employed
    trainees
    other people injured on employers’ premises, such as visitors.

## Slide 8: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of major injuries include:
    any fracture, other than to the fingers, thumbs or toes
    amputation of any limb
    dislocation of the shoulder, hip, knee or spine
    loss of sight or penetrating eye injury.

## Slide 9: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of serious conditions include:
  certain eye injuries
  electric shock requiring attention
  unconsciousness through lack of oxygen
  decompression sickness
  poisoning
  acute illness due to exposure of certain materials
  hospitalisation for more than more than 24 hours.
Notes: Title
The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of serious conditions include:
certain eye injuries;
electric shock requiring attention;
unconsciousness through lack of oxygen;
decompression sickness;
poisoning;
acute illness due to exposure of certain materials;
hospitalisation for more than more than 24 hours.

## Slide 10: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of reportable diseases include:
  certain poisonings
  some skin diseases such as occupational dermatitis and skin cancer
  lung diseases including occupational asthma, farmer's lung, pneumoconiosis, asbestosis
  infections such as: hepatitis, tuberculosis, anthrax, legionellosis and tetanus
  other conditions such as: occupational cancer, decompression illness and hand-arm vibration syndrome.

## Slide 11: The Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR)
Examples of reportable occurrences include:
  structural collapses such as buildings or scaffolds
  fires and explosions
  releases of gasses or other dangerous substances
  failure of breathing apparatus while in use
  incidents with dangerous substances in transit
  contact with or arcing of overhead cables.

## Slide 12: RIDDOR – Summary
The RIDDOR Regulations cover:
  deaths, major injuries and incapacity to work for more than 3 days
  specified diseases
  dangerous occurrences or near misses.
And finally….
  keep records of all reports
  remember RIDDOR involves everyone at work.

## Slide 13: Control of Substances Hazardous to Health
These regulations are usually referred to as COSHH and they contain responsibilities for:
  employers
  employees
  self employed
  subcontractors.
The regulations are aimed at protecting people when they are working with substances hazardous to their health.

## Slide 14: Control of Substances Hazardous to Health
The regulations state what employers must do.
  Assess risks to health caused by substances. used at work;
  Prevent or control exposure.
  Ensure use of control methods.
  Monitor the work environment.
  Carry out necessary health surveillance.
  Provide information, instruction and training as necessary.
  Provide suitable storage for hazardous substances.

## Slide 15: Control of Substances Hazardous to Health
The regulations also state what employees must do.
  Co-operate with the employer.
  Make correct use of control measures (safe systems, safety equipment).
  Report all defects (plant, machinery and safety equipment and other control measures).
  Attend medical examinations when required.
  Provide health information to medical advisers when necessary.

## Slide 16: Control of Substances Hazardous to Health
Hazardous substances can be:
  specified by law
  recognised from experience
  recognised with common sense.
Examples of hazardous substances include:
cement | plaster | wood
paint | MDF | paints
thinners | solvents | bitumen
oil | grease | dust.
fumes |  | 

## Slide 17: Control of Substances Hazardous to Health
Alternatively, hazardous substances may exist all around our working and living environment.
For example, there may be toxic substances already on site such as:
  in the soil from a previous use of the site
  silica contained in masonry and mortars
  accumulations of bird droppings
  substances left by others
  spillage of hazardous liquids.

## Slide 18: Control of Substances Hazardous to Health
COSHH does not apply to work with:
  asbestos
  lead
  radioactive materials.
These substances have their own specific legislation as they present a much greater hazard. Specialist training is required to be able to work with these substances.

## Slide 19: Control of Substances Hazardous to Health
solid materials | liquid
gas | micro-organisms.
breathed in | absorbed through the skin
swallowed. | 
Harmful substances may be in the form of:
Hazardous substances can be:
Effects vary between individuals but some may be instant and result in long-term illness or even death.

## Slide 20: COSHH – things to remember
Where am I working?
What are the hazards?
What are the rules? (safe systems, safety equipment)
Who else is involved? Can I endanger them? Can they endanger me?
How do I plan the work?
Does everything work correctly?
Do not use unsafe equipment: report all defects.

## Slide 21: Control of Substances Hazardous to Health
Look out for these signs:
Toxic or very toxic
Flammable / risk of fire
Harmful/Irritant
Corrosive

## Slide 22: Manual Handling Regulations
The Manual Handling Operations Regulations (often abbreviated to MHOR) are health and safety legislation that affects both employers and employees.
It passed into law in 1992, and was amended in 2002.

## Slide 23: Manual Handling Regulations continued
MHOR 1992 set out a clear ranking of measures for dealing with risks from manual handling. These are:
first: avoid hazardous manual handling operations so far as is reasonably practicable
second: assess any hazardous manual handling operations that cannot be avoided, and
third: reduce the risk of injury so far as is reasonably practicable.

## Slide 24: PPE at Work Regulations
Employers have duties concerning the provision and use of personal protective equipment (PPE) at work.
PPE is equipment that will protect the user against health or safety risks at work.
It can include items such as safety helmets, gloves, eye protection, high-visibility clothing, safety footwear and safety harnesses. It also includes respiratory protective equipment (RPE).
Session 9 gives an in-depth look at the PPE regs.

## Slide 25: Work at Height Regulations
The purpose of The Work at Height Regulations 2005 is to prevent death and injury caused by a fall from height. If you are an employer or you control work at height (for example, facilities managers or building owners who may contract others to work at height), the Regulations apply to you.
Employers and those in control of any work at height activity must make sure work is properly planned, supervised and carried out by competent people. This includes using the correct type of equipment for working at height. Low-risk, relatively straightforward tasks will require less effort when it comes to planning.
Session 12 gives an in-depth look at access equipment and working at height.

## Slide 26: Control of Noise at Work Regulations
The Control of Noise at Work Regulations 2005 (the Noise Regulations) came into force for all industry sectors in Great Britain on 6 April 2006 (except for the music and entertainment sectors where they came into force on 6 April 2008).
The aim of the Noise Regulations is to ensure that workers' hearing is protected from excessive noise at their place of work, which could cause them to lose their hearing and/or to suffer from tinnitus (permanent ringing in the ears).
The Control of Noise at Work Regulations 2005 replace the Noise at Work Regulations 1989

## Slide 27: Control of Vibration at Work Regulations
The Control of Vibration at Work Regulations 2005 (the Vibration Regulations), came into force on 6 July 2005 and aim to protect workers from risks to health from vibration.
The regulations introduce action and limit values for hand-arm and whole-body vibration.

## Slide 28: Electricity at Work Regulations
The purpose of this guidance is to highlight what can be done by duty holders to achieve electrical safety compliance with the duties imposed by the Regulations.
It is relevant to all work activities and premises except certain offshore installations and particular ships. Of particular relevance to duty holders, it will also be of interest and practical help primarily to engineers (including those involved in design, construction, operation or maintenance of electrical systems and equipment), technicians and their managers.
The Electricity at Work Regulations 1989 (SI 1989/635) (as amended) (the Regulations) came into force on 1 April 1990. The purpose of the Regulations is to require precautions to be taken against the risk of death or personal injury from electricity in work activities.

## Slide 29: Lifting Operations and Lifting Equipment Regulations
These Regulations (often abbreviated to LOLER) place duties on people and companies who own, operate or have control over lifting equipment. This includes all businesses and organisations whose employees use lifting equipment, whether owned by them or not.
In most cases, lifting equipment is also work equipment so the Provision and Use of Work Equipment Regulations (PUWER) will also apply (including inspection and maintenance). All lifting operations involving lifting equipment must be properly planned by a competent person, appropriately supervised and carried out in a safe manner.

## Slide 30: LOLER continued
LOLER also requires that all equipment used for lifting is fit for purpose, appropriate for the task, suitably marked and, in many cases, subject to statutory periodic 'thorough examination'. Records must be kept of all thorough examinations and any defects found must be reported to both the person responsible for the equipment and the relevant enforcing authority.

## Slide 31: Construction (Design and Management) Regulations
Whatever your role in construction, CDM aims to improve health and safety in the industry by helping you to:
sensibly plan the work so the risks involved are managed from start to finish
have the right people for the right job at the right time.

## Slide 32: CDM Regulations continued
CDM also helps you to:
cooperate and coordinate your work with others
have the right information about the risks and how they are being managed
communicate this information effectively to those who need to know
consult and engage with workers about the risks and how they are being managed.

## Slide 33: Approved Code of Practice
Each ACOP is approved by the Health and Safety Executive, with the consent of the Secretary of State. It gives practical advice on how to comply with the law. If you follow the advice, you will be doing enough to comply with the law in respect of those specific matters on which the Code gives advice. You may use alternative methods to those set out in the Code in order to comply with the law.
However, the Code has a special legal status. If you are prosecuted for breach of health and safety law and it is proved that you did not follow the relevant provisions of the Code, you will need to show that you have complied with the law in some other way, or a court will find you at fault.

## Slide 34
Any questions?