## Slide 1: PowerPoint 11: Access equipment
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Working at height – statistics
Nearly half of all fatal injuries in construction are caused by falls from height and these are the most common cause of fatal injuries in construction. There are two main categories of fall:
  high falls (over 2m)
  low falls (less than 2m).
  High falls are the biggest cause of fatal injury.
Most falls are from ladders (around 24%).
Falls from ladders (average 515 injuries per year).
Scaffolding (average 150 injuries per year).
Work area/platforms (average 128 injuries per year).

## Slide 3: Working at height – issues
The most common incidents involve:
  over-reaching
  balancing
  equipment failure
  misuse of equipment
  unexpected movement (particularly where ladders are involved)
  failure of a fragile surface.

## Slide 4: Working at height – some reasons for incidents
These events usually arise due to poor management control rather than because of equipment failure.
  Failure to recognise a problem
  Failure to ensure that safe systems of work are followed
  Failure to provide a safe system of work
  Inadequate information, instruction, training or supervision provided
  Failure to use appropriate equipment
  Failure to provide safe plant/equipment

## Slide 5: Using scaffolds safely

## Slide 6: Working at height
Always make sure that you do the following.
  Plan and organise what you do. Work from a safe and secure place or platform with proper edge protection.
  Only use scaffolds and scaffold towers that are fully and correctly erected.
  Use powered access equipment safely.
  Protect holes and leading edges, e.g. with guard rails and toe boards.
  Make sure that you are trained and competent to do the task.
  Raise any problems that you may have with your supervisor.

## Slide 7: Working at height – do’s and don’ts
When carrying out work on a roof, you should:
  avoid working in poor weather
  avoid working on sloping roofs without proper edge protection
  avoid throwing down waste or equipment.
Take care when working on or near fragile material – you can fall through as well as off it.

## Slide 8: Working at height – do’s and don’ts
Only use ladders for light work of short duration.
Also:
  Correct angle and secure top and bottom to prevent slipping (1 out for 4 up).
  Always make sure ladders are properly maintained.
  Never paint any ladder as this can hide defects.
  Never use a ladder with missing or damaged parts.
  Never over-reach.

## Slide 9: Types and use of access equipment
Work which cannot be carried out from ground level will require a working platform. These include:
  scaffolding
  mobile/static towers
  metal split head scaffolds
  trestles
  lightweight staging
  hop ups
  ladders.

## Slide 10: Metal split head scaffold
  Used to support working platforms and provide a continuous working area, ideal for ceilings.
  Made from ferrous metals and are usually galvanised.
  Will require regular greasing and oiling to allow adjustment.
  A minimum of four split heads is necessary for a working platform.

## Slide 11: Mobile tower scaffold
  Used for minor work to be carried out at lower levels either in or out of a building.
  Consist of a series of frames which are joined together to form a tower.
  Towers are mainly fitted with wheels to allow movement without dismantling.

## Slide 12: Trestle scaffold
  Platforms supported by ‘A’ frames or a similar type of folding support.
  Intended for lightweight work for short periods of time.
  Scaffold boards or lightweight staging provide the working platform.

## Slide 13: Lightweight staging
  A specially constructed timber/aluminium platform.
  Used for spanning greater widths than scaffold boards.
  Can be used without intermediate support when used on trestles or roof trusses.

## Slide 14: Hop ups
  Used for reaching low level work.
  Mainly used by painters and decorators or plasterers.
  Designed with a step to enable operatives an easy access.

## Slide 15: Ladders
There are two main types of ladders:
  pole ladders
  extension ladders.
A pole ladder is made from one straight tree trunk, cut down the middle; this is to ensure strength and flexibility.
Extension ladders are made from wood or metal and have more than one section sliding past the other.

## Slide 16: Stepladders
These are mainly used internally and should be used fully opened. Stepladders provide a working platform where the work area is just out of reach.
Like ladders, they can be timber or aluminium, consisting of stiles supporting flat treads.
A back frame is hinged at the top and secured at the bottom by a cord or locking bar.
Timber stepladders must not be painted, as this will hide any defects

## Slide 17: Types and use of access equipment – summary
  There are enough types of access equipment for any job at height to be carried out safely.
  Most access equipment is made from either metal or timber, depending on its uses.
  If you find any defects on a scaffold or working platform report it immediately to your supervisor.

## Slide 18
Any questions?