## Slide 1: PowerPoint 10: Safety signs
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Safety signs overview
Safety signs are positioned in and around the construction site to advise, give guidance and protect the workforce.
These signs are intended to give the operatives, client and visitors a clear message of the expectations in and around the site.
Safety signs are positioned at the start of a contract and are present until the final day of the site’s operations.

## Slide 3: Safety signs and the law
The Health and Safety (Safety Signs and Signals) Regulations require employers to provide safety signs to raise awareness of risks to health and safety.
  There are four types of safety signs in general use.
  Each has a designated shape and colour.
  They make sure that information is given in a standard format with minimum use of words.

## Slide 4: Safety signs
Remember the general duty of employees:
  cooperate with your employer by observing signs
  comply with the law and employer’s safe systems of work
  use safety equipment properly and correctly
  do not tamper with, deface, or remove safety signs.

## Slide 5: Prohibition signs
This sign means: you must stop or must not do something.
  It is circular with a white background, black pictogram and red border and crossbar.
  All writing is white on a red background.

## Slide 6: Mandatory signs
These mean that the sign must be obeyed.
  These signs feature a blue circle with white pictogram.
  Any text must be white on a blue background.

## Slide 7: Warning signs
These mean there is a risk of danger.
  A warning sign is triangular with a yellow background, black pictogram and black border.
  All writing is black on a yellow background.

## Slide 8: Safe condition signs
These mean safe place or safe way to go.
  These signs are a green rectangle or square with a white pictogram and text.

## Slide 9: Safety signs – summary
There are four types of safety signs in general use:
  Prohibition.
  Mandatory.
  Warning.
  Safe condition.
Each have a designated shape and colour.
If you are unsure about the meaning of a sign, or the risks involved in a task, always ask your supervisor.

## Slide 10
Any questions?