## Slide 1: PowerPoint 12: Power tools
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Working with power: electrical safety
Electricity is a very dangerous form of energy:
  it is invisible
  it can start fires
  it can kill.
  In the construction industry, electrocution causes a significant number of serious injuries and deaths each year. It is a serious hazard.
Notes: Title
Working with power: electrical safety
Electricity is a very dangerous form of energy:
  it is invisible;
  it can start fires;
  it can kill.
    In the construction industry about 7 people are killed each year by electrocution.
    Many more are seriously injured.

## Slide 3: Working with power tools
Some tips for safe use of power tools:
  Follow the safety procedures and never tamper with live electrical cables or machinery.
  Make sure any items of electrical equipment, including power tools, are in good condition and safe to work with.
  Do not plug in the power tool before trying it.
  If you plug in the power tool and there is a fault, you could be seriously injured or killed.
  Minor shocks can trigger a secondary accident, such as a fall from height.
Notes: Title
Working with power tools
Some tips for safe use of power tools:
  Never tamper with live electrical cables or machinery.
  Make sure any electrical equipment including power tools are in good condition and safe to work with.
  Follow the safety procedures.
  Do not plug in the power tool before checking it out.
  If you plug in the power tool and there is a fault, you could be seriously injured or killed.
  Minor shocks can trigger a secondary accident such as a fall from height.

## Slide 4: Working with power tools
Before use always check the body of the power tool:
    is it clean?
    is it dry?
    Portable Appliance Testing (PAT) label
    no visible cracks
    no loose or missing parts.
Notes: Title
Working with power tools
Before use always:
Check the body of the power tool:
      is it clean?
      is it dry?
      Portable Appliance Testing (PAT) label;
      no visible cracks;
      no loose or missing parts.

## Slide 5: Working with power tools
Before use always check the cable of the power tool for:
    bare wires
    frayed ends
    cuts or burns
    other obvious damage.
Notes: Title
Working with power tools
Before use always:
Check the cable of the power tool for:
      bare wires;
      frayed ends;
      cuts or burns;
      other obvious damage.

## Slide 6: Working with power tools
Before use always check the voltage label of the power tool:
    is it 110 volts?
    does it have a 110-volt yellow plug?
Check the plug of the power tool for:
    cracks
    loose or misshapen pins.
Notes: Title
Working with power tools
Before use always:
Check the voltage label of the power tool:
      is it 110 volts?
      does it have a 110 volt yellow plug?
Check the plug of the power tool for:
      cracks;
      loose or misshapen pins.

## Slide 7: Working with power tools – summary
Don’t forget!
  Check the voltage – is it 110 volts? Does it have a 110-volt yellow plug?
  Are the tool, cable and plug all in good condition?
  Know how to isolate power in an emergency.
  Although there is no set order for checking portable power tools, it is good practice to plan your own procedure.
  Get into the habit of checking every power tool before you use it.
  Your life may depend on it!
Notes: Title
Working with power tools – summary
Don’t forget!
  Check the voltage - is it 110 volts, does it have a 110 volt yellow plug?
  Is the tool, cable and plug in good condition?
  Know how to isolate power in an emergency.
  Although there is no set order for checking portable power tools, it is good practice to plan your own procedure.
  Get into the habit of checking every power tool before you use it.
  Your life may depend on it!

## Slide 8: Drill driver
The drill driver is highly versatile and can be used with different bits.
They insert and remove screws, cut circular holes with a saw cutter, or buff and polish.
Various designs of chuck are available for rapid interchange of bits.

## Slide 9: Percussion drills
This drill has a percussive hammer effect which enables it to bore into hard materials, such as bricks, blocks, stone and concrete.
This percussive action is optional and is brought into operation by means of a switch.
It can also drill free from percussion and be used to drill holes into materials such as timber, plastic or steel.

## Slide 10: SDS hammer drill
This drill has a hammer effect which is used to bore holes into hard masonry products such as bricks, blocks, stone and concrete.
The rotation action is operated by a switch and is easy to discard.
The still hammer action may be used when chasing walls.
This drill also has a unique chuck which requires the drill bits to have a certain style of insert end.

## Slide 11
Nail guns come in two forms: gas and battery. The gas nail gun also depends on battery power.
They are used to drive nails into the surface, saving on time, labour, damage and vibration.
The nails come in strips and are inserted into the bottom of the guns and are fed up through the gun as each nail is fired.
Nail gun

## Slide 12
Any questions?