## Slide 1: PowerPoint 13: Plant and machinery
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2
The transformation by construction of a design into a useful structure is accomplished by people using technology and machines (plant).
As machines evolve and technological capabilities improve, the way in which projects are constructed also changes.
But working near moving plant and machinery can be a high-risk activity. It is essential to ensure the safety of people working at or near locations where plant is used.
Use of plant and machinery

## Slide 3: Machine utilisation
Selecting the right machine is important because, unlike most other classes of machine, even a slight increase or decrease in physical size can greatly affect application.
There are three key considerations:
transport
productivity
site constraints.

## Slide 4: Plant
Plant is a machine that is either tracked or wheeled and used for clearing land, pushing soil, excavating or loading into trucks.
It is generally something that can be ridden upon and driven, whereas equipment generally refers to hand-held tools or similar.

## Slide 5: Equipment
Earth-moving equipment
Hauling equipment
Hoisting equipment
Conveying equipment
Aggregate and concrete production equipment
Pile-driving equipment

## Slide 6: Machinery use
Excavation
Digging and moving large quantities of earth
Placement
Compacting
Levelling
Dozing
Grading
Hauling operations involved in construction

## Slide 7: Trenching machine or excavator
Used for excavating trenches for laying pipelines, sewer, cables etc.
Operation is quick, giving the required depth or width.
Two types of trenching machine: wheel type, ladder type.

## Slide 8: Scrapers
Unique machine for digging and long-distance hauling of plough-able materials.
Self-operating machine
It is not dependent on other equipment.
Wheels of machine cause some compaction.
The basic parts of scrapers are the bowl, apron and tail gate or ejector.

## Slide 9: Bulldozer
The heavy blade attached to the tractor pushes the material from one place to another.
The tractor can be of the crawler or the wheeled type.

## Slide 10: Dump trucks
These are used for earth moving.
The selection of the type of dump trucks for a specific job depends on the soil condition.
These are heavy duty trucks, with a strongly built body which is hinged on the truck chassis at the rear end and one side respectively, and can be fitted to the rear in the case of rear dump and to the hinged side in case of the side dump, through the action of hydraulic jacks.
These trucks are suitable for use in hauling wet clay, sand, gravel, quarry rocks etc.

## Slide 11: Hoisting equipment
Hoisting is the lifting of a weight from one location and moving it to another location which is at a reasonable distance. Big projects such as construction of dams, industrial buildings etc. require hoisting equipment.
Hoisting equipment includes jacks, winches, chain hoists and cranes. A crane is the only machine which, as a single piece, is capable of providing three-dimensional movement of a weight.
Cranes are broadly classified as:
1. Stationary or derrick cranes 2. Mobile cranes 3. Overhead or gantry cranes 4. Traveller cranes 5. Tower cranes

## Slide 12: Mobile cranes
These cranes are mounted on mobile units which are either crawler type or wheel type.
Truck cranes have high mobility while the crawler-mounted cranes move slowly.
Crawler-mounted cranes are capable of moving on rough terrain.
These types of cranes consist of two main parts: the bridge and the crab.

## Slide 13: Tower cranes
A tower crane consists of a derrick crane mounted on a steel tower.
Tower cranes are usually used for industrial and residential high-rise buildings. They are commonly used for assembly of industrial plants with steel structures.
The main parts of tower crane are under carriage, slewing platform, tower with operator’s cabin and jibs.
The tower has a truss structure welded from steel bars and channels.

## Slide 14: Belt conveyor
Used when large quantities of materials have to be conveyed over long distances at fast speed.
It consists of a belt running over a pair of end drums or pulleys and supported at regular intervals by a series of rollers called idlers. These idlers are supported on a conveyor frame.
The middle sag provided in the belt prevent the spilling of material. Generally, rubber is most commonly used as conveyor belt.
The belt can be used to transfer loose aggregate and material up a height or around the site.

## Slide 15: Hazards
Plant and machinery can be particularly hazardous when operated in situations where:
people or other vehicles share the same site. Pedestrians are particularly vulnerable in areas where mobile plant and machinery is operated as the operator’s vision may be restricted
entry to the site is uncontrolled
work is being carried out in the vicinity of electrical equipment or in hazardous atmospheres
the plant/machinery is damaged, poorly maintained, used on unstable base or used incorrectly
the load exceeds the capacity of the plant.

## Slide 16: Risk control measures
These include the following:
isolate vehicles and plant used in or around the site and work area from the people on site
provide separate routes or pavements for pedestrians to keep them away from plant and machinery (e.g. footbridges, crossing points)
use fences, barriers and safety signs to secure the area
plan the direction that plant moves, so the visibility of operators is not restricted
use spotters to control traffic movement
implement safe working distances
use audible reversing alarms
ensure notices are in place at all entrances and exits
use designated delivery and turning areas.
make sure all visitors report to the site office.

## Slide 17
Any questions?