## Slide 1: PowerPoint 9: Emergency procedures
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Fire
A fire needs three elements to burn. All three elements must be present for a fire to start. If you remove one element then you can put a fire out.

## Slide 3: Fire triangle
    OXYGEN – or air in normal circumstances, will allow a fire to burn.
    HEAT – a minimum temperature is needed but a naked flame, match or spark is sufficient to start a fire, especially if in contact with something flammable.
    FUEL – can be anything that will burn, e.g. wood, furniture, flammable liquid, gas etc.

## Slide 4: Reducing fire risk
Things which might help reduce the risk of fire being started or people being harmed if there is a fire:
  not smoking at work (no smoking areas should be designated)
  maintaining all electrical appliances in a safe manner
  good housekeeping, being tidy
  removing combustible materials outside to a safe place.

## Slide 5: Reducing fire risk
Help prevent fires by:
  not storing highly flammable liquids if not necessary
  disposing of cigarettes carefully
  have clearly marked fire points nearby
  having procedures if there is a fire
  putting up signs and notices so people know what to do
  having regular evacuation drills
  keeping fire exits clear
  testing fire alarms frequently.

## Slide 6: Which fire extinguisher?
Different types of fire require a different type of extinguisher.
Never use hose reels, water extinguishers or any other means of extinguishing with water on:
    electrical appliances
    any fire involving fats, oils or paints
    any metal fire
    risk of electrocution or explosion.

## Slide 7: Which fire extinguisher?

## Slide 8: In case of fire
If a fire does break out, no matter how small:
  raise the fire alarm
  call the fire brigade
  close all doors and windows to prevent spread
  leave the building
  always keep between the fire and the way out.

## Slide 9: Access and egress
It is a duty of an employer to ensure that employees and the client are safe in and around the construction site.
The employer must ensure that all access to the site is safe to walk around.
The employer must ensure that all walkways are unobstructed, signs are clearly marked, walkways are clearly lit and they are protected at all times on their routes in and around the site.
Employers must provide barriers to protect the workers from any site traffic and prevent them coming into any harm while on site.

## Slide 10: Assembly points
Assembly points, or muster points, must be pointed out to new workers during their induction programmes.
These assembly points are to ensure that, in the event of an alarm being raised on the site, all the workers can safely and quickly move into the zone of the assembly points while the alarm is dealt with.
When in the assembly point zone, a check will be carried out of the total site workforce to check who is present.

## Slide 11: Employer’s emergency roles and responsibilities
Employers are required to carry out many duties on construction sites. However, the following are important duties in relation to emergency procedures.
  Provide adequate supervision and safe systems of work and safe means of access and egress.
  Consult with employees over health and safety matters.
  Display certain signs and notices.
  Have in place adequate measures for emergencies, including fire.
  Appoint someone competent to advise on health and safety.
  Provide first aiders and facilities.

## Slide 12: Employee’s emergency roles and responsibilities
Employees also have numerous duties to carry out on construction sites. However, the following are important duties in relation to emergency procedures.
  Do not fool around at work.
  Report any accidents.
  Report any hazardous situations.
  Always use the right equipment and report any issues with equipment.

## Slide 13: Employee’s roles and responsibilities continued
  Always use the correct and safe way of doing something.
  Do not do anything that is prohibited.
  Observe any safety signs or notices.
  Keep the workplace clean and tidy.
  Do not create any tripping hazards.

## Slide 14
Any questions?