## Slide 1: PowerPoint 8: Personal protective equipment
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Personal protective equipment
The Personal Protective Equipment Regulations 1992 apply to all work situations.
There are over 1000 airborne substances identified as being potentially harmful.
Occupational asthma affects more than 70,000 people.
This number increases annually.

## Slide 3: Personal protective equipment
On many occasions people have to:
wear protective clothing
use protective equipment.

## Slide 4: Personal protective equipment
People wear protective clothing or use protective equipment:
because they have been told to
because it makes sense.
The more often for the second reason, the better.

## Slide 5: Personal protective equipment
You must use the correct PPE for the job.
PPE must fit correctly.
Employers must supply suitable PPE.
Employees must use PPE correctly.
If you cannot prevent, you must protect.
The Personal Protective Equipment Regulations 1992 apply to all work situations.

## Slide 6: Ear protection
This must be worn when required.
Report any defects with equipment to supervisor.
Two basic types or ear protector:
ear plugs
ear muffs.

## Slide 7: Ear protection
Disposable ear plugs:
made from fine mineral fibre, polythene and plastic foam
must be inserted correctly
not to be re-used
only handled with clean hands.

## Slide 8: Ear protection
Ear muffs:
must completely cover ear
sealed to the head by foam or liquid seal
loose muffs are ineffective.

## Slide 9: Eye protection
Required by law if there is the possibility of eye injury. For example, when:
grinding
welding
hammering
cutting.
Or when using:
hot metal
chemicals.

## Slide 10: Eye protection
Goggles or spectacles need:
strength
effective seals to goggles
resistant to temperatures
filters to absorb harmful light.
Always use the correct eye protection for the job.

## Slide 11: Head protection
Construction Regulations 1989 require suitable head protection to be worn on:
all building sites
unless there is no risk of head injury other than by persons falling.
There are many makes of safety helmet available but the type used must be made to British Standard.
You always must wear a safety helmet when required to do so.

## Slide 12: Foot protection
Foot protection is mandatory on all construction sites.
This must be steel toe-capped boots or wellingtons, with a steel midsole to prevent punctures by sharp objects.
Appropriate protective footwear must also have good ankle support.

## Slide 13: Respiratory protective equipment (RPE)
Employers must educate the workforce regarding airborne hazards present in the environment.
The choice of equipment depends upon the:
type of hazard
concentrations of hazardous substances
length of exposure.

## Slide 14: Examples of respiratory protective equipment (RPE)
Disposable dust mask
Dust respirators

## Slide 15: Skin protection
Potentially harmful substances:
pitch, tar, bitumen
cement, brick, stone dust
tile, plaster dust
paint, varnish, lacquer, adhesives
wood dust, fibre glass, resins
solvents, fuels, oils
spirits, thinners, acids, alkalis.

## Slide 16: Skin protection
Ways to protect your skin:
gloves, gauntlets
overalls
goggles
aprons
boots – steel toe caps and mid-sole protection
leggings.
You must wear appropriate skin protection for the job to be done.

## Slide 17: High visibility clothing
High visibility clothing is mandatory in construction sites whenever there are vehicles present.
This type of clothing is worn to notify the operators of vehicles that pedestrians are on the site. The hi-vis clothing is both colourful and reflective.
.

## Slide 18: Things to remember
PPE must be worn when required.
It must be suitable for the work to be carried out
You must use PPE as directed.
Report any faulty equipment.
If unsure about anything – Ask!

## Slide 19: Session consolidation questions
Q. What does PPE stand for?
Q. What PPE could you use to protect your mouth?

## Slide 20
Any questions?