## Slide 1: PowerPoint 14: Areas of specific risk
PowerPoint presentation
Unit 105: Protecting health, safety and the environment when working in the construction and built environment sector

## Slide 2: Session overview
In this session you will learn about dangers associated with the construction industry.
You will find out about safe methods of identification, protection, commissioning and decommissioning of services.
Failure to follow guidelines when working on site can lead to accidents and even fatalities.

## Slide 3: Confined spaces
A confined space:
is large enough that an employee can enter physically and carry out a task
has limited or restricted means for entry or exit.
is not designed for continual occupancy.
This could be a tank, vessel, chamber, pit, silo, vault or hopper.

## Slide 4: Confined spaces
A safe system of work is needed for a confined space operation, requiring:
planning the work
safe access
use of cable- and pipe-locating devices
safe digging practices
safe egress.

## Slide 5: Confined spaces
Some confined spaces require a permit to carry out any work within them. If they do, they usually contain a potential to cause harm such as:
hazardous chemicals
electrical transformers
plant room.

## Slide 6: Establish command
Any team member can be command:
  usually highest trained
  can be passed as more people arrive
  need to know the ICS
  trained in CSR.

## Slide 7: Responsibilities while working in an area of danger
Make initial assessment and evaluation.
Establish goals and objectives.
Determine additional resources.
Establish a command post.

## Slide 8: Key checks prior to entering a confined space
Once information indicates that PPE on hand is adequate:
  obtain air monitoring samples
  assess hazards
  characteristics of space.

## Slide 9: Safety precautions
Perimeter control:
  may need police
  barrier tape, ropes, barricades.

## Slide 10: Hazards present
Atmospheric
Energy sources
Entrapment
Fall
Fire/explosion
Hazardous material

## Slide 11: Industries engaged in excavation
Water, sewer, pipeline contractors
Communication and power line contractors
Concrete worker and drilling contractors

## Slide 12: Hazards of excavation work
Cave-ins
Underground utilities
Materials/equipment falling into excavation sites
Struck-by accidents
Asphyxiation
Explosions
Falls
Electrocutions
Drowning

## Slide 13: Safety considerations
Excavation is one of the most hazardous types of work in the construction industry.
Accidents result from inadequate planning.
Build safety into pre-bid planning.

## Slide 14: Safety considerations
Plan safety into the job. Consider:
  traffic
  proximity of structures and their conditions
  soil
  surface and ground water
  water table
  overhead/underground utilities
  weather.

## Slide 15: Locating utilities
Employers must determine the estimated locations of utility installations.
Contact utility companies before starting excavation.
Utility owners must attempt to find exact location of utilities.
Proceed with caution if the exact location of utilities cannot be found.
Use safe and acceptable means to locate exact locations of installations.

## Slide 16: Safety starts at the surface
Warn mobile equipment operators about the edge of the excavation site.
Ensure there is adequate access and egress.
Take care when walking near excavation sites.
Barricade or cover wells, pits, shafts.
Use appropriate PPE.

## Slide 17: Protecting utilities
Exact locations of utilities must be determined.
Utilities must be exposed before digging.
Excavation sites must be protected and supported to safeguard employees.
Approach utility lines with care.

## Slide 18: Employee access/egress from excavations
Ramps must be designed by a competent person.
Ramps must be structurally sound and not create a tripping hazard.
Use surface treatments on ramps to prevent slipping.

## Slide 19: Employee access/egress from excavations
Trenches that are more than 1.2 m or 4 feet deep need a safe means of egress:
  stairway
  ladder
  ramps.
Means of egress must be fixed and secure.

## Slide 20: Employee access/egress from excavations
Means of egress must be within 7m of workers.
Ladders must extend a minimum of 90cm above the landing.
Use metal ladders with caution around utilities.

## Slide 21: Hazardous atmospheres
Explosive
Flammable
Poisonous
Corrosive

## Slide 22: Loose rock and soil as hazards
Prevent loose rock/soil/ spoil from falling onto employees in excavation sites.
Use barricades to contain material.
Keep surface materials at least 1 m from the edge of excavation sites.
Keep employees off sloped surfaces at levels above other employees.

## Slide 23: Support, shield, and protective systems
Shoring systems support the sides of the excavation with:
  timber
  aluminium
  hydraulic, pneumatic, or mechanical systems.

## Slide 24: Daily inspections
Inspect excavations for possible:
  cave-ins
  failure of protective systems
  hazardous atmospheres
  other hazardous conditions.

## Slide 25: Dangers while working around electricity
Electricity injuries are usually caused by the explosive effects of arcing current, and by any associated fire or flames which may result, when a live cable is penetrated by a sharp object such as the point of a tool.
Such effects can also occur when a cable is crushed severely enough to cause internal contact between the conductors or between metallic sheathing and one or more conductors.
Injuries are typically severe, potentially fatal, burns to the hands, face and body and electric shock is less likely.

## Slide 26: Dangers while working around electricity
Incidents may also arise from cables which have been damaged but left unreported and unrepaired.
Other nearby services, such as plastic gas pipes, may also be at risk from damaged live electricity cables.
This could result in explosions and a greater fire risk.
Great care is needed when working in and around electricity

## Slide 27: Gas pipes
Damage to gas pipes can cause leaks which may lead to fire or explosion
There are two types of damage:
that which causes an immediate leak
that which causes a leak some time later.
The damage may occur at the time the work is carried out or subsequently: for example, poor reinstatement may leave a pipe inadequately supported or subject to unequal forces.

## Slide 28: Water pipes and sewers
Although damage to water pipes is less likely to result in injury, the following may occur:
A jet of water from a main can injure a person. It may also contain stones or other hard objects ejected from the ground around the pipe.
Leaks of water from underground pipes can affect adjacent services and reduce support for other structures, for example: damage to mains can result in flooding, leading to subsequent risks from drowning or the rapid collapse of support to the sides of an excavation; water can enter gas pipes if they are also damaged.
While some sewage is pumped at pressure, sewers are generally gravity-fed, and the main hazard from damage to a sewer is the possibility of contamination.

## Slide 29
Any questions?