## Slide 1: PowerPoint 7: Emerging technologies and materials 3
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 2: Emerging technologies and materials in construction
      Some examples of evolving materials are:
        graphene
        surface coverings
        ventilated building materials
        liquid roof
        transparent aluminum
        self-healing concrete.
                Source https://www.letsbuild.com/blog/10-innovative-construction-materials infographic

## Slide 3: Evolving materials: Graphene
        Graphene was isolated in 2004 by two researchers at the University of Manchester, Professor Andre Geim and Professor Kostya Novoselov. They won the Nobel Prize in Physics for their pioneering work extracting the graphene from graphite.
        Graphene is revolutionising scientific fields due to its unique properties. It has a tensile strength 200 times stronger than steel and an electrical mobility (that is how quick the electron moves) two to three times that of silicon.
Potential applications in architecture include small-scale products such as coatings, solar cells and electronics, long-lasting LEDs, impermeable paint, corrosion-proof steel, interactive panels, spray-on solar panels and self-cleaning concrete.

## Slide 4: Evolving materials: Graphene
        Graphene composites are:
        Stronger than steel
        1 million times thinner than a human hair
        More conductive than copper
        Stretchable, transparent and flexible
        Multidisciplinary, world’s first two dimensional material
https://www.graphene.manchester.ac.uk/learn/applications/composites-and-coatings/Composites_1748x2480.jpg

## Slide 5: Evolving materials: surface coverings
        3D-printed bioplastics
        Waste is a major problem in the construction industry. Dutch firm Aectual believe 3D printing floors and stairs from a renewable bioplastic source will make a difference to the environment.
        Source: https://www.engineering.com/BIM/ArticleID/17639/Aectual-3D-Prints-Everything-from-Floors-to-Walls.aspx

## Slide 6: Evolving materials: Alusion panels
The material: architectural stabilised aluminium foam is claimed to be uniquely versatile, suitable for covering buildings, doors, floors and more.
This Toronto-based business discovered a way of injecting air into molten aluminium that forms bubbles due to the dispersion of ceramic particles in the mix. Benefits include noise reduction, 100% recyclable, strong and non-combustible.
Cymat Technologies
https://www.alusion.com/files/Brochure_AlusionTM_Feb2020.pdf

## Slide 7: Evolving materials: ventilated building materials
        Ventilation refers to the process of 'clean' air (normally outdoor) being supplied to a space, while stale air is removed.
        Ventilated façade system (rain screens): Cladding materials include panels made of fibre cement, ceramics, steel, aluminium. high-pressure laminate (HPL) and aluminium.
        A ventilated façade is two layers of façade separated by an air cavity. This separation creates an open cavity, allowing exchange of the air contained between the wall and the outer cladding.
        Using a ventilated façade has thermal, acoustic and structural benefits.
        Source: https://innowood.com/concealed-fixing/

## Slide 8: Evolving materials: ventilated building materials
        Breathing walls: The design of porous materials for heat exchange and decentralised ventilation
        This study demonstrated how to design pores in building materials so that incoming fresh air can be efficiently tempered with low-grade heat while conduction losses are kept to a minimum. Any material can be used in principle, so long as it can be manufactured with millimeter-scale air channels.
        Source: https://reader.elsevier.com/reader/sd/pii/S0378778817300476?token=C8A5BFBB37535EFCB07423266E08B649B8C6C9ABAD35EA81726D0985E0B987EC2E87B4CE26229EC9F68B3A2C86B1A8C9

## Slide 9: Evolving materials: breathing walls
This is a pneumatic façade, that is a breathable façade. Covered in pore-like holes to allow the air to flow through.
This biomimetic project was led by Stuttgart University student Tobias Becker.
Source: https://youtu.be/a67brMDgiW4
FUTURISM CREATIVEJUNE 22ND 2016 WEBSITE: http://futurism.com

## Slide 10: Evolving materials: building façade
Decker Yeadon developed a breathable façade that mimics the design of organic skins. The system works using two glass panels that are sandwiched together called ‘muscles’. Inside the sandwich is a flexible engineered ribbon made of polymer materials that can be polarised. These muscles contract or expand according to pressure differences.
This façade controls the flow of light, matter and temperature between the inside and outside. The technology can then be adjusted, making it similar to an air conditioning unit. Imagine a curtain, AC unit and a window all in one system without electricity.
Homeostatic Building Facade (internationalfacade.com)
Material transformations: Martina Decker at TEDxNJIT – YouTube

## Slide 11: Evolving materials: liquid roof
        A liquid roof coating is a single piece roof membrane with elastic properties. When applied it becomes the top layer of the roof system. Liquid roofs have existed since the early 1800s, when natural bitumen was combined with jute, straw, rag felt and other man-made materials.
        Modern liquid roofs:
        Are applied cold by roller or brush
        Are high performance, rapid curing
        Can be applied to flat or pitched roofs, made of asbestos, felt, asphalt, concrete, metal, bitumen, wood or metal
        Can be applied onto wet or dry surfaces
        Can be used on building components such as tiles, down pipes, chimneys, roof lights, up stands and parapet walls
        Can provide anti-skid finish for designated walkways and balconies.

## Slide 12: Evolving materials: transparent aluminium
        Aluminum oxynitride (known commercially as ALON), is a transparent ceramic made of aluminum, oxygen and nitrogen. It is commonly referred to as transparent aluminium.
        Although this material is still very expensive, it has the potential to create large glass structures such as aquariums, windows and façades. It will not fracture like silica glass and can be used for harsh environmental conditions.
        Watch this video to find out more about this material:
                /

## Slide 13: Evolving materials: self-healing concrete
Concrete is a popular choice for large-scale structures, such as bridges, tunnels, roads and buildings, but is not without problems. Every year billions of pounds are spent maintaining, fixing and restoring concrete structures, damaged by vehicle vibration ground movement.
Cardiff University Research team Materials for Life (M4L) looked into the development of healing agents. Research is continuing under (RM4L) Resilient Materials for Life. Watch the video to find out about RM4L.
                Home - M4L (rm4l.com)

## Slide 14: Evolving materials: self-healing concrete
Watch the video to find out about RM4L.

## Slide 15
Any questions?