## Slide 1: PowerPoint 9: Off-site construction 2
PowerPoint presentation
Unit 106: Introduction to emerging technologies in construction and the built environment sector

## Slide 2
Types of off-site construction: sub-assemblies
Sub-assemblies are a combination of components that are manufactured off-site. They may form panelised or volumetric systems and require delivery, storage and skilled assembly as part of the construction programme.
I-joists
Steel elements
Roof systems
Floor systems
Stairs
Doors
Windows

## Slide 3
Types of off-site construction: components
Components are constituent parts of a building made as independent units. They are usually self-contained and sourced from one supplier.
The term is used for:
fasteners and fixings
metal, meshwork and seals
adhesives
vapour barriers
breather membranes
cladding
curtain walling panels.

## Slide 4
Types of off-site construction: panelised system
      Open system
      Made with structural elements only, non-insulated, occasionally one side is sheeted.
      Closed system
      Insulated, sheeting on both sides and a service zone.
      SIPs (Structural Insulated Panels)
      Variation of closed panels; solid insulation ‘sandwiched’ with two layers of oriented strand board (OSB) .

## Slide 5
Types of off-site construction: volumetric units
Volumetric units are three-dimensional units that enclose usable space.
Typically, they are fully finished internally and can also be finished externally.
They can also be non-structural – pods: used for bathrooms, plant rooms and roof-top services.

## Slide 6
Types of off-site construction: volumetric units
Panel assembly. Before the assembly of the volumetric unit, the panels are manufactured in a similar way to a closed panel factory.
Unit assembly. The panels are placed to form floor, walls and roof of the volumetric unit. At this stage, some additional operations are completed, such as the installation of insulation.
Windows and doors. The building envelope is completed with the installation of windows and doors.
MEP systems installation. MEP stands for mechanical, electrical and plumbing. These systems are installed by a skilled worker.

## Slide 7
                Source:
Types of off-site construction: volumetric units
Internal finishes. The volumetric units are completed internally with wall linings, such as plasterboard and tiles, and with flooring systems, such as parquet. In some cases, furniture and electric appliances are also installed.
External finishes. The volumetric elements may need to be completed with a breather membrane and then clad.

## Slide 8
These are combinations of more than one system, using a mixture of sub-assemblies, panelised and/or volumetric systems.
Types of off-site construction: hybrid systems

## Slide 9
Any questions?