## Slide 1: PowerPoint 5: Bricks and blocks
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Using bricks and blocks
Bricks and blocks can be used in many different ways.
Methods of setting out walls and the type of materials to be used will be stated in the specification.
For example, a cavity wall can consist of:
  face brick outer leaf and block (concrete or insulation) inner leaf
  block outer leaf and block inner leaf
  brick or block outer leaf and timber frame inner leaf.

## Slide 3: Types of brick
When used as a material for constructing walls, brick can broadly be split into two categories:
  Face brick
  Common brick
Face brick can become the external finish of the structure. There are a huge range of face bricks in many different colours and textures that can be used in a building design.
Common bricks can be manufactured from clay or concrete and are often out of sight behind render or cladding.

## Slide 4: Types of brick continued
Engineering brick is a dense brick manufactured from a particular type of clay. It has low water absorption levels, making it less prone to frost damage.
This type of brick is suitable for exposed positions in a structure and provides effective weathering features, such as projecting sills at door and window openings.
Engineering brick can also be used as a damp barrier in a wall. This type of brick is expensive so its use may be limited.

## Slide 5: Types of block
Blocks can be manufactured from a coarse material (aggregate) or fine insulating materials, such as pulverised fuel ash (PFA).
Coarse aggregate blocks are usually referred to as concrete blocks.
Dense concrete blocks can be used in situations where the bricks need to have greater strength, such as below the ground.
Lightweight concrete blocks can be used in situations where they do not have to carry high loadings.

## Slide 6: Types of block continued
Thermal insulation blocks are made from cement, lime, sand, PFA and water.
.
PFA is mixed with sand and water to form a slurry. This is then heated before being mixed with cement, lime and a small amount of aluminium sulphate powder.
The aluminium reacts with the lime to form bubbles of hydrogen. These tiny bubbles or ‘voids’ act as a barrier to reduce heat transfer.
Thermal insulation blocks are easy to handle and cut.

## Slide 7
Any questions?