## Slide 1: PowerPoint 20: Straight walls in stone
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Stone walls
Stone is a material that has been used in masonry construction activities for centuries.
There are many different methods of using stone in the construction of straight walls.
Bonding stones together to form a structurally stable and durable wall takes considerable skill and experience.
Some stone is carefully ‘dressed’ to produce specific sizes and even shapes. Other stone walls use natural materials that have simply been extracted from the ground.

## Slide 3: Stone walls continued
Stone walls with no set pattern are constructed with bonding arrangements that cannot be repeated.
These are often referred to as ‘random rubble’ stone walls.
A minimal amount of trimming and shaping is performed by the bricklayer or stone mason.
This type of wall requires vision and artistic skill to produce an attractive result. It is extremely time consuming and costly.

## Slide 4: Stone walls continued
Because the stone materials in a random rubble wall have no regular edges or shape, a string line can only be used as a guide.
Profiles can be set up at each end of the wall and a string line attached to them to act as a guide to lay the stone in a straight line.
A great deal of care and skill is needed to produce an attractive and accurate result.

## Slide 5: Stone walls continued
Stone walls with distinct patterns are constructed from stone that is dressed to specific sizes and proportions.
Often referred to as coursed stonework, each stone is sized to specific dimensions with straight edges that make laying it as part of a straight wall easier to achieve.
A string line can be used with this type of stone wall in a similar manner to a straight brick wall to produce an accurate result.

## Slide 6: Stone walls continued
Stone is a natural material that produces durable structures.
When constructed with care and skill, a stone wall can be an attractive product that adds character to a construction project.
Unlike bricks and blocks which are regular in shape and size, natural stone is irregular, heavy and challenging to use. But it offers great job satisfaction when a good result is achieved.

## Slide 7
Any questions?