## Slide 1: PowerPoint 4: Equipment for masonry work
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Spot board
Spot boards are essential pieces of equipment for carrying out masonry activities. They are made of sheet materials such as plywood.
Cement mortar is placed on a spot board to allow the bricklayer to prepare and shape it when producing a bed joint.
For convenience, the spot boards are placed between stacks of masonry materials and are often propped on blocks as a support.

## Slide 3: Wheelbarrow
Many work activities on site depend on the use of a wheelbarrow.
They are used to transport cement mortar to the work location and, with care, can be used to move bricks, blocks and stone into position.
While plastic barrows have the advantage of not rusting or corroding, they are usually not durable enough for use on construction sites.
A steel wheelbarrow is more rigid and therefore easier to manoeuvre, and if looked after, will last a long time.

## Slide 4: Buckets
A bucket is an essential piece of equipment on site and is used by the bricklayer to carry water for mixing. Some bricklayers use a bucket to carry essential tools to the work location.
If a suitable grade of plastic is used in manufacture, a plastic bucket can be very durable for use on site.
In the past, buckets were manufactured from steel that had a protective coating to resist rust and corrosion (known as galvanised steel). However, steel buckets are obviously heavier to use than plastic.

## Slide 5: Shovels
Shovels are used in masonry construction activities for mixing and moving mortar and for moving other loose materials.
They come in many shapes and sizes designed for different jobs. The top shovel shown here has a wide blade and can be used to lift large amounts of material from a level solid base.
The bottom shovel shown here has a tapered ‘nose’, which makes it more useful for digging directly into piles or heaps of materials.

## Slide 6: Straight edge
A straight edge is used to transfer levels over a distance greater than the length of a spirit level.
It needs to be manufactured from materials that are rigid and stable. The example above is made from a lightweight metal.
A straight edge made from timber would need to be frequently checked for accuracy as wood can warp and twist over time.

## Slide 7: Gauge rod
A gauge rod provides a reliable, easy-to-read reference to check the vertical spacing of brickwork or blockwork.
It can be made on-site from available timber and the measured gauge can be marked with saw cuts at the correct positions.
Using this, the work can be easily checked to ensure the specified gauge is met without the constant use of a tape measure.

## Slide 8: Site square
Most buildings are set out as square or rectangular structures. To set out simple building shapes with right angled corners, a site square can be used.
The square in the upper illustration is made of metal to ensure it remains suitably rigid and accurate. It can also be folded for convenience when carrying or storing it.
With care, a site square can be assembled on site using available timber.

## Slide 9: Gauge box
To ensure reliable consistency in the proportions of materials mixed to produce cement mortar, a gauge box can be used.
This consists of a metal or timber bottomless box, which is placed on a level base and filled with cement powder or sand.
The cement or sand must be flush with the top of the box to ensure consistency is achieved.
The box is then lifted away, and the process repeated according to the proportions of material required for the mortar mix.

## Slide 10: Profiles
Profiles provide a temporary means of indicating corners and wall positions when setting out a building.
They are assembled as required using timber pegs and boards. String lines can be attached to the profiles to mark out the line of excavations when creating foundations.
They can be left in position to show the bricklayer the line and position of masonry constructed below ground.

## Slide 11
Any questions?