## Slide 1: PowerPoint 12: Methods of preparing the work area –safety
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Managing risk
There are many potential hazards that can be encountered when preparing the work area for masonry construction activities.
It is essential to think about safety when planning and preparing for a work task.
Preparing a risk assessment supports safe working practices by identifying potential hazards and risks associated with an activity.
By thinking ahead and carefully considering any potential hazards that could occur, risks can be reduced or removed and can be monitored as work progresses.
Area/ activity | Hazard | Risk to (list persons) | Current precautions | Action | Action required by | Date for required action | Complete
Risk Assessment
Assessment carried out by: Date assessment was carried out: Date of next review:

## Slide 3: Managing risk continued
When preparing for work activities, moving materials into position may involve heavy machinery movements. This creates many potential hazards to workers close by.
A risk assessment will help in planning to minimise risks of this sort, by alerting workers to potential hazards and stating measures that can be taken to safeguard them from harm.

## Slide 4: Preparing safely
Once the masonry materials are moved to the work location, some manual handling will be necessary.
Lifting heavy and awkwardly shaped resources (such as stone) properly is essential in preparing the work area safely and avoiding injury.
  When lifting heavy items, be sure to have the correct:
  posture before lifting
  technique when lifting
  posture and technique when lowering the load.

## Slide 5: Preparing safely continued
When stacking materials at the work location, they must be arranged in a stable manner. Unstable stacks of heavy materials are a potential cause of injury.
Bricks and blocks can be stacked in neat layers since they are regular in shape.
Bricks can be stacked on edge and if brick tongs (or a clamp) are used, a row of six bricks at a time can be placed on the stack.
Blocks can be neatly stacked but are more stable if arranged flat as shown here.

## Slide 6: Preparing safely continued
Packs of bricks are delivered to site with steel or strong plastic bands holding the pack together.
Always use the correct tool to cut the bands and take care that the bands do not spring out and strike other workers nearby.
Show consideration for the safety of others by disposing of the bands appropriately after removal. They can create a trip hazard if left lying around.

## Slide 7: Preparing safely continued
There will be occasions when masonry materials are stacked along the edge of an excavation trench ready to build work below ground level.
Always make sure the ground supporting stacks of materials on the edge of a trench is firm and level.
It may be necessary to spend some time removing soft or loose material before starting the stacking out process.

## Slide 8: Preparing safely continued
Handle bricks and blocks carefully to avoid damage and injury to yourself.
If they are handled roughly, they can develop cracks in them that are not easy to see. If cracked, they may break into two or more heavy pieces, which can fall and injure an operative’s legs or feet, so care is needed.
Special care is needed handling dense concrete blocks. It can be very easy to trap your fingers between heavy blocks when stacking them one on top of the other.

## Slide 9
Any questions?