## Slide 1: PowerPoint 6: Stone
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Using stone in masonry tasks
Some stone is carefully ‘dressed’ to produce specific sizes and even shapes.
Other stone walls use natural materials that have simply been extracted from the ground and are used with little additional work.
Dressing stone is a skilled occupation requiring specialist tools and equipment.

## Slide 3: Using stone in masonry tasks continued
Some hand tools used by a stone mason are similar to those used by a bricklayer.
To create quoins and angled features in stone takes time and care.
Trimming natural stone requires an understanding of the make-up of the material. A good stone mason develops an ‘eye’ for the way layers in the stone are arranged.
These layers can be used to good advantage to cause the stone to break along lines that correspond to the desired shape or angle.

## Slide 4: Using stone in masonry tasks continued
Stone is a tough and durable material so in order to cut and shape stone requires tough tools.
Hand tools must be kept in good condition. Chisels must be sharp and not be allowed to develop ‘mushroom’ heads.
When the end of a steel chisel is repeatedly struck, it can become misshapen and potentially cause injury to the user.
For cutting larger stones to required sizes, some power tools can be used to improve productivity.

## Slide 5: Using stone in masonry tasks continued
Because natural stone is heavy and irregular in shape and size, it can be difficult to transport and handle manually.
When building a stone wall, enough space must be allowed in the work location to position the stone materials for safe and efficient working.
Bricklayers and stone masons may need to work together to safely move and lay stone materials when constructing a wall.

## Slide 6: Using stone in masonry tasks continued
Stone is a material that can produce a range of decorative effects by being used in different ways.
To produce buildings and other structures using stonework is more time-consuming than brickwork or blockwork.
It requires a range of skills and an artistic flair to produce an attractive and durable result.
Building in stone can be rewarding and satisfying.

## Slide 7
Any questions?