## Slide 1: PowerPoint 9: Methods of preparing mortar
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Mortar specification
Mortar is mixed according to specified ratios. The mortar mix ratio will be specified according to the masonry material being used.
The ratio of the mix should produce a mortar that is slightly less hard than the bricks or blocks being laid.
This allows for any slight movement caused by thermal expansion or by shrinkage in the masonry during setting and hardening.

## Slide 3: Mortar specification continued
Bricks and blocks vary in hardness and strength. For example, engineering bricks are extremely hard and are used in structures which have to carry high loadings and stresses, such as bridges.
The mortar mix ratio specified would be designed to produce a mix that’s a little weaker than the engineering brick but strong enough to resist the weight and forces placed upon it.
This means that the figure showing the proportion of sand in the mix ratio might be decreased, so that the proportion of cement would be greater.

## Slide 4: Ratios
A ratio of 1:5 would represent a mortar mix containing one part of cement to five parts of sand.
To make it stronger, we would reduce the amount of sand or increase the amount of cement.
Softer materials such as calcium silicate bricks (sometimes referred to as sand/lime bricks) or softer types of clay bricks, such as ‘flettons’, would require a weaker mortar mix ratio.

## Slide 5: Ratios continued
Blocks can also vary in hardness and strength.
A dense concrete block manufactured from coarse aggregate will require a harder mortar mix ratio than a lightweight thermal insulation block manufactured from pulverised fuel ash (PFA).
The mix ratio for thermal insulation blocks will be weaker to allow for thermal movement.
If the mortar mix ratio for thermal insulation blocks is too strong, cracking will occur at window and door openings and at junction walls.

## Slide 6: Gauging mortar
To make sure that the mortar mix is consistent, the amounts of materials used are ‘gauged’. Accurate proportions are unlikely to be achieved if the material is measured by ‘shovelfuls’.
Different amounts will be loaded onto a shovel depending on the strength of the operative.
Wet or damp materials will be heavier than dry materials and will stick together on the shovel, which means that the amount added to a mix will vary.

## Slide 7: Gauging mortar continued
To make sure that consistent proportions of sand and cement are added to a mortar mix, a gauging box can be used.
This piece of equipment is a bottomless box made of timber or metal which is filled with material until flush with the top.
A mortar mix ratio of 1:3 (one part cement to three parts sand) would need one box of cement to three boxes of sand. The accurately measured amounts are then mixed together.

## Slide 8: Gauging mortar continued
When producing mortar, the specified mix ratio must be adhered to in order to achieve:
  adequate strength – but slightly softer than the masonry materials
  durability – resistance to chemical attack and frost damage
  strong bonding with masonry components – sticking the components firmly together
  a sealed surface on the mortar joints to protect against wind-driven rain.

## Slide 9
Any questions?