## Slide 1: PowerPoint 16: Linear measurement
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Linear measurement
The term ‘linear’ measurement refers to measurement of length. This can be a length measurement between two points along a line.
When using construction drawings, the length and width of a building will be shown as a linear measurement.
These are horizontal measurements. Measurement of the height of a building can also be described as a (vertical) linear measurement.
Length
Width

## Slide 3: Linear measurement continued
If the length and width for all sides of a rectangular building are added together, then we find the linear measurement of the perimeter.
Establishing length or width measurements and multiplying them by height measurements allows us to calculate quantities of masonry materials for the work task.
Linear measurement also allow us to establish the positions of features in a building.
Length
Width
Width
Length

## Slide 4: Linear measurement continued
The linear measurements in this drawing show the length of the building and also show the position and length of a projecting section of the design.
The measurement from end-to-end of the building is referred to as the overall dimension and the other measurements, which added together are equal to the overall dimension, are referred to as ‘running’ or cumulative dimensions.
To complete the information this drawing can provide, the width dimensions would be added.

## Slide 5: Linear measurement continued
Understanding how these dimensions work together allows us to check measurements and identify errors in a drawing.
This drawing has a dimension missing. However, with the information that can be extracted from the linear measurements given, the missing dimension can be established.

## Slide 6: Linear measurement continued
A working drawing such as this floor plan provides a great deal of information about the dimensions for this building.
It shows window and door positions, internal wall positions, corner positions and an indication of where services enter or leave the building.
Notice the use of overall and cumulative dimensions in a number of places.
Can you spot any missing dimensions?
5000
5000
765 2664
4910
4000
650 2800 650
4350
4750 5000
9750
6220
1245 913 1387 2000 675
Dining / Lounge
External Walls:
100mm Brickwork 50mm Cavity
9mm Plywood with vapour barrier
140mm Framing (140mm × 47mm studs @600 ctrs with 150mm Glass fibre Insulation to achieve min U-valve: 0.35w/m K
12.5mm Foil backed Plasterboard and skinn
Stair construction:
Total 13 Risers Riser: 204mm Going: 225mm
Hand rail height: 850mm
Landing Gaurding height: 900mm
Kitchen
Garage
W.C.
2548
1912
B
2 layers 12.5mm plasterboard
fire protection
All new timber walls
to have sound resistance of min. 40dB. formed from 15mm plaster- board (to achieve 9.8kg/m2) both sides on 89×39 sw studs at 400 ctrs, with sole plate, head and cross noggings. Sound insulation quilt (min. density 10kg/m3) filled between studs.
Entrance Doors
to have a minium clear opening width of 775mm

## Slide 7
Any questions?