## Slide 1: PowerPoint 13: Planning the sequence of work (1)
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Timescale
The progress of work on a construction site is planned to occur within set timescales.
A programme of work is the key to a successful and efficiently run contract and will help the site manager and supervisors follow a set sequence of operations.
The most common way of creating a programme of construction activities is to use a bar chart.
This planning and monitoring tool is often known as a Gantt chart.
Time (days) |  |  |  |  |  |  | 
Task | 1 | 2 | 3 | 4 | 5 | 6 | 7
Prepare the ground |  |  |  |  |  |  | 
Spread foundations |  |  |  |  |  |  | 
Lay cables for services |  |  |  |  |  |  | 
Build walls up to DPC |  |  |  |  |  |  | 
Proposed time in green |  |  |  |  |  |  | 

## Slide 3: Drawings
One of the main methods of communicating information for any building activity is by means of drawings. They provide a great deal of information without having to use lots of writing.
The architect spends a lot of time understanding the requirements of the client and translating these ideas and requirements into working drawings.
The bricklayer needs to understand how to interpret these drawings and make the structure a reality.

## Slide 4: Drawings continued
Drawings are produced in a number of different ways to give a complete understanding of the work task.
Each type of drawing is produced to a different scale, to give a view that is closer or further away.
This is a block plan which gives a broad view, allowing us to see the position of a building in relation to others.
A block plan is drawn to a scale of 1:2500 or 1:1250.
12
13
3
1
4
Albert Road
Sutton Road
George Road
A block plan

## Slide 5: Drawings continued
This is a site plan, sometimes known as a location drawing.
It shows the position of the proposed building and the general layout of things like roads and boundaries on the site.
A site plan is drawn to a scale of 1:500 or 1:200.
Once we have an overview of how the position of the building relates to the surroundings, we need to look more closely at the specific location.

## Slide 6: Drawings continued
This view provides information on how components such as door and window frames are positioned in the structure and a view of the roof design.
It also gives an indication of the number of storeys or floor levels.
Elevations are drawn to a scale of 1:50, 1:100 or 1:200.
An elevation drawing shows the general layout of the building from the front and sides. If necessary, an elevation of the rear may be included.

## Slide 7: Drawings continued
A floor plan shows the external dimensions of the structure and the dimensions for the positioning of internal walls.
This is vital information for the bricklayer, as it clearly shows the position of doors, windows and openings for services.
A floor plan is drawn to a scale of 1:50 or 1:100.
.
Specific details about the layout of a building, including dimensions, are provided by the floor plan.
5000
5000
765 2664
4910
4000
650 2800 650
4350
4750 5000
9750
6220
1245 913 1387 2000 675
Dining / Lounge
External Walls:
100mm Brickwork 50mm Cavity
9mm Plywood with vapour barrier
140mm Framing (140mm × 47mm studs @600 ctrs with 150mm Glass fibre Insulation to achieve min U-valve: 0.35w/m K
12.5mm Foil backed Plasterboard and skinn
Stair construction:
Total 13 Risers Riser: 204mm Going: 225mm
Hand rail height: 850mm
Landing Gaurding height: 900mm
Kitchen
Garage
W.C.
2548
1912
B
2 layers 12.5mm plasterboard
fire protection
All new timber walls
to have sound resistance of min. 40dB. formed from 15mm plaster- board (to achieve 9.8kg/m2) both sides on 89×39 sw studs at 400 ctrs, with sole plate, head and cross noggings. Sound insulation quilt (min. density 10kg/m3) filled between studs.
Entrance Doors
to have a minium clear opening width of 775mm

## Slide 8: Drawings continued
An additional source of useful information for the bricklayer is provided by sectional drawings.
This is like a slice through the structure which shows details that would otherwise be hidden. A section is drawn to a scale of 1:50 or 1:100.
Elevation ‘B
’
Section ‘X–X’

## Slide 9: Specification
The specification is a contract document. This means it is legally binding.
It is used in conjunction with the drawings. Giving written instructions in a separate document avoids potential confusion.
The example shown here includes a lot of information about the bricks to be used for a project, including:
  type
  appearance
  water absorption, and much more.

## Slide 10: Schedule
A schedule is mainly used on sites where there are a number of building designs, with each type having different components and fittings.
A schedule is usually used in conjunction with drawings.
A typical drawing will have doors and windows labelled D1, D2, W1, W2, and so on.
These labelled components are then listed in the schedule along with other information.

## Slide 11
Any questions?