## Slide 1: PowerPoint 15: Calculating quantities – area
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Quantities and area
Many construction workers shy away from carrying out calculations of quantities, perhaps thinking that it is too complex for them to deal with.
Failing to calculate the correct amount of materials needed for a task could lead to running out of materials before the task is finished.
Calculating quantities of bricks and blocks accurately is important as mistakes can lead to unnecessary expense and inefficiency.
On a personal level, if you cannot calculate the quantity of work completed, you will not be able to be paid accurately.

## Slide 3: Quantities and area continued
Following some simple steps makes calculation tasks easier.
To calculate the number of bricks needed for the wall, first we need to work out the area of the face.
To do this we simply multiply the length by the height.
To make it easier, first convert the measurements from millimetres to metres.

## Slide 4: Quantities and area continued
To convert millimetres to metres, simply move the decimal point three places to the left.
Take the measurement for length first, which is 1790mm.
1790mm becomes ...
1790.00
179.000
17.9000
1.79m
Decimal point moved three places to the left

## Slide 5: Quantities and area continued
When we do the same for both dimensions of the wall we have:
Length 1.79m
Height 0.975m
To establish the area of the face of the wall, simply multiply 1.79×0.975 which equals: 1.745m² (or square metres). We could round this figure up to 1.75 to make things even simpler.
For a half-brick thick wall there are 60 bricks to a square metre (m²), so if we multiply 1.75×60 we get 105 bricks as our calculated quantity.

## Slide 6: Quantities and area continued
To calculate the number of blocks needed for a wall, we follow the same process and multiply the area of the wall face by 10, since there are 10 blocks to a m².
Using already calculated area of 1.75m², we can calculate that we need 17.5 blocks.
In reality, you should round this figure up to 18 and add an additional amount to allow for waste.
Calculating allowances for waste will be discussed in another session.

## Slide 7: Quantities and area continued
When openings occur in walls, we need to calculate the area of the opening in the same way as already described and then subtract it from the overall area of the wall.
In the case of a smaller opening, it may be more efficient to ignore the opening and treat the wall as a solid without an opening.
This is because an allowance would need to be made for waste created by cutting bricks and blocks to maintain the bond either side of the opening.

## Slide 8: Quantities and area continued
Keep in mind that when calculating quantities for a wall that includes a return, there will be an overlap between the face section of wall and the return section of wall.
This is represented by the red section in the illustration.
If a building design had many external and internal corners, (or if the walls are one brick thick) it is useful to take this into consideration to avoid unnecessary waste.

## Slide 9
Any questions?