## Slide 1: PowerPoint 21: Quoins and stopped ends
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Quoins
A quoin is the name used for a corner in masonry.
Skill and care are needed to build quoins, since they are used to guide the construction of straight sections of wall.
When the quoins at each end of a wall are completed, a string line is attached and the infill between corners can be completed.
Accurate alignment and levelling of the quoins is therefore vital so that the wall is straight from end-to-end.

## Slide 3: Quoins continued
The method of building a quoin involves stepping each course back from the one below as the work progresses.
This process is referred to as ‘racking back’.
As each course is laid it must be accurately gauged. Standard gauge of a brick and a bed joint is 75mm.
To make checking the gauge for accuracy and consistency easier, a gauge rod can be made with the course spacing marked on it with saw cuts.
Racking back

## Slide 4: Quoins continued
To build a quoin in brick, follow these steps:
Lay bricks for the first course along the predetermined line of the wall.
Level these bricks from end-to-end. Tap the bricks – NOT the level – to align them.
Use the spirit level as a straight edge on the face of the bricks to ensure they are straight. Remember, tap the bricks and NOT the level to align them.
Take the time to get this first stage right. Remove bricks to adjust the size of the bed joint if necessary.
Note: The chosen height of the quoin will determine the number of bricks to lay in the first course. Don’t extend the first course longer than the length of your spirit level.

## Slide 5: Quoins continued
The bricks laid at a right angle to form the corner are called a ‘return’.
Make sure the return bricks are ‘square’ to the face line of the wall. (A steel square like this one shown here is helpful).
Level from the corner point to the end of the return. Do not make any adjustments to the corner position – only adjust the end of the return.
Use the spirit level as a straight edge to align the face of the return bricks along their length.
Check the work for accuracy often.

## Slide 6: Quoins continued
The quoin is raised a course at a time, repeating the same steps for each course.
Plumbing must be checked at each end of the course as it’s laid.
Each course must also be checked for gauge to maintain consistent and accurate bed joints.
As the work proceeds, the corner point must be kept plumb on the face and the return.

## Slide 7: Quoins continued
As each course in the quoin is laid, the spirit level should be presented to the work as shown here.
This process is called ‘ranging’.
It ensures that when the string line is attached from the end-to-end of the wall to build the infill, the courses of the quoin will ‘flow’ into the rest of the wall.
Care and accuracy in building quoins will result in a good overall appearance in the wall.

## Slide 8: Stopped ends
A stopped end is a plumb end section of wall with no return masonry.
The principles and steps used to construct a quoin also apply to constructing a stopped end, but without the return masonry.
The accuracy with which the stopped end is constructed will directly affect the accuracy of the finished wall.
When plumbing a stopped end, only the face and end of the work can be plumbed – not the back.

## Slide 9: Block quoins and stopped ends
Quoins and stopped ends in blockwork are constructed using similar principles and steps to those used in brickwork.
Because the components are larger and often heavier than bricks, more care is needed when positioning them to avoid injury.
Aligning them accurately will take greater effort and control.
Notice that to maintain half bond in a quoin, a cut block is added next to the header block forming the return.

## Slide 10
Any questions?