## Slide 1: PowerPoint 19: Straight walls in brick and block
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Stretcher bond
The most common bond is ‘stretcher bond’. The name refers to the long face of the brick, which is called the ‘stretcher’ face.
In stretcher bond, the bricks in each course are arranged with an overlap the width of a brick (102.5mm).
This means that the perp joints in any course are exactly halfway along the face of the stretchers in the course below, so stretcher bond is often called half-bond.
65mm
215mm
102.5mm
Header face
Frog
Arris
Stretcher face
Stretcher bond
Half brick overlay

## Slide 3: Stretcher bond continued
Because the bricks in stretcher bond overlap by half a brick length, it’s necessary to cut half bricks to establish the correct bond.
Cutting bricks is an operation that can only be mastered with experience, so be prepared to have disappointments at first.
The primary tools for cutting by hand are a club (or lump) hammer and a brick bolster.
The aim is to produce clean sharp edges, especially on the face side of the cut brick. This will ensure a good appearance in the finished wall.
Cut half brick

## Slide 4: Stretcher bond continued
It’s good practice to set out a wall dry before laying the bricks in mortar, especially if the wall must be built to specific linear measurements.
Setting out the first course dry means we can check whether the joint sizes will be suitable and either tighten or open the perp joints so that the wall will fit within the specified dimensions.
By varying the size of the perp joints, slight size differences in bricks can be accommodated.

## Slide 5: Half bond in blocks
Blocks are also usually half bonded to create a wall with strength and stability.
Similar principles to brickwork apply when setting out the bond for blockwork.
A half block must be cut to ensure the correct overlap between courses is created from the end of the wall or corner.
A lump (or club) hammer and bolster are used to cut blocks accurately by hand with similar techniques to those used for cutting bricks.

## Slide 6
Any questions?