## Slide 1: PowerPoint 8: Stacking and storing materials
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Protection
Resources for masonry construction activities are valuable and need to be protected from weather, damage and theft.
With many resources, manufacturers will provide weather protection by using measures such as wrapping in polythene.
These protection measures should be preserved and maintained when materials are delivered to site and placed in storage.

## Slide 3: Protection continued
All site workers should take careful note of the protection measures used for storing materials.
If protective coverings on delivered materials are damaged, replacement protection should be provided.
It is helpful to be familiar with available resources on site that can be used to protect materials, especially if bad weather is forecast.
Taking the time to maintain weather protection can assist in meeting deadlines and maintaining productivity.

## Slide 4: Protection continued
Storing materials in a planned and orderly way will protect them from accidental damage.
The blocks shown here are stored in neat stacks on pallets so that they can easily be moved by machine to the work location. This minimises the risk of damage and reduces potential losses.
Keeping a construction site tidy and orderly protects the materials and maintains safety for workers.

## Slide 5: Efficiency
As well as protecting materials, carefully planning storage aids efficiency as a work task can be interrupted if it is discovered that resources for the job have been damaged through poor storage.
Correct storage is not difficult. For example, rolls of damp proof course should be stacked on their side, as shown here, to avoid distortion and possible cracking.
Bags of cement should be neatly stacked, and the batch used up before placing new stock on top of the stack.

## Slide 6: Efficiency continued
Heavy items should be stored and handled carefully to protect them and to make sure that work proceeds efficiently.
These heavy concrete blocks have been transported from storage by machine.
The steel straps holding the pack together have been left in place until the materials are to be used, to avoid blocks falling and breaking.
Masonry cement
These steel lintels have been moved to the work location using the same efficient method.

## Slide 7: Security
To maintain cost efficiency, it is important to protect resources on site by storing them securely. Lockable containers are often used to store high value items.
Other materials and resources are stored securely in a fenced compound. This will be positioned to allow easy access for delivery vehicles.
The storage compound will be arranged so that access by the machinery used to take resources to the work location is easy and efficient.

## Slide 8: Security continued
A construction site will often be protected and secured by hoardings around the working area.
Delivery vehicle entry and exit can be monitored and controlled to ensure nothing is brought on site or taken off site without authorisation.
There are often separate entry points for workers and staff to enter on foot.
This prevents unauthorised access and gives protection against possible theft of valuable resources.

## Slide 9
Any questions?