## Slide 1: PowerPoint 10: Methods of mixing mortar
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Mixing by hand
Mixing mortar by hand is hard work, but by following a simple sequence and working on a clean solid base, it can be made a little easier.
A common rule when mixing by hand is ‘three times dry – three times wet’.
This means that the dry materials are moved from their placed position to the side and then back again three times over in order to mix the sand and cement thoroughly before adding water.

## Slide 3: Mixing by hand continued
Once the dry materials are well mixed and positioned in a tidy mound, a large circular dip is formed in the centre and water is added carefully.
The water is gradually mixed in, until it is uniformly spread through the materials. It can then be turned three times ‘wet’, in a similar manner to the dry mixing and more water slowly added as required.
If a plasticiser is used, this should be added to the water and not to the dry materials.

## Slide 4: Mixing by hand continued
When mixing by hand, don’t use a shovel that is too big or difficult to handle. It is more efficient and much easier to use a smaller shovel with a tapered ‘nose’.
As water is added to the dry materials, they will get heavier, and using a shovel that is suited to the job and the operative’s capabilities will make mixing quicker and more efficient.
Producing mortar mixes by hand that are consistent between batches is a task that requires skill and experience.

## Slide 5: Mixing by machine
Mixing on site is usually completed using a drum mixer. This can be powered by electricity, a diesel engine or a petrol engine.
A drum mixer of any size is a powerful piece of machinery and must be treated with respect.
When mixing mortar with a drum mixer, always add an amount of water first, the cement second and the sand third.
If the cement is added after the sand, it can form into small balls, which prevent thorough mixing and can effect the final strength of the mortar.

## Slide 6: Mixing by machine continued
Mixing mortar on site by machine can be done using a silo mixer.
This piece of machinery contains mortar materials in dry storage in large silos which are brought to site pre-filled and ready for mixing operations.
A water supply is connected to the machine, which then mixes the mortar internally to the required consistency and workability.
The machine can be operated by semi-skilled workers to produce the exact amount to complete the work task with the minimum of waste.

## Slide 7: Mixing by machine continued
Mortar can be mixed by machine in factory conditions for delivery to the construction site.
Mortar mixed off site will usually be mixed by weight batching and not by volume. This is a very accurate method of making sure that the correct proportions are used.
The mixed mortar delivered to site may include a ‘retarder’, which is an additive that slows down the speed at which cement sets by up to 48 hours or more.
Pre-mixed mortar delivered to site

## Slide 8
Any questions?