## Slide 1: PowerPoint 3: Tools for masonry work
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Trowels
To build a wall in brick, block or stone we use a laying trowel to produce a mortar bed joint and perp joints. There are different shapes and sizes of trowel available.
This is the bricklayer’s main tool and is used consistently throughout a working day.
A pointing trowel is a smaller tool used to produce a joint finish in masonry and can also be used to smooth mortar applied to surfaces such as the top of a pier or pillar.

## Slide 3: Levels
Spirit levels are used frequently during masonry construction operations to check that the work is level and plumb.
Spirit levels are available in a range of lengths and sizes for various applications.
The smaller level shown here could be used to level individual bricks in a brick-on- edge coping for example.

## Slide 4: Hammers
Hammers used by a bricklayer are designed for tough cutting work.
These tools are specifically designed to cut and trim bricks and blocks to the required length and shape.
The hammer shown here with a bladed end is called a brick hammer and the hammer with a bulkier head is called a club (or lump) hammer.
Brick hammer
Club (or lump) hammer

## Slide 5: Hammers continued
This hammer is a specialist tool used by bricklayers to trim and shape masonry materials very accurately.
When creating angles or even curves, fine adjustments can be made with this tool which is known as a scutch hammer.
A separate part of the hammer known as a comb can be replaced when it becomes worn.
Scutch hammer
A comb

## Slide 6: Bolster chisel
There are many different chisels and cutting tools that are used in combination with a club (or lump) hammer.
This is a bolster chisel which is used to accurately cut bricks and blocks to specific dimensions.
Caution – using a different hammer with a bolster chisel, such as a brick hammer, risks causing injury to your hand – it is very easy to miss the chisel because of the smaller hammer head.

## Slide 7: String line
One of the most important tools used in masonry construction work is a relatively simple one.
To build a straight wall longer than the length of a spirit level, a string line is an essential piece of equipment.
The line is wound onto pins that can be driven into hardened mortar joints. The line and pins are often used with corner blocks which can be attached to brick or block corners.

## Slide 8: Jointer
A jointer is used to produce a finish to the bed and perp joints. This tool produces a half-round profile to the mortar joint.
The process is sometimes referred to as ‘ironing the joint’ and ensures that the joint finish is durable.

## Slide 9: Tape measure
A tape measure is essential to maintaining accuracy and ensuring your work conforms to drawings and the specification.
Tape measures are available in many lengths. The 10m tape shown here is convenient for use in most masonry construction activities.

## Slide 10: Looking after tools
Looking after your tools will mean they are always fit for purpose and that you can always produce the best quality work possible.
Keep them clean, keep chisels sharp, treat more fragile tools such as spirit levels with care, and they will serve you well for a long time.

## Slide 11
Any questions?