## Slide 1: PowerPoint 22: Wall ties in cavity walls
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Cavity walls
A cavity wall consists of two leaves or skins of masonry that on their own are relatively weak.
When properly tied together with suitable wall ties, the stiffness and load-bearing capacity of the combined skins can be almost equal to a similar solid wall.
Installing an adequate number of correctly positioned and installed wall ties is the bricklayer’s responsibility.

## Slide 3: Wall ties
In the past, ties were manufactured from galvanised steel (which means they were coated in zinc as a protection).
Over time the protective coating weakened which led to failure of the ties.
This resulted in serious damage to many structures with cavity walls.
Wall ties are now manufactured from stainless steel, which is much more durable.

## Slide 4: Wall ties continued
For wall ties to function properly in tying the two leaves of a cavity wall together, they must be positioned correctly in the bed joints.
The illustration shows the maximum spacing required by building regulations for a wall with a cavity less than 75 mm.
For a cavity wall with a wider cavity (e.g. 100mm) the horizontal tie spacing should be closer together.
Maximum 150mm
Maximum 225mm
Maximum 900mm
Maximum 450mm

## Slide 5: Wall ties continued
A major function of a cavity wall is to prevent moisture entering a structure.
Wall ties are designed with a feature referred to as a ‘drip’, which prevents water from tracking across them from the outer leaf to the inner leaf.
The drip on a wall tie must be positioned in the centre of the cavity to work properly.
Care must be taken not to allow mortar droppings to build up on wall ties, which could prevent the drip from working.

## Slide 6: Wall ties continued
The ends of the wall ties must be inserted a minimum of 50mm into the bed joint.
When installing wall ties, never push them sideways into a bed joint as an afterthought.
Remember to install them in the correct positions by pressing them into the newly laid mortar bed joint from above, before laying the brick or block on top of them.

## Slide 7
Any questions?