## Slide 1: PowerPoint 17: Waste percentages
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Calculating waste percentages
It’s difficult to avoid generating waste during masonry construction operations.
During transport of materials, items can be damaged and made unsuitable for use.
When cutting masonry materials, an amount of waste is created because the section of brick or block remaining after cutting operations may be unusable.
This means that when calculating quantities of materials for a work task, a percentage must be added for waste.

## Slide 3: Calculating waste percentages continued
The percentage figure used to calculate allowances for waste may vary depending on a number of factors.
For example, the specified bricks may be soft and prone to damage or they may be brittle and prone to shattering. The percentage figure would need to account for the potential waste anticipated due to the materials used.
Or the project design may include masonry features that require a large number of cut bricks to be produced.
This would increase the amount of waste produced by cutting operations.

## Slide 4: Calculating waste percentages continued
As a rule of thumb a commonly applied percentage figure for calculating waste when using masonry materials is 5%.
To calculate the required number of bricks or blocks, the area of the face of the wall must first be established in m² (or square metres).
Then to calculate the number of bricks required, multiply the m² figure by 60 for bricks and 10 for blocks.
The percentage decided on for waste is added to the calculated number of bricks or blocks.

## Slide 5
Any questions?