## Slide 1: PowerPoint 24: Working to standards
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Quality of finish
When masonry work is constructed to a high standard of finish, it contributes to the creation of an attractive environment in which to live and work.
Maintaining high standards in your work can give a great deal of job satisfaction.
A quality finish will also produce a structure that is durable and will be seen for many years to come.

## Slide 3: Quality of finish continued
Producing work to high standards starts with getting the basics right.
To speed up the job, some bricklayers have the bad habit of ‘tipping and tailing’ their perp joints as shown in the illustration.
This means that instead of completely filling the joint, a small amount of mortar is placed on the front and back edges of the header face, which leaves a void in the finished joint.

## Slide 4: Quality of finish continued
Working to develop good habits and work practices leads to the production of work that looks attractive and is durable.
Skilled workers capable of producing work to high standards are valued by employers.
It’s important to take the time to check your work carefully.
When producing joint finishes, develop the skills needed to choose the right time to perform the jointing operation. Avoiding mortar smudges and producing clean well-defined joints takes practice.

## Slide 5: Quality of finish continued
Some work tasks present a greater challenge, such as pointing masonry with a coloured mortar.
Choosing the right tools for the job will make the task easier. However, constant practice and being diligent is the only way to improve techniques and skills.
A great deal can be learned by simply observing those who are more skilled and have had time to develop their abilities.
Analyse the quality of your work carefully each time you complete a job.

## Slide 6: Quality of finish continued
The bed and perp joints need to be tooled or ironed in order to satisfy two requirements.
  To produce the desired appearance as specified.
  To weatherproof the joint in order to prevent the entry of moisture.
  It is good practice in brickwork to joint all the perps first, followed by the bed joints.
  This reduces the number of small projections where the perp joint and the bed joint intersect.

## Slide 7: Quality of finish continued
Not maintaining high standards by completing the work properly can result in gaps and voids being left, which will make the masonry vulnerable to the effects of poor weather.
When moisture enters the poorly finished bed joint, it may stay there for some time and may freeze during cold weather.
Since water expands as it freezes, it can potentially destroy the mortar joint and further deterioration will take place over time.

## Slide 8: Working to tolerances
Working to standards involves working within given tolerances.
A tolerance is an allowable variation between the specified measurement and the actual measurement.
It’s usually expressed as a plus or minus figure, for example ±4mm as shown in the illustration. If the wall is out of plumb beyond the tolerance it is not acceptable.
Tolerances are set within British Standards. As an example, a wall built 5m high should not be more than 8mm out of plumb in either direction.

## Slide 9: Working to tolerances continued
Tolerances apply to many aspects of masonry construction including level, face plane, brick and block sizes, and more.
Producing work as accurately as possible will mean the finished structure will be stable and fit for purpose. Work hard to keep your work well within given tolerances.

## Slide 10
Any questions?