## Slide 1: PowerPoint 2: Building accurately
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Accurate trowel work
Rolling mortar on the spot board is the traditional way of preparing the material to lay a bed joint.
Keep in mind that the rolling action takes a great deal of practice to master.
Eventually, a suitable roll can be formed which can be placed accurately on the wall with a swift action that controls the flow of mortar into the desired position.

## Slide 3: Using a spirit level – levelling
Keep in mind that the spirit level is a precision instrument. Never strike the spirit level to align the bricks horizontally.
Place the spirit level on the course of bricks to be levelled (as shown in the illustration) and gently tap the bricks.
If excessive adjustments are needed, it could be that bricks in the course will have to be removed and the thickness of the bed joint adjusted.

## Slide 4: Using a spirit level – plumbing
Rest the spirit level against the corner edge of the bricks.
To keep the spirit level stable, place your foot against the bottom of the level while holding the top of the level with your free hand.
Carefully adjust the bricks at either end of a course and look down the face of the wall to make sure it lines up with the spirit level.

## Slide 5: Using a spirit level – plumbing continued
Plumb the return edge of the work in the same way as the face.
It may be necessary to tap some bricks in or pull some forward to meet the spirit level in order to achieve accuracy.
Remember – never strike the spirit level to plumb the masonry.
Always tap the bricks to line them up vertically.

## Slide 6: Using a spirit level – lining
Lining the face of bricks between the plumbed ends of each course will help to produce a wall that has an accurate face plane.
Rest the edge of the spirit level against the face of the bricks in each course and adjust them as needed.
This will align the bricks in the face of a wall to give a uniform flat appearance.
Do not refer to any of the bubbles in the level.
Simply use the level as a straight edge.

## Slide 7: Using a spirit level – ranging
The final check to be made with the spirit level is to range the work.
This means holding the spirit level as shown in the illustration to check that the end of each course is in line.
The spirit level is simply used as a straight edge for the bricks or blocks to be adjusted to align with.

## Slide 8: Using a spirit level – blockwork
The same principles apply to levelling, plumbing and lining blockwork as already described for brickwork.
When we are satisfied that our quoins are completed accurately, we can use them as a guide to ‘run in’ the masonry between the corners.

## Slide 9: Laying to the line
Laying to the line is another aspect of bricklaying that requires time and practice in order to develop speed and accuracy.
Never lay the bricks touching the line. Doing this will cause the line to move away from the face of the wall and will result in a curved face plane.
‘Eye’ down the wall to ensure the face plane is smooth and the perps are lined up vertically.

## Slide 10: Lining in stone work
Laying stonework to the line requires a different approach to maintain accuracy.
Because some stone will not be uniform and consistent in shape, a string line cannot be directly attached to quoins or corners.
The illustration shows how timber profiles can be used to attach a string line as a guide to build a straight wall.

## Slide 11: Accuracy in gauging mortar
Providing accurate amounts of materials for mixing mortar is known as ‘gauging’.
Measuring materials by the ‘shovelful’ will not produce a reliably consistent mix.
A gauging box is a bottomless steel or timber square or rectangular box which is placed on a clean flat surface and filled with either sand or cement until flush with the top.
Consistent amounts can then be easily measured.

## Slide 12
Any questions?