## Slide 1: PowerPoint 7: Mortar materials
PowerPoint presentation
Unit 107: Working with brick, block and stone

## Slide 2: Sand
Sand for use in mortar comes from two main sources.
  It can be dug from pit deposits, appropriately known as ‘pit sand’. This type of sand produces a mortar that is easy to work.
  As pit sand deposits decline and planning permission for removing sand from pit locations becomes more difficult to obtain, sand is increasingly being extracted from the sea. This is often referred to as ‘dredged sand’.
Dredged sand processing plant

## Slide 3: Sand continued
All sand used for masonry must be well graded. This means that it must contain a uniform mix of fine, medium and coarse particles.
Mortar made from poorly graded sand will be weaker as there will be more tiny spaces that need to be filled.
These tiny spaces or voids can cause shrinkage as the mortar hardens, which can result in cracks forming.
Rain can then penetrate the wall which will cause deterioration over time.
Large grains: 35% (2.5–5 mm)
Medium grains: 40% (0.5–2.5 mm)
Small grains: 25% (less than 0.5 mm)

## Slide 4: Sand continued
Sand used for mortar must be washed and free of mud and silt.
A mortar mix containing excessive mud or silt will be weakened and over time this could lead to structural failure.
A specification may require a ‘silt test’.
In this test, the clean sand sinks to the bottom of the test vessel (tube) so that the amount of silt and mud or clay can be clearly seen.
Clay layer
Silt layer
Sand layers

## Slide 5: Cement
Cement powder is produced from limestone and is used in mortar as a ‘binder’.
It effectively fills the voids between the sand and makes sure that the finished mortar is hard and durable enough for the job.
A chemical reaction occurs between the cement powder and the water added to the mix. This is called ‘hydration’ and this reaction makes the mortar set hard.
A cement manufacturing plant

## Slide 6: Cement continued
There are many different types of cement that can be specified according to the requirements of the job.
  Ordinary Portland Cement (OPC) is the most commonly used cement. It is suitable for general masonry work and will produce a mortar of high quality and strength.
  Masonry cement is similar to OPC but contains a filler, so a mortar using this type of cement requires a higher proportion of cement powder to provide adequate strength.
  Rapid Hardening Portland Cement (RHPC) can be used where a shorter setting time is required.
Masonry cement

## Slide 7: Plasticiser
To make cement mortar more ‘workable’, a plasticiser must be added.
Modern plasticisers are chemical additives that are included in the mixing process as a liquid or a powder.
They should be used carefully in accordance with the manufacturer’s instructions.
Chemical plasticisers work by introducing tiny air bubbles to the mixture, which allow the particles of sand to move over each other more freely. This is called ‘air entrainment’.

## Slide 8: Lime
In the past, it was common practice to use hydrated lime as a plasticiser.
This increases the powder content of the mix, which forms a paste that lubricates the particles of sand.
Hydrated lime is still specified in certain instances, but it has more health and safety considerations (and can be more hazardous to health) than chemical plasticisers, which are easier to work with.
Mixing a mortar using hydrated lime can generate a lot of heat – enough to melt a plastic bucket.

## Slide 9: Water
Water is an essential constituent and without it, mortar would not harden or set.
The water used in producing mortar should be potable, which means that it is suitable to drink.
Using water of drinkable quality means that no chemicals will be present that could interfere with the hardening process or affect the mortar in undesirable ways.
If water from a stream or pond near a building site was used, it could affect the hardening process or discolour the mortar.

## Slide 10: Additives
There are other additives that can be used when mixing mortar that are used less frequently.
  Retarder is used to slow down the setting (or hydration) process to extend the time that the mix remains workable.
  Accelerator works in the opposite way, to increase the speed of setting. This could be useful where the work task involves interruptions to traffic flow or when working within tidal fluctuations.
  Frost protector is used to prevent freezing conditions from damaging mortar during the setting and hardening process.

## Slide 11
Any questions?