## Slide 1: PowerPoint 12: Second fix, finals and snagging activities
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Second fix activities
  Second fix is generally started once the building is dry and after all first fix carpentry, services, plastering and missed coats are finished, to avoid these activities damaging the finish.
  Second fixers generally use lighter tools and work to a finer finish than first fix carpenters, requiring tighter gap tolerances and minimal dents or breakout.
  Second fix joints are normally decorative rather than structural and therefore do not require structural jointing and are often just butted.
  Second fix activities include hanging doors and fitting ironmongery, cutting and fitting mouldings, fitting units and worktops, such as for kitchens, fitting service encasements, fitting cladding or panelling, fitting window boards and fitting staircase banisters and spindles.

## Slide 3: Second fix activities and specialisms: joinery
The main second fix activities for joiners or wood machinists are:
producing second fix components such as skirting boards or handrails, often with detailed mouldings
building bespoke interior doors and linings
producing bespoke units and worktops for kitchens and other items of furniture for other areas of the home, often fitting them
producing detailed panelling and cladding sometimes fitting them
turning items such as spindles and newel posts.

## Slide 4: Second fix activities and specialisms: carpentry
The main second fix activities for carpenters are:
fitting internal doors to linings, including door furniture and fixings
fitting kitchen and bathroom units and worktops
fitting handrails and balusters to stairs and landings
fitting mouldings and decorative features such as radiator covers, giving the building its finish
fitting cladding and panelling to existing walls
boxing in exposed services to a fine finish, often filling the boxes with insulation to reduce pipe noise.

## Slide 5: Service encasements
Services are the pipes and cables that carry electricity, water and gas around a building. These are often unsightly and require insulating.
Service encasements are normally made from battens and plywood and fixed with screws as shown.
They are then filled and painted and can have mouldings applied to make them less noticeable.
Screws

## Slide 6: Encasements
Service encasements can be for:
housing boilers (boiler cupboards)
pipework
cables
fuse boxes
underside of baths (bath panels)
around shower units
steel beams, steel and concrete piers.
Some service encasements are closed and some need to be accessible to allow maintenance. Closed encasements are often finished with fire-resistant plasterboard.
Framework for bath panel

## Slide 7: Kitchen units and worktops
Kitchen fitting is another specialism that falls into the second fix schedule, often completed by specialist kitchen fitters.
Setting out and using datum points is essential to ensure level worktops, wall and floor units.
New products are always emerging such as self-closing drawer runners and corner unit hardware, so up-to-date product knowledge is important.

## Slide 8: Kitchen units and worktops
A kitchen fitter should identify the following before beginning work:
the lowest point of the floor, which will determine where the widest section of kickboard will be
the square of all corners and whether the walls are level
the location of services, especially if chased into walls or under floor
the floor and wall units required, with their sizes, locations and handing
worktops and sink and hob positions
finishing trim such as cornice, pelmet and plinth.
location of white goods (e.g. washer, dryer, fridge and cooker).

## Slide 9: Kitchen units and worktops
Bespoke kitchen units are made for domestic and commercial use, however made-to-measure furniture of this type is expensive.
Most kitchen units are mass-produced by joinery manufacturers, constructed from melamine-faced chipboard (MFC) or melamine-faced medium-density fibreboard (MFMDF) and supplied as base, wall units and end panels.
They are made using a method known as ‘box’ or ‘slab’ construction and are supplied as either rigid units, that are glued and fully assembled during manufacture, or as flat-pack units where all components are supplied individually and are assembled on site using the supplied fittings.

## Slide 10: Wardrobes and other fitted units
Carpenters also design and build fitted units such as wardrobes and cupboards.
This requires multiple measurements prior to manufacture to ensure the unit fits and complements the height of the room’s mouldings, style and proportions.

## Slide 11: Banisters and balusters
Banisters are handrails positioned to protect people from long drops and steps. They aid people climbing and descending stairs.
Newel posts are the uprights that support the banisters.
Balusters or spindles are the smaller uprights that fill in the gaps between the newels. No gaps greater than 100mm can be allowed between spindles.

## Slide 12: Newels, banisters and balusters
Spindles are normally butted up to the grooves in the handrail and baserail and are either pinned and glued, or glued using bevelled fillets which fit within the grooves.
Banisters and spindles both require bevel cuts where they are used on staircases.
Banisters require morticing into the newels and dowelling to ensure strength. Baserails can be butted and fixed to the string.

## Slide 13: Cladding and panelling
Cladding and panelling refer to facing off a structure with a visibly pleasing or protective coating.
In this image, wainscoting is being applied to studwork. This is match-boarding which is fixed to timber grounds, in this case battens. The top end grain is normally hidden by capping and skirting is normally applied over the cladding.
If fitting cladding to a damp or external wall, a waterproof membrane can be applied to the grounds prior to cladding.
Skirting board
Secret-nailed boarding
Decorative capping
Plasterboard
Timber grounds

## Slide 14: Cladding and panelling
Panelling is defined by the framed sections created that fit together to create a pleasing design.
Normally the frames are raised as with this flat panel wainscoting or flush with the raised section of fielded panels
This panelling is called wainscoting as it comes up to dado height and is pictured with skirting and dado rail.
Wainscoting does not have to be panelled and can be clad in many ways.
/

## Slide 15: Hanging doors
One of the activities a carpenter or joiner will carry out is using a variety of hinges to hang doors or window casements, while maintaining an even gap and avoiding the door binding on the frame by positioning and cutting the hinges correctly.
If the door does not hang perfectly within the frame, the lock or latch may fail to operate, and the door will not shut.

## Slide 16: Hanging doors
External timber doors require a 3mm even gap all around the door due to the depth and expansion. This means a 3mm gap between the top of the door and the head of the frame and a 3mm gap between both stiles of the door and the frame.
A 3mm to 5mm gap is required between the bottom of the door and the threshold depending on type of door and cill, as this area receives more moisture.
With internal doors this clearance can be reduced to 2mm all round, including at least a 3mm clearance off any floor finish such as carpet, laminate flooring or tiles.

## Slide 17: Hanging doors
A door may require some removal of material by planing, sawing or routing, to ensure it is the correct shape and size.
If the door is to be fitted into a frame with a threshold and water bar, the bottom rail will need rebating prior to fitting and if it has a 9º cill it will need a bevelled cut.
You should never remove material from the head or top rail, it is better practice to square up the opening.

## Slide 18: Ironmongery
After a door has been hung, it will need a latch or lock fitted to secure it, along with door handles or doorknobs and other associated ironmongery.
On larger contracts, this information would be on the door and ironmongery schedule.
Fitting instructions are included with most items of ironmongery.
Furniture is often removed prior to painting to avoid it becoming marked or painted. Re-fitting the furniture is often called ‘final fix’.
Most problems when fitting locks, latches and door handles are caused by poor workmanship. This often comes up on a ‘snagging’ list.

## Slide 19: Ironmongery (sometimes fitted at final fix)
The positioning of door ironmongery will depend on factors including:
the construction method used in the manufacture of the doors.
the material from which the doors are made.
the specification and schedule.
the ironmongery fitting instructions.
customer preferences.
However, there are standard positions that are used for specific pieces of ironmongery.

## Slide 20: Snagging
Snagging is the final stage before the work is signed off.
Snagging refers to any faults found by the customer or supervisor which are added to a ‘snagging list’.
Sometimes there will be a dedicated snagger who will rectify any faults with the carpentry or furniture.
Common items that need snagging are doors and handles, windows and damaged units or worktops.

## Slide 21
Any questions?