## Slide 1: PowerPoint 10: Basic calculations, squaring off and basic geometry
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Metric and imperial
Metric measurements are decimal and therefore have a base of 10. Linear measurements can be listed in millimeters, centimeters, metres and kilometres represented as mm/cm/m or km, respectively.
Imperial measurements use various base numbers including 12, as in 12 inches to the foot, and 4 as with inches being divided into 1/4‘s, 1/8ths,16ths etc.
The majority of British architects, joiners and carpenters now use metric as their standard reference due to trade with other countries and its simplicity. For this reason, we will be referring to measurements in metric relating to sizes when planning and producing work.
Imperial measurements are still used in the industry.

## Slide 3: Metric and imperial
Imperial
12 inches = 1 foot
3 feet = 1 yard
22 yards = 1 chain
10 chains = 1 furlong
8 furlongs = 1 mile
Metric
1mm = 1000th metre
1cm = 100th metre
1m = 1000th kilometre
Conversions
1 inch = 25.4mm
1 foot = 304.8mm
1 yard = 914.4mm
1 mile = 1609.34m
Examples: 6” (inches) = 25.4 x 6 = 152.4 mm
4’ (foot) = 304.8 x 4 = 1219.2 mm

## Slide 4: Area and volume
To work out how much floorcovering to order you need to calculate the area of the space.
The area of a quadrilateral is calculated by multiplying one side by another and is represented by ² e.g: 400mm×300mm=0.4m×0.3m= 0.12m²
When ordering rough sawn timber in bulk it is common to order in volume called ‘cubes’, represented by ³. This is calculated by multiplying width by length by depth e.g 400mm×300mm×20mm = 0.4m×0.3×0.02=0.0024³ or 0.0024 metres cubed.
Check the decimal point is in the correct place before ordering.
AREA
VOLUME

## Slide 5: Applications of trigonometry
What are the main uses for basic geometry in wood occupations?
  Setting out studwork
  Squaring off joists
  Setting out roofs
  Working out lengths of rafters
  Setting out staircases
  Working out lengths of strings and handrails
  Squaring off frames and openings
  Setting out formwork and posts

## Slide 6: Pythagoras theory and the 3/4/5 ratio
On this particular triangle he noticed that the ratios of the sides were 3/4/5
This is useful when trying to find a 90º angle between side A and B, e.g. when setting out studwork.
First measure 3 units along side A and 4 units along side B. When the distance between the two points is 5 units the angle is square
Multiples of 3/4/5 can also be used as long as the ratio remains the same: e.g. 9/12/15
Pythagoras theory states:

## Slide 7: Pythagoras theory and the length of side C
Pythagoras theory states:
This theory applies to all right-angled triangles and can be used as a tool, to work out any missing side using the two given sides.
To find side C where A is 3, and B is 6 you should multiply both by themselves and add together them. Then find the square route of the result and you have: C= 6.7082
Notes: Replace with 3/6/6.71 model

## Slide 8: Diagonals
Joinery and carpentry products require 90º or square corners.
All right-angled quadrilaterals (squares and rectangles) have equal diagonal measurements as opposed to quadrilaterals like the parallelogram shown below, which have different angles and therefore different diagonal measurements.
A squaring rod is a straight pointed timber that is cut the length of the diagonals and is used to check frames for square when gluing up.

## Slide 9: Angles of a triangle
When you know one other angle of a right-angled triangle it is possible to find the third
The angles of a triangle always add up to 180º
So if you know one angle is 30º and a right angle is 90º then you know the third angle must be 60º as the total of three angles is 180º

## Slide 10: Angles of a triangle
This principle also applies to a angle that dissects a straight line as straight lines are half of a full revolution and therefore half of 360º and equal 180º as seen on a clock at 6 o’clock.
So if you know the angle of one side of the dividing line, you can work out the other side.

## Slide 11: Angles of a triangle
These calculations are used regularly by carpenters to calculate angled cuts. They are essential for various tasks from setting out roofs and stairs to the use of compound mitre saws.
Triangulation is also used by surveyors and civil engineers to work out projected height distances and to level footings to ensure that constructions are built level and stand upright.

## Slide 12
Any questions?