## Slide 1: PowerPoint 8: Joinery
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: The objectives of joinery
  The main reasons for making a joint are:
  To extend the length of a piece of timber or board whilst maintaining the strength of the material.
  To join timbers together at an angle of 90º as in door and window frames using mechanical joint features.
  To join curved and compound angles such as handrails.
  To join timbers together at any angle using structural joints as in staircase strings.
  To negate the use of adhesive (in green timber) and allow joined timbers to move together as they expand and shrink.

## Slide 3: The principles behind joinery
  The strength of a joint is based on contact area. The greater the contact area between timbers, the stronger the joint. Examples of this are the finger joint or the scarf joint.
  The type of joint used needs to reflect the stresses on the installed timbers or frames, as in a mortice and tenon used on doors as opposed to bridle or half lap joints.
  Joints should be correctly proportioned so even stresses are placed on both timbers that are joined.
  Rebates and mouldings should be considered and integrated to enhance the mechanical strength and finish of the joint.
  Timbers require different joints adhesives and treatments depending on species, moisture content and conditions.

## Slide 4: Types of 90º joint
  Butt (screwed, strapped, nail plates, dowelled or biscuited)
  Half lap (dowelled)
  Bridle (dowelled)
  Housing (screwed)
  Finger or comb
  Mortice and tenon
  Dovetail
  Box joints
  Butt mitre
  Half lap mitre

## Slide 5: Types of straight joint: widening (W) and linear (L)
  Scarf (L)
  Table spliced (L)
  Splayed (L)
  Finger or comb (L)
  Tongue and groove (LW)
  Rebate or Half lap (LW)
  Dowelled (W)
  Biscuit or spline (using a biscuit jointer) (W)
  Worktop joint or handrail (with mechanical connectors) (L)
  Pocket screwing (W)

## Slide 6: Butt joints
Skew or dovetail nailing or screwing helps prevent separation and pulls timber in as it shrinks. The nature of the butt joint means that light gaps are visible if cut inaccurately or the timbers shrink.
Butt joints need to be square on two planes to keep the frame both square and free from twist.
Skew nailed butt joint section
Skew nailing
Skew nailed butt joint
Butt joint with framing anchors

## Slide 7: Mitres and scribes
A mitre joint is commonly used at internal and external, square intersections of mouldings. It can be cut by machine using a chop saw, or by hand using a mitre box. A scribe is used internally. Scribes and mitres are decorative not structural.
Mitre joint Scribe joint

## Slide 8: Cutting scribes from internal mitres
Scribes can be cut by cutting an internal mitre and following the profile of the cut with a coping saw or jigsaw. This method requires two cuts and does not allow for the flooring or walls being out of level.

## Slide 9: Direct scribe
Scribes can also be made by butting the two surfaces together and using a pair of compasses or scribing block to follow the profile of the surface being scribed to. This is a common method when scribing kitchen end panels to uneven walls.
Care must be taken to keep the scribe point and pencil level to the surface being scribed to, to maintain the correct height or position of the scribe detail.

## Slide 10: Halving joints
Types of halving joints: dovetail halving (left) and corner halving (right)

## Slide 11: Housing joints
Housing joints are used in non-structural joints such as door linings and window boards. The housed timber means that gaps are not revealed if the timber shrinks.
Three types of housing joint: through, stopped and tongued

## Slide 12: TGV
TGV boards normally include a V chamfer and are sometimes jointed on sides and ends. The joint allows expansion and contraction without a visible gap or the timbers completely separating.
Tongue and groove V-jointed board
Tongue and groove joint: V-jointed

## Slide 13: Reinforced butt joints
Whether you are using biscuits, dowels or splines the process is similar. In the case of widening joints, they require accurate machining as the finish must be flush. Once the machine or jig is set up correctly this is a very efficient way to joint multiple boards
Edge joint with biscuits Edge joint with a loose tongue Edge joint with dowels A kitchen unit jointed with dowels

## Slide 14: Dowels and biscuits
Dowels and biscuits should be tight fitting and are able to swell through gluing and moisture to increase the strength of the joint.
Biscuits are cut using a specialist groover or biscuit jointer. Dowels are drilled in with the help of a jig to keep it straight and to position it.

## Slide 15: Engineered dowels
This is similar to a dowel joint, but the dowels are a different shape and look like dominos. They are made from both soft and hardwood for internal and external use and can come in long lengths, enabling them to be used as false tenons even on door styles.

## Slide 16: Finger or comb joints
Finger joints can be used at 90º to make drawers and boxes. A box joint is similar but with larger and fewer cuts. The more fingers, the greater the contact area.
Finger joints can be used to extend the lengths of timber. This is a strong joint due to the amount of contact and glue area. These joints require specialist cutters and are generally created on spindle moulders or tenoners.

## Slide 17: Bridle joints
Bridle joints are divided into thirds of the thickness of the timber to maintain the maximum strength of the two pieces being joined. They have various applications including mitred and T joints and would generally need through dowelling for heavy frames to avoid separation.

## Slide 18: Mortice and tenon joints
With these joints the male part is called the tenon and the female is called the mortice. They are extremely strong if made well.
Tenons can be stopped so they do not run through the back of the timber. In the first image the tenon has been stopped at the intersecting mortice to accommodate the other tenon.
Tenons can also be through, as shown in the bottom image. This tenon has been wedged to avoid separation.

## Slide 19: Mortice and tenon joints
The image shows the correct divisions of joint. All tenons are a third the thickness of the timber. The haunch of the top and mid rail are a third the depth of tenon and the bottom tenon depth is divided into quarters.
1/3
1/3
1/3
1/3
2/3
1/4
1/4
1/4
1/4
1–2 times tenon thickness
Mortice and tenon joints
1/3

## Slide 20
Handrail connectors can be straight or angled. A pilot hole is drilled to take the long screw which is wound in. Two intersecting through holes in the other piece allow access to the connector, allowing the joint to be tightened.
Handrail connectors

## Slide 21
Worktop connectors are straight connectors that are let into cut outs in the underside of the worktop (called dog bones due to their shape). These are housed openly to allow access to the connector allowing the joint to be tightened. Biscuits are often used in conjunction to align the two surfaces and create a tighter joint. Waterproof glue or silicone is used on the joint to keep moisture out.
Worktop connectors

## Slide 22: Kitchen unit connectors
Cam and dowel connectors are made of a screw-in dowel. This is then pulled tight by a cammed circular insert which pulls in the raised end of the dowel as it turns.
The cammed insert allows pressure to be exerted on weak material such as chipboard without ripping out.
Closing

## Slide 23
Any questions?