## Slide 1: PowerPoint 5: Hand tools
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Hazards associated with hand tools
The two most common hazards associated with the use of hand tools are:
  misuse
  improper or lack of maintenance.
Misuse occurs when a hand tool is used for something other than its intended purpose.
An example would be using a panel saw to rip timber. This may cause the saw to bind and flex, cutting the user’s arm.
Tip: If you are applying a lot of strength using a tool, you are using it wrong, using the wrong tool or the tool requires immediate maintenance.

## Slide 3: Hazards associated with hand tools
  Maintenance
  Improper maintenance allows hand tools to deteriorate into an unsafe condition.
An example of this would be a blunt chisel. This could result in the user applying excessive force while paring leading to them following through and cutting or stabbing themselves. Maintenance includes:
  Visual inspections (checking saws aren’t warped, metal fractures)
  Checking for sharpness (newspaper test, eyeing down the edge)
  Sharpening, cleaning and oiling (cleaning rust and residue, protection)
  Storage (dry, separate edges, secure)
  Correct use ( e.g. not using a wood saw on plasterboard or soft block)

## Slide 4: Legislation associated with hand tools
Health and Safety at Work Act 1974
This is the main health and safety legislation that operates in the UK. It places a duty on employers to ensure that:
woodworking machinery is safe to use
a safe system of working is in place
workers are informed about all risks and hazards
all operatives are trained and competent to operate machinery.

## Slide 5: Legislation associated with hand tools
Provision and Use of Work Equipment Regulations (PUWER) 1998
These regulations place a duty upon all employers to ensure that:
equipment is suitable for the purpose it is being used for
woodworking tools are maintained
inspection of tools and machinery is undertaken
risks from using woodworking tools are minimised.

## Slide 6: Which tool do I need?
There is a tool for every job. Our job is to identify the correct tool and to use and maintain it correctly. For example:
Wooden-handled chisels require a wooden mallet or failing that you should use the cheek of your hammer to avoid breaking the chisel handle.
A lump hammer and bolster should be used to remove brick or block. A claw hammer could break, and you will damage the face, making it more liable to break skin and slip on nails.

## Slide 7: Using a hammer
Hammers are designed to be held at near the end of the handle, to utilise the weight, and often have a flared grip to prevent them from slipping out of the user's hand. However not all do, so always take care to have a dry grip that is free from sweat and grease.
Users who hold the hammer higher up the handle tend to suffer from wrist and hand problems and tend to have more accidents.

## Slide 8: Which tool do I need?
Specially designed tools may be needed in some hazardous situations.
  Non-sparking tools in the presence of flammable vapours or dusts.
  Insulated tools with appropriate ratings must be used for electrical work.
  Low vibration hammer handles for long duration work.
  Shock-resistant chisel handles for continuous heavy work.

## Slide 9: The first and most important tool you need
  Tape measures are available in a variety of lengths, makes and uses.
  The hook should always be free to slide in and out and move the thickness of the material that it is made from. This is so you can hook it to get an accurate external measurement, or push it for an accurate internal measurement
A well-engineered tape measure will have the width from the back of the case to the zero point on the tape marked on the case. The tape to the left has a hinged tab on the back of the case exactly 100mm from the zero point, making measuring internals far easier and more accurate than bending a tape into a corner. But you must remember to add 100mm back on to your length!

## Slide 10: Hand saws
There are four basic types of hand saw which carpenters and joiners use. These are:
  Rip saws
  Crosscut saws
  Panel saws
  Tenon saws
  Dovetail saws
  Hardpoint saws
  Multi-purpose hardpoint saws
Other saws include: flush cut, pad, fret, hack, bow, mitre and coping saws.

## Slide 11: Hand saws
  Rip saws are used for cutting along the grain.
  Crosscut saws are for cutting across the grain.
  Panel saws are a general-purpose type of cross cutting saw (boards).
  Tenon saws are narrow and stiffened to allow accurate cross cuts.
  Dovetail saws are small, stiffened and sharpened for ripping.
  Flush cut saws are flexible and sharpened on one side.
  Pad saws are for cutting small openings such as keyholes.
  Coping and fret saws are bow saws designed to cut curves as in a jigsaw. A fret saw is used for finer work.
  A mitre saw is set in a frame which can be used to cut accurate angles.
  Japanese saws (pictured) cut on the pull stroke and are very effective.

## Slide 12: How to use a hand saw
When holding a saw, you should point your finger down the top of the blade to keep the saw straight; most handles are moulded to facilitate this. This enables you to subtly twist the blade to alter the direction of the cut. Saws without backs such as panel saws can cut shallow curves in boards by twisting the saw in this way, which is made easier spraying the saw with lubricant.
To begin a cut. you should place the thumb of your other hand upright with nail facing downward and run the saw two or three times against, it using a backstroke and keeping the blade vertical. Cut as close to the waste side of your pencil mark as possible.

## Slide 13: How to use a hand saw
Before attempting a cut always make sure:
Your work area is tidy with no metal objects near that could catch the blade ruining teeth.
Mark-up timber on at least two sides to guide the sawcut. It is good practice to mark on all four sides when crosscutting to check sides are square and faces parallel.
Position the timber as near to the edge of the timber as you can while maintaining a straight arm and clamp when possible.

## Slide 14: How to use a hand saw
Crosscutting is normally best somewhere near 45º and is normally quick and relatively easy due to the saw cutting at 90º to the grain, slicing through it.
Ripping requires a shallower angle and separate the timber down the grain using a gouging action to rip the grain fibres apart. On larger timbers this can be difficult and time consuming, especially if attempted with the wrong saw.

## Slide 15: Hand saws
Heel
Teeth
Blade
Handle
Back
Toe

## Slide 16: Hand saws and TPI
  TPI stands for teeth per inch (25mm). When counting the number of teeth, include the first and last tooth.
Cut
90°
4.5 teeth per 25mm
Cut
8 teeth per 25mm
65°

## Slide 17: Hand saws
Hand saws vary in length from 450mm up to 650mm.
  Rip saws are generally 650mm in length, with a tooth size of 5 teeth per 25mm.
  Crosscut saws range from 450 to 600mm in length, with teeth sizes ranging from 8 to 10 teeth per 25mm.
  Crosscut saws of 500–550mm in length with 10 teeth points per 25mm are commonly known as panel saws. These saws are used to cut plywood and thin boards or large joints
650–750mm
3–5 teeth/25mm
60°
6–8 teeth/25mm
60°
500–550mm
8–10 teeth/25mm
60°
Rip saw
Cross saw
Panel saw

## Slide 18: Hand saws
Rip saws are made for cutting timber along the grain. The teeth of this saw are large and flat, shaped to cut like chisels.
Rip saw:
Cutting with the grain
Cut
90°
4.5 teeth per 25mm
Chisel edges act as a series of chisel cuts

## Slide 19: Hand saws
Crosscut saws are designed to cut across the grain. The teeth resemble knife points, each being sharpened at an angle across the blade to produce knife edges.
Cut
8 teeth per 25mm
Knife points sever fibres to produce a clean cut across grain
65°
Crosscutting:
Cutting across the grain

## Slide 20: Pitch of teeth
To make saws cut smoothly, the front faces or edges of the teeth slope forward.
This slope is called the pitch and varies from 30 for rip saws up to 140 for crosscut saws.
Rip saw Crosscut saw

## Slide 21: Chisels
There are many types of chisels available, each one designed to be used for a specific purpose. The five used most commonly are:
Bevel edged
Firmer
Paring
Mortice
Gouge

## Slide 22: Bevel-edged chisels
  The back of the blade is bevelled along both edges so that they can be used to cut in acute corners.
  Lightweight, suitable for paring.
  Available with wooden, fibre glass or plastic handles.
  If a hammer is used on this type of chisel, it should be used with the cheek to avoid breaking the handle.

## Slide 23: Firmer chisels
  Used for general bench and site work. Normally square edged.
  Solid steel blade is much stronger than a bevel-edged chisel.
  Can be used for paring or cutting joints.
  Can withstand light blows from a mallet, but care must be taken.
  If the chisel has a wooden handle, it may split due to repeated blows from a mallet.

## Slide 24: Mortice chisels
  Used for the cutting of mortices or slots which often form part of a joint.
  Strongly made to withstand heavy blows from a mallet.
  The blade’s thickness prevents the chisel twisting in the mortice or slot.
  The handle of this type of chisel can be wood or plastic.
  Some chisels have a leather washer incorporated to absorb the shock when struck with a mallet or hammer.

## Slide 25: Gouges
A gouge is a chisel with a curved cutting edge. It is used to cut curved or contoured work.
There are two main types of gouge:
scribing gouge (in cannel)
firmer gouge (out cannel)
The cannel is the bevel, so:
  an in-cannel gouge is ground on the inside
  an out-cannel gouge is ground on the outside.
Blade
Blade ground on inside
Scribing gouge
Blade
Blade ground on outside
Firmer gouge

## Slide 26: Gouges
Scribing gouges are ground on the inside and are used for contour work where hollow or concave curves are required.
Firmer gouges are ground on the outside are suitable for convex curves and any kind of scooping-out operation. These are sometimes called a carving gouge.
These chisels are used to fit and scribe joints of moulded timber, e.g. in doors and windows

## Slide 27: Planes
Types of plane
There are many types of plane available, each one designed to be used for a specific purpose. The most commonly used, from longest to shortest are:
  Try plane
  Jack plane
  Smoothing plane
  Shoulder plane
  Block plane
  Bullnose plane

## Slide 28: Planes
Toe
Knob
Mouth
Plane iron
Sole
Adjusting screw
Frog
Frog adjustable screw
Handle
Lateral adjustment lever
Back iron
Lever cap Cap screw
Blade
Cam
Heel

## Slide 29: Try plane
  The longest bench plane, ranging from 450mm to 600mm.
  Sometimes called jointer or trying plane.
  Generally used for smoothing long lengths of timber.
  The length helps to make the surface as level as possible.
  Typical blade width is 60mm.

## Slide 30: Jack planes
  Medium-length bench plane, generally 350mm to 380mm.
  Similar blade width to the smoothing plane.
  Used for rapid and accurate removal of waste material such as dressing doors for hanging.
  A great plane for square edging medium-sized components.
  Also used to clean up bench joinery joints.

## Slide 31: Smoothing plane
  The shortest of the bench planes.
  Used for removing pencil and machine marks along with final finishing or cleaning up.
  Useful for cleaning up opposite grains, such as door joints
  Also used for bevelling, arising and chamfering to leave a smooth finish.

## Slide 32: Block plane
Used like a smoothing plane for finishing work
Often has cheaper disposable blades
Easy to handle and light for fine work
Can be used single handed
Fine adjustments and shallow cutting angle allow microns to be removed

## Slide 33: Shoulder plane
Similar set to a block plane for finishing work
Has an extended toe to enable tenons to be planed flat
Blade runs to the edge of body enabling shoulder cuts
Easy to handle and light for cross grain work

## Slide 34: Bullnose plane
Similar to a shoulder plane but without the extended toe
Cuts right to side edge as with the shoulder plane
Cuts as close to front edge as possible leaving little clean up for internal rebates
Single handed use for fine work
Can be used to arris edges into corners

## Slide 35: Cramps
Cramps are normally used to secure work while cutting or assembling glued work by applying pressure.
Sash cramps (pictured top) use flat bars and sliding jaws, one of which can be wound in to cramp the material.
G cramps (below) are fixed, available in various sizes and are less prone to vibration than quick release cramps although take longer to set up.

## Slide 36: Cramps
Quick release bar cramps can be used single handed and are lighter than most cramps, allowing easy assembly,
F clamps are similar to G cramps but have a sliding jaw that can be wound in, reducing tightening and loosening time.
Other cramps include:
Toggle
Strap cramp
Sprung cramp
Frame cramp
Screw cramp
Wedges and bench dogs

## Slide 37: Cramping devices
Vices are an essential tool for benchwork and come with quick release mechanisms, enabling them to be slid into position before cramping. They are designed to allow joiners to work on timber hands free.
Floorboards cramps are designed to cramp well dried floorboards tightly together prior to nailing, reducing air gaps and drafts.

## Slide 38: Sharpening
An oilstone is a fine-grained stone and an abrasive surface which is used to sharpen some cutting tools.
These are available in coarse, medium or fine grades, often as a combination with two of them on opposite sides.
Combination stones like these can be used with oil or water but never with both.

## Slide 39: Sharpening
Diamond stones carry out the same job as oilstones. A very fine lubrication or water is required. They are a lot cleaner than oilstones.

## Slide 40: Whetstones
Whetstones carry out the same job as oilstones but are often a much finer grit allowing a finer polish. They need to be soaked in water and are easier to mark than other stones. They are a lot cleaner than oilstones but need more maintenance than diamond stones such as re-honing.

## Slide 41: Method
The sharpening or honing angle on a chisel or a plane blade is 30°
When honing a hand tool all of the stone must be used to prevent hollowing the stone. A figure of 8 is a good method of honing.

## Slide 42: Method
Whenever you sharpen a chisel/plane on an oilstone, follow these three golden rules:
Use the whole area of the oilstone to keep it flat.
Lubricate the oilstone with a thin layer of oil, and wipe clean after use to avoid clogging the surface of the oilstone.
The oilstone should be held firm in a vice or on a flat surface.
Pressure
Keep flat

## Slide 43
Any questions?