## Slide 1: PowerPoint 9: Planning and setting out
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: The processes of planning
Scale drawing, CAD design often from architect, or sketch from manager or customer with actual measurements and sizes marked.
Setting out full sized rod from drawings, including all details.
Make up a cutting list of all components to produce a materials list
Use material list to obtain correct amount of timber.
Square edge and dimension all timber marking face side and edge.
Mark all timber from setting out rod including joints, moulds and rebates using face marks to orientate faces.
Manufacturing process can begin. Machining can constantly be checked against the rod.

## Slide 3: Setting and marking out tools
Marking gauge
Mortice gauge
Cutting gauge
Range of steel rules
American roofing square
Marking knife
Dividers
Protractor, drawing set squares, compass, pencils

## Slide 4: Setting and marking out tools
Combination square
Carpenter’s try squares
Set mitre
Combination gauge
Sliding bevel
Squaring over box
Framing square

## Slide 5: Drawings
Detailed scale drawing with measurements of a sash window showing the detail required to set out a full-sized rod (note the gaps around the sashes)
Jamb
Head
Meeting stiles
Cill

## Slide 6: Setting out rods
  A rod allows the joiner to design his project actual size, using actual profiles and rebate measurements to work out the joints.
  A rod allows the joiner to check the components against the drawing for accuracy which helps avoid wastage.
  Drawing different elevations of the project helps the joiner visualise and alter the design if required.
  Rods can be kept as a resource to use on future jobs.
What are the main reasons for drawing up a 1:1 rendering of what is to be built, and how is a rod used?

## Slide 7: Tolerances
These are industry standards regarding the fit and size of gaps of carpentry and joinery products.
They are generally listed as specifications by a products supplier but can also be found in architect's drawings or found online.
A good example of this would be fire doors, which are supplied with specifications showing the amount of material that can be removed, and the gap and groove sizes for the intumescent strips. Gap sizes vary from door to door between 2mm and 4mm. If gaps are too large, they can completely negate the fire protection that the door should provide making a 30-minute FD30 door burn through in 5 minutes.
Other tolerances include the gaps around windows which avoid water being trapped between the sash, frame and sill. The gap between the bottom rail of the sash and the sill is essential to allow water blown into gaps around the sash to flow away (see drawings and rods).
Tolerances should be included in the planning stages and always in setting out, so excessive planing and fitting can be avoided, which could weaken the joint structure of the product.

## Slide 8: Setting out rods
  Doors and casement windows, especially when they have detailed mouldings and panelled or glazed rebates
  Sash windows, especially the joints at the cill and meeting rail
  Staircase details such as newel post housings for kite winder staircases
  Curved and shaped work that move through two or three planes, such as handrail wreaths
  Detailed panelling work
  Frames and detailed linings
What are some of the main projects where rods are most useful?

## Slide 9: Face side and face edge
  Face side and face edge is normally determined by deciding which is the best side of the timber. An example of this would be the inside of a wall string, and deciding which is the cleanest, most knot and defect-free face side of the stock. This can be decided once the faces have been roughly planed to expose the properties of the timber.
  Once selected, the face side and face edge are marked as shown in the drawing. These are the first two sides of the timber to be planed straight and square edged with each other. Once a square and edge side have been established these are marked as shown. The other sides can then be made parallel and squared off from them, by using them as a datum point. This is shown by the square working from the face edge in the drawing.
    edge

## Slide 10: Storey rods and datum points
This is a rod, in the case of stairs, that is the height from finished floor to finished floor and allows the joiner to work out the rise and going required for a staircase.
It can also be the determined by the height from floor to ceiling for a job where storey height door frames are to be used and would display the height of the door opening, thickness of the transom, distance of the fixed light, and the thickness of the head.
It can also be used to mark off items such as cornice, picture rail, dado, panelling, and other items within buildings that need to be the same height above or below the datum.
The position of each tread can then be marked on the rod which can be easily used to check newel housing positions by placing them side by side.
Floor to floor height:
the distance needed
to calculate the rise
and going of a
staircase

## Slide 11: Storey rods and datum points
A datum point is used as a reference by marking a level line around the room, as with a laser level, and lining the datum point on the rod up with it. All heights can then be transferred.
Plate shelf
Skirting
Rebate bead
Bolection mould
Framed ground
Dado
Rail
Plough groove
Solid raised panel
Stuck mould
Ply panel Panel mould
Softwood grounds
Vertical door detail
Framed ground
Framed ground
Full height, vertically laid matchboarded panelling
Bottom of cornice
Top of picture rail
Datum
Top of dado rail
Top of skirting
Head
Borrowed light
Transom
Storey height board
gives you the thickness of the head and transom
Height of the door opening

## Slide 12: Cross marking
Cross marking requires lining groups of components face side up and normally edge sides opposite.
This utilises the planed and squared side and edge of one timber to mark across all components at once from first stages.
Used to maintain the parallel in frame construction, including studwork and joinery.
Saves time and makes mass production more efficient, as with windows of the same height for the same building.

## Slide 13: Cross marking strings, combined margin and pitch board
  Once divided, the marking out is done using a pitch board laid on the margin; here a template combines both. Rise and tread templates are then laid on the outer edges of pitch marks and marked around.
When marking out stairs, the setting out is done directly onto the strings. These should be cross marked as shown to ensure they remain identical reflections of each other. Note face marks.
Riser temp
Tread temp
Pitchboard and margin temp
Margin line
Face mark
Dividers
Left and right-hand string

## Slide 14: Pitch boards and tread and riser templates
  This pitch board has a fence that runs along the edge of the strings and spans the margin. This is marked separately using a margin board or combination square.
The tread and riser templates are tapered to allow the treads and risers to be wedged from underneath and behind respectively.
Tread template and wedge allowance
Riser template and wedge allowance
Rise
Going
Battens to run against string

## Slide 15: Summary
In summary a rod is an actual representation and physical reference point for component sizes, joint proportions and mouldings.
A bench rod is a 1:1 scale drawing of the product, providing as much information of side and plan details as is required to construct it accurately and efficiently.
Rods are used to ‘mind map’ a procedure and allow a joiner to anticipate problems and overcome them before manufacturing components, avoiding waste and machining issues.
A correctly drawn rod is something to be trusted and used as a constant reference throughout the setting out, marking out and manufacture procedures, avoiding costly mistakes and relieving the ‘will it work?’ stresses from production.

## Slide 16
Any questions?