## Slide 1: PowerPoint 2: Health and safety
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Personal Protective Equipment (PPE)
Using personal protective equipment is your responsibility. Physical protection protects you against physical injury.
  Protective equipment includes:
Hard hat
Gloves
Safety glasses
Hearing protection
Respiratory protection
Protective footwear and clothing
Hi-vis
Knee pads

## Slide 3: PPE: Respiratory protection
  Face masks are categorised based on which hazards they are suitable for:
  FFP 1 refers to the least filtering of the three masks with an aerosol filtration of at least 80% and leakage to the inside of maximum 22% This mask is mainly used as a dust mask (e.g. for home renovations)
  FFP2 masks have a minimum of 94% filtration percentage and maximum 8% leakage to the inside. They are mainly used in construction, agriculture, and by healthcare professionals against influenza viruses.
  FFP3 masks are the most filtering mask of the FFPs. With a minimum filtration percentage of 99% and maximum 2% leakage to the inside, they protect against very fine particles such as asbestos.
  Source: https://standards.cen.eu/index.html

## Slide 4: PPE: respiratory protection
  Disposable paper facemask (normally FFP1)
  Disposable valved paper facemask (normally FFP1/2)
  Moulded silicone mask with filters (normally FFP3)
  Dust filters/vapour filters
  Full-faced respirator (FFP3)
  RPE is available in different styles depending on the hazard it is suitable for:
  Many timbers are toxic or are identified as ‘sensitisers’. For instance, yew dust is highly toxic and can cause death.

## Slide 5: PPE: hearing/noise protection
  ‘The level at which employers must provide hearing protection and hearing protection zones is now 85 decibels (daily or weekly average exposure) and the level at which employers must assess the risk to workers' health and provide them with information and training is now 80 decibels.’ Source: https://www.hse.gov.uk/noise/regulations.htm
  ‘The generally accepted standard to minimise hearing risk is based on an exposure to 85 dBA for a maximum limit of eight hours per day, followed by at least ten hours of recovery time at 70 dBA or lower.’
  At 91 decibels, your ears can tolerate up to two hours of exposure.
  At 100 decibels, damage can occur with 15 minutes of exposure.
  At 112 decibels, damage can occur with only one minute of exposure.
  At 140 decibels, immediate nerve damage can occur.
  Source: /www.noisehelp.com/noise-dose.html

## Slide 6: Collective control measures: signage
  Mandatory signs (blue) circular: Things you must do. Informs of mandatory site/workshop requirements.
  Prohibited signs (red) circular: Things you must not do. Informs of prohibited actions within the site/workshop.
  Warning signs (yellow) triangular: Be aware. Informs all who enter of the dangers within the site/workshop.
  Information signs (green) square or rectangular: Follow me. Gives information to all who enter the site/workshop.
  Fire signs (red) square: Here it is. Informs where the fire equipment is located.

## Slide 7: Types of protection: signage
Other signage can be found in the COSHH specifications regarding volatile organic compounds (VOCs). These are compounds which are harmful to life.
The orange symbols are the European standard. This was replaced by the red diamonds which are world standard and recognised everywhere.
Causes fire
Explosive
Dangerous to the environment
Intensifies fire
Long term Corrosive health hazard
Toxic
Irritant
May explode when heated
European symbols International symbols

## Slide 8: Fires
If you discover a fire you should:
Raise the alarm by shouting ‘Fire!’, pressing the nearest alarm button or calling 999.
Only attempt to put the fire out if it is small, you are trained to do so and have the correct extinguisher or blanket available. Ensure your exit is clear before attempting to do so. Those not trained must evacuate immediately.
Leave all belongings and tools and leave in an orderly manner, helping those who may need help.
Assemble at the emergency assembly point and await further instruction.

## Slide 9: Fires
Fire require three sources to burn. These are:
Oxygen
Heat or a spark
Fuel
If any one of these are not present the fire will not burn. Most fire extinguishers remove the oxygen or heat from the equation. Different types of fuel require different types of extinguisher.

## Slide 10: LEV: Local exhaust ventilation
  Dust bag
  Portable extraction unit
  Industrial extraction unit (normally fixed in a workshop setting)
  Air filter (normally ceiling mounted and used in workshops and offices)

## Slide 11: Barriers and walkways and security
  Sign in book
  Site induction
  Security barriers
  Heras fencing
  Designated walkways
  Handrails and kickboards
  Safety areas
  Fire collection points

## Slide 12: Risk assessments, first aid and near miss records
  Health and safety briefings
  Staff training
  Site induction
  Safety boards
  Health and safety inspections
  First aiders
  Near miss book
  Continual risk assessments

## Slide 13: Risk assessments
Five steps to risk assessment can be followed to ensure that your risk assessment is carried out correctly, these five steps are:
Identify the hazards.
Decide who might be harmed and how.
Evaluate the risks and decide on control measures.
Record your findings and implement them.
Review your assessment and update if necessary.

## Slide 14: Health and safety risks
  Safety risk: an immediate danger to your safety
  Falls from height (ladders, scaffold, MEWP, fragile roofs, voids)
  Lifting operations
  Plant (stuck by, overturn, crushing MEWP)
  Fixed and portable machinery
  Collapse
  Asphyxiation
  Electrocution
  Falling objects
  Slips, trips and falls
  Struck by projectile (eye injuries)

## Slide 15: Health and safety risks
  Health risk: a mid or long-term, often irreversible risk to your health
  Noise
  Hardwood/engineered board dust
  Asbestos dust
  Silica dust
  Vibration
  Manual lifting
  Dermatitis
  Environment (temperature, damp, lighting etc.)
  Repetitive work (standing, position), housemaid’s knee (bursitis)

## Slide 16: Reporting accidents
You must comply with the Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR) 2013
An accident that causes death, major injury or absence from work for more than three days must be reported to the HSE using an Accident Record Form. Minor accidents are usually reported in an Accident Book.
It is your responsibility to report all accidents and near misses to a supervisor who completes accident reports. You will need to give information if you are involved in or witnessed an accident or near miss.
Reporting accidents and near misses helps you to identify hazards and take actions to avoid accidents in the future.

## Slide 17: Health and Safety at Work Act 1974 and regulations
  Electricity at Work Regulations, 1989
  Management of Health and Safety at Work Regulations, 1999
  Workplace (Health, Safety and Welfare) Regulations, 1992
  Provision and Use of Work Equipment Regulations (PUWER), 1998
  COSHH (Control of Substances Hazardous to Health Regulations), 2002
  RIDDOR (Reporting of Injuries, Diseases and Dangerous Occurrences Regulations), 2013
  Personal Protective Equipment at Work Regulations, 1992 (PPE must be mandatory and supplied free of charge)
  Control of Noise at Work Regulations, 2005
  Construction Design Management regulations (CDM), 2015

## Slide 18: Be methodical, be responsible
  Many work accidents can be avoided by maintaining a tidy and organised workspace and carrying out regular safety checks.
  Accidents frequently occur because of rushing and improper set-up.
  Never use machinery without undergoing relevant training.
  Always put your own safety and that of others first by double checking, especially when setting up machinery, power tools and extraction.
  Always check the mandatory requirements of the workplace.
  Wear the appropriate PPE for the task.

## Slide 19
Any questions?