## Slide 1: PowerPoint 11: Structural and first fix activities
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Structural activities prior to first fix
What are some of the structural activities for a carpenter prior to first fix?
  Post and beam timber framing
  Installing prefabricated external walls and roofs
  Cutting roofs and finishing eaves
  Building and installing dormers
  Installing roof trusses
  External structural studwork
  Formwork for concrete pads
  Installing steel or timber beams and lintels
  Temporary shoring

## Slide 3: First fix activities and specialisms in wood occupations
Traditionally, first fix begins when the roof is on and the building is relatively watertight. Although sometimes internal joists and flooring are laid, and studwork constructed, prior to the roof being installed. Activities include:
  Structural joists and studwork
  Door and window frame fitting
  Floor joist coverings
  Fitting staircases
  Fitting ceilings
  Fitting partition studs
  Fitting linings

## Slide 4: First fix activities and specialisms in wood occupations
What are the main first fix activities for a joiner?
  Setting out, marking out, manufacturing, assembling and finishing:
  Staircases
  Window and door frames
  External doors and sashes
  Porches, conservatories and atriums
  Green oak structures

## Slide 5: Truss roofing
  The image shows a gable ended pitched roof made with prefabricated trusses.
  This is a cheap and efficient way to fit a roof. The trusses are evenly spaced on the wall plate, where they are nailed, and then strapped from within at the ridge and diagonally, bracing the trusses.

## Slide 6: Truss roofing
  This image shows the layout of the bracing timbers.
  It also shows the ladders that create the gable ends and the trimmed rafters around the chimney.
  Trusses and wall plates will then also be fixed to the walls using metal straps.

## Slide 7: Truss roofing
  This image shows a trussed lean-to roof.
  It also shows the ladders that create the eaves and the horizontal and vertical wall plates.
  Trusses and wall plates will then also be fixed to the walls using metal straps and concrete screws.

## Slide 8: Cut roofs
  This image shows a common rafter and the names for each cut.
  The section removed by seat and heel cuts to accommodate the wall plate, is called a bird's mouth.
  The span is measured horizontally from the outside of the wall plate to the centre of the ridge.

## Slide 9: Cut roofs
  This image shows a common rafter with overhangs cut to accept fascia and soffit.
  Also pictured are the bevels positioned on the margin to mark out each cut.
  Note the rise is calculated to the margin created by the intersection of seat and heel cuts.

## Slide 10: Cut roofs

## Slide 11: Cut roofs
  This image shows an intersection between a main roof and an additional roof using a valley lay board. It shows the additional ridge, common, jack and valley rafters which in this case are jacks.
  A ridge is temporarily supported, and the rafters are fixed through the ridge into the opposite rafter. Rafters are also fixed to the wall plates (not shown) which are fixed to the walls using metal straps.

## Slide 12: Cut roofs
  This image shows an intersection between a main roof and an additional roof using a valley rafter. It shows the main and additional ridge, common and jack rafters. Also note the valley rafter, spanning from wall plate to ridge
  A ridge is temporarily supported, and the rafters are fixed through it into the opposite rafter. Rafters are also fixed to the wall plates which are fixed to the walls using metal straps.

## Slide 13: Cut roofs
  This image shows a hipped roof. It shows the ridge, common, hip and jack rafters. The hip rafter acts similarly to the full valley rafter in the previous slide but is an external rather than internal intersection.
  A ridge is temporarily supported, and the rafters are fixed through it into the opposite rafter. Rafters are also fixed to the wall plates which are fixed to the walls using metal straps.

## Slide 14: First fix joists
The image shows various types of joist and the methods used to fix them.
Herring bone struts are an efficient and effective way to keep joists upright as they tighten as the timber shrinks and use less timber than noggins.

## Slide 15: Engineered joists
This image shows metal web floor joists which use a similar principle as herring boning to produce light and strongly engineered joists.
I beams are generally made from OSB board, which is made from recycled timber, and softwood. They are lighter, cheaper and shrink less than solid joists.

## Slide 16: Trimming joists
The image shows the trimmed joists around a stairwell. Notice that they are doubled up and bolted.
The floating joists to the right and overlap to the left would sit directly onto supporting walls.
Joists are shown fitted in standard joist hangers and the trimmers are fitted with wider hangers that fold over the back of the second joist.

## Slide 17: Floor joist and flat roof coverings
The image shows how flooring should be staggered to avoid joints lining up.
When laying chipboard, it is essential to stagger the joints to stiffen the floor and avoid straight joints or repeated patterns
What staggered joints should and shouldn’t look like
Even distribution which provides a natural looking floor
The planks are too evenly laid. Incorrect fitting
The planks are too evenly laid. Incorrect fitting

## Slide 18: Floor joist and flat roof coverings
Underfloor heating can make solid floorboards shrink and crack, especially if they are not dried enough. Solid flooring should be stored in the building where it is to be fitted for some time to allow it to adapt to the conditions prior to beginning to fit it.
Floorboards such as these are usually nailed.
Solid flooring will shrink and expand more than engineered products. A sufficient expansion gap should be left around the walls to allow for this as the flooring will begin to buckle if it expands with no room to do so and can push a wall out.

## Slide 19: Floor joist and flat roof coverings
OSB is more commonly used for flat roof coverings. OSB is generally covered with bitumen sheeting or fiberglass protecting it from UV damp and moisture which will degrade it over time.
Ply is used in areas of moisture such as bathrooms.
Tongue and grooved chipboard is the most widely used product for internal joist coverings. TGV chipboard is treated with moisture resistance but should not be left in wet or damp conditions prior to the joints being glued and taped as it can become soft and lose its integrity. TGV flooring is normally glued and screwed to avoid squeaking as the joints rub together.

## Slide 20: Studwork
Studwork refers to all vertical frames that are made to create structural or external walls and internal partitions.
The studs are the uprights.
The top and bottom pieces are called the head, ceiling or top-plate, and sole, floor or base-plate respectively.
The lines of short horizontal pieces joining the studs are called noggins.
Base plate
Noggins
Studs
Top plate
Centres

## Slide 21: Studwork
The studs are set vertically and parallel to each other. They are also set a certain distance apart, measured from the centre of each stud to the next. For general partitions this is usually 600mm centre (to allow for a 1200mm board), and 400mm (again for a 1200mm board) for kitchen or bathroom partitions that are to be tiled and require more rigidity.
Studwork can be set out by marking soleplate positions on the floor and squaring the corners using the 3/4/5 method.

## Slide 22: Studwork
The most efficient way to build studwork is to lay the plates down on a flat surface and cross-mark the stud positions and spacings ensuring that the studs all remain parallel. The studs are then cut to the same length and laid out in between the ready marked head and sole plates. The studs are then fixed using two nails or screws in each butt joint.
Noggins can be measured from the initial set-out and should all be cut the same size, apart from the outsides which are tailored to the width of the partition.

## Slide 23: Window frames
Windows are available in various styles, including box sash, casement, stormproof casement, fixed or roof light. They are made from materials including treated softwood, hardwood, aluminum and plastic.
Windows are generally made to measure and are fitted in various ways, depending on the style of window.
Windows can be fitted using cill bars, frame clips, frame fixings, or clip in linings, as with some plastic windows, and are normally sealed to the walls after fitting using mastic.

## Slide 24: Door frames
Door frames can be side hung, pivot hung, sliding or bi-fold, to mention just a few styles.
They are made from materials including treated softwood, hardwood, aluminum and plastic; these are generally used for external doors.
Door frames can be fitted using cill bars, frame clips, frame fixings, or clip-in linings, as with some plastic doors, and are normally sealed to the walls after fitting using mastic.

## Slide 25: Door frames
Door frames must be fixed securely enough to take the weight of the door and the stresses created by opening and closing, slamming and wind.
Door frames must be fitted plumb and free from twist. This ensures that the doors open level and do not catch the floor or soffit.

## Slide 26: Staircases
A joiner will draw the total rise and suitable going for a set of stairs.
Stairs are traditionally constructed using no metal fixings between the steps and the strings. The treads and risers shown are cramped, glued, wedged and finally blocked together to provide extra support. Risers are screwed to treads in this case. Site carpenters are sometimes expected to assemble stairs in situ.
Mike Jones

## Slide 27: Staircases
This jig is set up for the rise and going position on the stringers. A router can then be used to cut out the housings for the risers and treads.
The strings of the stairs are fixed to the newel using a barefaced tenon that is drawn tight using offset dowels. The proportions of the top tenon is thirds and the lower tenon is quarters.

## Slide 28: Staircases
Staircases in dwellings should have a minimum width of 900mm
Public buildings should have a minimum width of 1000mm between handrails or 1200mm between walls
Stairs should be made in sections if more than 2000mm wide

## Slide 29: Staircase requirements
Stairs must comply with section 1 (K1) of the Building Regulations.
When constructing private dwelling stairs, a step needs to comply with table 1.1 of K1.
  This provides:
  a minimum going of 220mm
  a maximum rise of 220mm
  a maximum pitch of 42º
Housing
Nosing line
Riser
Riser wedge
Tread
Tread wedge
Rise
Going
. 42°
Nosing
Max. pitch

## Slide 30: Staircase components
Inner string (closed)
Outer string (closed)
Tread
Riser
Newel post
Baluster (or spindle)
Banister (or handrail)
Base rail
Apron lining
Landing
Curtail step

## Slide 31: Staircase components
The image on the right shows a cut or ‘open’ string on the nearside, and a full or ‘closed’ string on the far side. It also shows a central bearer, or ‘carriage’ that supports the centre of the treads. Cut string stairs are common for sawn garden projects.
Open strung staircases are also common in older buildings and have return nosings which extend over the strings and decorative brackets on the visible side of the strings to cover the string cut where it meets the underside of the nosing.

## Slide 32: Linings
A lining is a piece of PSE or finished material that covers or lines studwork around openings such as doors and loft hatches. The jambs are usually housed into the head as shown.
The doorstop is then fitted to the lining to provide a slam and a tight seal, eradicating light gaps around the door. For fire doors these are deeper and contain intumescent strips which expand under heat sealing the gaps, thus reducing the spread of fire.

## Slide 33: Linings
Linings must be fitted plumb and free from twist. They are generally thinner and more flexible than frames, and therefore require carefully packing off behind the screws to avoid them being pulled out of shape.
Finally, architrave is fitted to complete the casing and create a decorative finish. This covers all the gaps created by packing off and those at the edges of the plasterboard.

## Slide 34
Any questions?