## Slide 1: PowerPoint 3: Materials used in wood occupations
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Construction and joinery timber
Timber relates to all wood that has been cut for use in construction.
  Types of timber
  Timber is categorised as either hardwood or softwood, depending on the type of tree the timber has been cut from. These two types of tree are different, and the timber from each has a different structure.
  Types of processed timber include:
  Manufactured timber
  Chemically treated timber
  Manufactured boards

## Slide 3: Softwoods
Softwood timber comes from coniferous trees, which are generally evergreen, have needle-like leaves and, in the case of pine trees, produce pinecones. They are normally less dense than hardwoods as they are faster growing. Common softwoods are:
  Redwood
  Pine (Scots, White, Yellow, Parana)
  Larch
  Cedar (Western Red)
  Spruce (European, Sikta)
  Douglas Fir
  Western Hemlock

## Slide 4: Common hardwoods
Hardwood timber comes from deciduous trees. These are generally broad-leaved trees which lose their leaves in the autumn, like oak, although this is not always the case. They are normally denser than softwoods as they are slower growing. Common hardwoods are:
  Oak (Red, White, Live)
  Mahogany (Sapele, Utile, Meranti)
  Teak (Iroko)
  Ash
  Beech
  Maple
  Cherry
  Balsa
  Walnut

## Slide 5: Engineered board and timber
  Plywood (glued and pressed laminated veneers)
  MDF (medium density fibreboard)
  OSB (oriented strand board)
  Fibreboard (one or two sided)
  Chipboard (particle board)
  Glulam beams (glue and laminated timber)
  Laminated flooring (board and solid timber laminate)
  Blockboard

## Slide 6: Softwood qualities and limitations
Species | Qualities | Limitations
Pine | Good figure, stainable and paintable | Very weak due to fast growth, marks easily, sap pockets
Larch | Weather resistant, readily available, Hard, strong | Splintering and splitting; too oily to paint. Sensitiser
Cedar | Weather resistant | Expensive, too oily to paint. Sensitiser. Splintering and splitting
Spruce | Cheap, fast growing | Sap pockets; loose grain
Douglas Fir | Medium strength and durability | Brittle; can split and mark easily, too oily to paint
Redwood | Good finish, medium strength and durability. weather resistance | Expensive. Sensitiser

## Slide 7: Hardwood qualities and limitations
Species | Qualities | Limitations
Oak | Hard, durable, strong, good figure, good finish, wide boards | Iron disease; shakes, end splitting; slow growing, slow drying. Sensitiser
Mahogany (sapele,utile) | Soft and dense, straight grain, fine finish, stable, wide boards | Overharvested, rare, expensive; slow growing. Sensitiser
Teak (Shorea,Iroko) | Water/ UV resistant, tight grained, easy to work | Expensive; brittle; blunting tools; oily. Sensitiser
Ash | Shock resistant, Light, good figure, strong, hard, good finish | Ash dieback; can end split; toxic. Not weatherproof. Hard to treat or polish. Brittle
Maple | Dense, hard, good figure, stable, Elastic, usable sapwood, | Low durability. Tool burn. Sensitiser
Cherry | Good figure, straight grain, easy to work, flexible, durable | Expensive, blemishes, water damage
Balsa | Soft, light easy to machine, buoyant, fast growing, sapwood | Weak; brittle,;splitting; sapwood is permeable

## Slide 8: Engineered board qualities and limitations
Type | Qualities | Limitations
Plywood | Many grades. Rigid and durable, can be flexible. Odd veneers for stability; smooth finish, paintable | Can delaminate or have voids and knots, no end grain fixing, blunting, Dust can be toxic (i.e eucalyptus)
MDF (medium density fibre board) | Stable and smooth. Can be treated, recycled, can be moulded and carved, Good finish for painting as no grain rise. | Can fluff and crumble, tooling burn, no end grain fixing, harmful dust, disintegrates in damp conditions even when treated
OSB (oriented strand board) | Cheap, recycled, relatively stable especially after fixing, water resistant, takes fixing better than chipboard | Brittle, not weatherproof, rough finish, not stable, blunting, no end grain fixing. Requires flat storage
LDF chipboard (particle board) | Can be treated, recycled. Cheap flooring material, can be moulded with mechanical tongue and groove allowing tight joints | Brittle, little flexibility, blunting, Poor screwing/nailing, edges can crumble, poor strength under direct compression
HDF hardboard (high density fibre board) | Very durable and water resistant, recycled, fibres exploded prior to pressing making it very dense | Expensive, is not always supplied in large sizes or thicknesses

## Slide 9: Other materials used by a carpenter: some examples
Type | Qualities | Limitations
UPVC | Stable and smooth. Does not require treating or painting. Takes fixings well and does not react to rust or rot | Can break down due to UV and weathering. Brittle and can chip. Very difficult to repair.
Metal studwork | Easy to mass produce and fix. Does not break down or rot quickly. Light and easy to transport. | Not as sturdy as timber stud. Can rip free from fixings as fixed through thin material. Can be difficult to fix to. Requires pattressing for heavy hangings.
Metal RSJ | Strong rolled steel H shaped sections for load bearing. Good span covering properties compared to concrete lintels | Harder to drill and shape than timber, cut edges can be sharp and swarf produced dangerous
Insulation board | Very light foamboards sandwiched between foil. Good heat and noise properties, waterproof | Toxic dust produced when cut, brittle
Rock wool | Light fibrous wool used to insulate lofts and services | Toxic dust can affect breathing and skin.

## Slide 10: Metal timber fixings: qualities and limitations
Type | Qualities | Limitations
Pozidriv screws | Mass produced and cheapest option for fast screwing | Can round off depending on use and material
Slot-head screws | Nice finish as slots can be lined up for door furniture | Can slip easily so manual fitting is necessary
Torx screws | Excellent grip and easier to use with no slipping | More expensive and less common
Wire pins | Small shaft and head making them easy to conceal | Can bend easily if not hit directly on the head. Heads can snap
Oval nails (brads) | Asymmetric wire nails in various lengths and thicknesses. Can be punched flush | Can bend easily if not hit directly on the head. Hammer can slip on small head.
Clout nails | Galvanized short fat nails with a large head that is nailed flush with surface. Ideal for fitting felt and joist hangers | Short shafts make them hard to hold and nail. Heads can collect moisture

## Slide 11: Metal timber fixings: qualities and limitations
Flat head or counter sunk screw. Designed so that the screw sits flush with the surface being fixed, so that the head will not catch.
Raised or oval head screw is a combination of the counter sunk and domed head. They are countersunk but the top of the head protrudes above the surface. They are largely used as a decorative feature.
Domed, round or pan head screws provide a larger surface area for the screw to ‘stop’ on the surface being fixed. These are ideal for a solid fix where there is no need for the screw head to be flush or below the surface of the material.
Bugle head screw is a variation of the counter sunk screw head, but the under surface of the head is curved, like a bugle. This reduces damage to plasterboard, reducing tearing of the paper, so is typically found on drywall screws.
Flange head screws provide a wide base and large surface area, while also providing a sturdy head for transfer of force through the drive. A flat washer is not generally required with these screw heads.

## Slide 12: Metal timber fixings: qualities and limitations
Preparation for fixing depends on the type of fixing used
Pilot holes are normally the size of the root diameter as shown to guide the screw through whilst leaving some material to pull on.
Clearance holes are the size of the major diameter, so the screw only takes to the timber being fixed to and does not pull on the top timber.

## Slide 13: Adhesives: qualities and limitations
Type | Qualities | Limitations
PVA glue | Cheap and effective water-based product; wipe off to clean up. Non-toxic | Can be affected by moisture. No initial bond; takes 24 hours for full bond
Polyurethane glue | Fast setting; easy to clean once dry. Strong & waterproof. Good penetration; gap filling | More expensive than PVA. Chemical that can be damaging and difficult to remove from skin
Resin glue | More expensive than PVA. Water-based but water resistant. Good initial tack and reduced clamping time compared to PVA | Shorter shelf life and fewer applications than PVA and not as strong as PU glue. Not gap filling
Cascamite or urea formaldehyde | Cheap as mixed from a powder as needed. Water and heat resistant | Limited work time before setting Poor shelf life containing chemical irritants
Gap filling adhesive | Strong initial tack and gap-filling properties | Hard to clean off so squeezing out not recommended

## Slide 14
Any questions?