## Slide 1: PowerPoint 7: Drawings and documents
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Drawings and documents used in wood occupations
Different documents are used in the construction industry for planning, designing and eventually constructing the project.
Some of these sources are written and some are visual, such as drawings, tables and charts.

## Slide 3: Drawings and documents used in wood occupations
Many different documents are used to manage and organise a project. These documents are associated with:
  planning permission
  building regulations
  construction designs
  low carbon outcomes
  contractual arrangements
  management of the project
  health and safety.

## Slide 4: Specifications
A specification is used to specify
a material or process that the designer requires to be met. It will have been agreed with the client.
    For example, the specification for cedar boarding would be: ‘22mm thick x 120mm wide boards with tongue and grooved edges, planed finish, untreated, fixed using secret nailing to softwood grounds.

## Slide 5: Schedules
The overarching schedule for site work will be the GANTT chart.
  GANTT chart or programme of works.
  Ground works and foundations schedule.
  Brick and blockwork schedule.
  First fix schedule.
  Second fix schedule.
  Snagging schedule.
Other more specific schedules will be drawn from these. For example, a door schedule would provide the door number from the drawing, its size and what ironmongery is to be fitted.

## Slide 6: Example of a schedule
Master Internal Door Schedule |  |  |  |  |  |  | 
Ref: | Door size | S.O. width | S.O. height | Lintel type | FD30 | Self closing | Floor level
D1 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D2 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D3 | 762 ×1981 | 824 | 2040 | BOX | No | No | GROUND FLOOR
D4 | 838 ×1981 | 900 | 2040 | N/A | Yes | No | GROUND FLOOR
D5 | 838 ×1981 | 900 | 2040 | BOX | Yes | Yes | GROUND FLOOR
D6 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D7 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D8 | 762 ×1981 | 824 | 2040 | N/A | Yes | No | FIRST FLOOR
D9 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | FIRST FLOOR
D10 | 762 ×1981 | 824 | 2040 | N/A | No | No | FIRST FLOOR
D11 | 686 ×1981 | 748 | 2040 | N/A | Yes | No | SECOND FLOOR
D12 | 762 ×1981 | 824 | 2040 | BOX | Yes | Yes | SECOND FLOOR
D13 | 762 ×1981 | 824 | 2040 | 100 HD BOX | Yes | Yes | SECOND FLOOR
D14 | 686 ×1981 | 748 | 2040 | N/A | No | No | SECOND FLOOR

## Slide 7: Programme of works
A programme of works is used to plan the activities on site in order to meet the client’s completion date. It allows site managers or supervisors to see if work is to schedule, what materials, labour and equipment are required, and when.
A number of computer programs are available to draw programmes of works. Programmes are often known as Gantt charts.
The activities are listed vertically and the time runs from left to right. Activities are often highlighted as ‘critical’ and form a path through the programme.
The next slide demonstrates a simplified programme of works.

## Slide 8
GANTT CHART |  | Calendar date |  |  |  |  |  |  |  | 
Works programmed | Required | 24th | 25th | 26th | 27th | 28th | 1st | 2nd | 3rd | 4th
Wall plates fitted Joists blocked off Pipe work finished | First fix Carpenters Scaffolders Plumbers | X |  |  |  |  |  |  |  | 
Groundwork inspection. Cut roof/dormer birdcage | NHBC Inspector First fix Carpenters Scaffolders |  | X | X | X |  |  |  |  | 
Electric first fix FF Soffits and facias | Electricians First fix Carpenters |  |  | X | X |  |  |  |  | 
Roof/eaves/dormer clad Joists covered GF | First fix Carpenters Scaffolders |  |  |  | X | X |  |  |  | 
Felt and batten Joists covered FF Walls rendered | First fix Carpenters Roofers Renderers |  |  |  |  | X | X |  |  | 
Roof tiled Studwork set out plates GF | First fix Carpenters Roofers |  |  |  |  |  | X | X | X | 
Scaffold and birdcage down Studwork GF | First fix Carpenters Scaffolders |  |  |  |  |  |  |  | X | 
Electric first fix GF Stairs delivered | Electricians Plumbers |  |  |  |  |  |  |  | X | X

## Slide 9: Bill of quantities
These documents are produced by the quantity surveyor. They summarise a project’s quantities and leave columns for a contractor to insert a price and complete a tender submission.
BILL OF QUANTITIES |  |  |  |  |  | 
Number | Item Description | Unit | Quantity | Rate | Amount | 
 |  |  |  |  | £ | p
A250 A290 A339.01 A339.02 A339.03 | CLASS A: GENERAL ITEMS Specified Requirements Testing of Materials Testing of recycled and secondary aggregates Information to be provided by the Contractor Production of Materials Management Plan Method Related Charges Recycling Plant/Equipment Mobilise; Fixed Operate; Time-Related De-mobilise; Fixed | sum sum sum sum sum |  |  |  | 

## Slide 10: Drawings
The two main methods of drawing production are:
  manual technical drawing
  CAD (computer aided design).
  Manual techniques involve the use of drawing equipment, a drawing board, paper, a sharp pencil and fine line pens.
  CAD uses a software package and a mouse to produce digital drawings. These are then printed digitally or as hard copies using a plotter.

## Slide 11: Drawing by hand
The basic equipment for drawing manually consists of a drawing board with a parallel rule or a T-square and various squares, compasses and protractors.
Fine line pens are used for a lighter more accurate line.
Drawings will usually be to scale which is listed in the corner along with other job details.

## Slide 12: Hand produced drawings
Drawings produced by hand require little outlay to produce and supply sufficient information for most projects.
Scale drawings may be copied onto a different paper size from the original, meaning that the scale cannot be measured using a scale rule.
Items drawn normally include measurements from various perspectives (elevations) to inform the user of all measurements.
Detail drawings can be used to create 1:1 setting out rods which can be used to produce detailed wooden joints.

## Slide 13: Scale
Scales are used to reduce the size of components or buildings down to a level that will fit on drawing paper. Different scales can be used to enlarge any component where more detail is required.
Typical scales in construction are:
  1:5 – used for detailed components
  1:100 – used for elevations and plan views
  1:500 – used for block plans
  1:1250 – used for location plans.

## Slide 14: Orthographic projection
Orthographic projection is a drawing where the front elevation of a structure has the plan view directly below it.
Side or end elevations are shown directly each side of the front elevation.
Elevation ‘A’
C
A
B
‘X’
Elevation ‘B’ ‘X’
Plan
Elevation ‘C’
Section ‘X–X’
Orthographic projection

## Slide 15: Orthographic projection
The 3D image shows how each 2D elevation is drawn in this type of projection.
Front elevation | 
Plan view | End elevation
E
F
P
Orthographic projection

## Slide 16: Isometric projection
An isometric projection shows the front elevation, side elevation and some of the plan. These are the three dimensions.
One corner of the structure is represented as closer to the viewer, with receding lines that are set at 30º to the base line.
The 3D effect makes it easier to visualise the complete structure.
90°
30°
Base line
Isometric projection

## Slide 17: CAD and BIM
Designers now use computer aided design (CAD) to work in 2D and 3D. Consultants’ drawings are often uploaded into one 3D model. This allows for any details to be coordinated across the whole project.
Building information modelling (BIM) allows production of 2D renderings as well as details on costings, schedules, materials and all the information required.

## Slide 18
Any questions?