## Slide 1: PowerPoint 6: Power tools
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Hazards associated with power tools
The most common hazards associated with the use of power tools:
  The rotational nature of cutting tools (centripetal force, entanglement)
  The power source
  Sharpness of cutters, knives and blades
  Loose metal accessories such as riving knives, fences or guards
  Misuse: e.g. when a power tool is used for something other than its intended purpose. An example would be using a crosscut blade to rip timber. This may cause the saw to bind which can result in kick back.
Tip: If you are a applying a lot of strength using a tool, you are using it wrong, using the wrong tool or the tool requires immediate maintenance.

## Slide 3: Power sources
The four main types of power supply for portable power tools are:
  battery
  110V mains supply
  230V mains supply
  compressed air.
Other types of power source are:
415V 3 Phase power to drive large fixed machinery
  canister gas: used alongside batteries in nail guns

## Slide 4: Power tool safety
For tools that need to be connected to a power supply this can be 230V (normal domestic mains supply) or 110V (as a reduced voltage via a transformer).
The use of tools at 230V is not recommended, as any electrical shock from the tool at this voltage can be fatal. If they are used, then an RCD (residual current device) should be used.
Only tools using a supply of 110V, reduced from 230V through a transformer, can be used on construction sites.
All power tools are now made with double insulation and should be stamped with a double insulation sign.
A permit must be obtained to use gas-fired nail guns.

## Slide 5: Transformers
Pictured is a 110V transformer. It is a legal requirement to use 110V tools on construction sites but not in workshops.
230V tools cannot be used or altered to be used with a transformer as the motors are made differently.
110V significantly reduces the risk of dying if you accidentally cut through a cable.

## Slide 6: Voltages
These are the plugs used with each voltage. Colours are used to indicate the voltage and make it clear which plugs fit together.
The position and numbers of pins inside the plug also indicate the voltage. They help ensure that the correct plug is used, making it impossible to connect two different colours
110V 1 phase – yellow
230V 1 phase – blue
400V 3 phase – red

## Slide 7: Legislation associated with power tools
Health and Safety at Work Act 1974
This is the main health and safety law that operates in the UK. It places a duty on employers to ensure that:
woodworking machinery is safe to use
a safe system of working is in place
workers are informed about all risks and hazards
all operatives are trained and competent to operate machinery.

## Slide 8: Legislation associated with power tools
  Provision and Use of Work Equipment Regulations (PUWER) 1998
These regulations place a duty upon all employers to ensure that:
equipment is suitable for the purpose it is being used for
woodworking tools are maintained
inspection of tools and machinery is undertaken
risks from using woodworking tools are minimised.

## Slide 9: Legislation
The Control of Noise at Work Regulations 2005
Woodworking machinery can be very noisy when it is being operated. Precautions must be taken to ensure that workers’ hearing is not damaged by the use of the equipment they are working with.
Measures to be taken may involve:
isolation of noisy machinery
training on its use
personal protective equipment (PPE) such as ear defenders

## Slide 10: Legislation
Approved codes of practice
The Health and Safety Executive (HSE) publishes an Approved Code of Practice in the safe use of woodworking machinery (ACOP).
This details all the measures that can be put in place to comply with each regulation.
For example, the training of woodworking machinists in operating different machines, protection against specific hazards, maintenance and inspection.

## Slide 11: Guidance: Health and Safety Executive guidance sheets
The HSE website provides several publications that can help with using woodworking machinery. These include:
circular saw safety posters
information about the risks of inhaling wood dust
Control of Substances Hazardous to Health (COSHH)
safe practice videos
sample risk assessments
guidance on manual handling in woodworking.

## Slide 12: Guidance: manufacturers’ specifications and service manuals
The manufacturers of woodworking machinery supply guidance documents on the operation, maintenance and use of their machines.
Guidance is needed on replacement parts, what lubrication is required, and cleaning and servicing routines.
This is a requirement under the HASWA 1974.
These leaflets provide valuable information on how to operate a machine correctly.

## Slide 13: Which tool do I need?
Impact drivers should not be used to fit fine work such as ironmongery because it is too aggressive. A combi drill or manual driver allows more control, avoiding damage to work and worker.
A dull blade on a circular saw can cause the user to force the saw through the timber. This can dull the blade further as it gets hot and becomes warped. A warped blade can cause the saw to jump.
There is a tool for every job. Your job is to identify the correct tool and to use and maintain it correctly. For example:

## Slide 14: Which tool do I need?
Some power tools must not be used in hazardous situations.
  Non-sparking tools in the presence of flammable vapours or dusts
  Insulated tools with appropriate ratings must be used for all work, especially outside
  Low vibration handles for long duration work
  Hot tools (that create heat or sparks) such as an angle grinder require a permit

## Slide 15: Power tools
Power tools carpenters use include:
  Combi drills, SDS drills, impactors, nailguns and screwguns
  Circular saws (portable, radial arm, compound mitre, rail)
  Jigsaws, reciprocating saws, multi-tools
  Power planers and sanders (belt, pad, orbital)
  Routers, laminate trimmers
  Angle grinders
  Biscuit jointers, engineered dowel jointers

## Slide 16: Power tools
Power tool which joiners use include:
  Combi drills, impactors, nailguns and screwguns
  Circular saws (portable, radial arm, compound mitre, rail, panel, dimension, rip)
  Jigsaws, bandsaws, fretsaws
  Power planers and sanders (belt, pad, orbital, linishers, drum sanders
  Routers, laminate trimmers, table routers, spindle moulders, tenoners
  Angle grinders, bench grinders,
  Biscuit jointers, engineered dowel jointers
  Morticers, pillar drills

## Slide 17: Drills and impactors
Power drills come in many different forms for many different jobs.
There are four main categories:
  drill drivers
  auto-feed screwdrivers
  percussion drills
  SDS hammer drills.
Many of these drills accompany each other when used on certain tasks. For example, an SDS hammer drill or percussion drill may be used to drill a hole into masonry, and then (after using the correct wall plug) the drill driver will be used to drive the screw into the plug providing a secure fixing.

## Slide 18: Drills and impactors
  Highly versatile and can be used with different bits.
  Combi drills pilot and through drill, countersink, insert and remove screws, cut circular holes with a saw cutter, or buff and polish.
  Impactors have a socket bit to negate slipping bits and impact as they turn to drive the fixing into the timber.
  Quick release chucks are available for combi drills enabling a rapid interchange of bits.
  Most drills and impactors are battery powered, making them safer to use

## Slide 19: SDS drills
  Have a hammer effect which is used to bore holes into hard masonry products such as bricks, blocks, stone and concrete.
  The rotation action is operated by a switch and is easy to discard.
  The still hammer action may be used when chasing walls.
  This drill also has a unique chuck which requires the drill bits to have a socket style of insert.

## Slide 20: Nail guns
  Nail guns usually come in first fix and lighter second fix models. The correct type and nail must be selected for the application required.
  Nail guns can be powered by battery, airline or battery and gas.
  Training is required to use nail guns as many accidents are common, including people shooting themselves in the chest or stomach.

## Slide 21: Drill bits and countersinks
Drill bits come with quick release socketed ends, as with SDS bits or plain bar ends which the chuck of a drill can clamp around.
Care should be taken that they are not bent and are fitted centrally
Countersinks create a conical hole for countersunk screws to fit snuggly into making them flush with or below the surface.
Countersunk screws can be easily removed and reused and do not damage the timber during retrieval.
Wood bits and countersinks should always be sharp. Some drill bits such as spade and spar bits can be honed with a diamond stone.
Auger bit
HSS metal bit
Normal masonry
Quick release bit holder
Spur wood bit
Flat wood or spade bit
SDS masonry bit
Counter sink and pilot hole

## Slide 22: Circular saws: portable circular saw
  The portable circular saw is primarily designed for cutting timber to length across the grain. It can be used to rip timber, but care must be taken that the correct blade is used to prevent the saw blade jamming – the blade can ‘bite’ and cause the saw to kick back towards the user.
  Using an appropriate fence and with various adjustments to the bed and depth of cut, it can also be used to cut:
  bevels
  compound bevels
  housings

## Slide 23: Circular saws: portable circular saw
Circular saws should always have the base flush and in full contact with the timber and, in this case, the temporary fence.
Some users will be tempted to sit the base on its toe and slowly lower the heel to make a plunge cut to save time. However, this operation is dangerous and most circular saws are fitted with a plunge stop allowing safe operation.
Riving knives should always be used unless plunge cutting. Wedges should be used behind the cut if binding to release pressure and avoid kick-back, when the saw can jump out of its channel, often towards the user.

## Slide 24: Circular saws: sliding compound mitre saw
  The saw is primarily designed for cutting timber to length across the grain.
  It can be used to cut straight and compound mitres as the blade both rotates on a flat plane and tilts on the vertical plane allowing it to cut two angles at once as in a jack rafter.
  As with all circular saws, care must be taken to avoid material kicking back if it gets trapped between blade and fence.
  With various adjustments it can also be used to cut:
  bevels
  compound bevels
  housings

## Slide 25: Circular saws: radial arm saw
  The radial arm saw is primarily designed for cutting timber to length across the grain.
  The extension table should be fitted to both sides and the timber held firmly against the fence.
  Care should be taken when cutting to prevent the saw blade jamming – the blade can ‘bite’ and pull itself into larger timber sections.
  With various adjustments to the arm, saw pivot and height, it can also be used to cut:
bevels
compound bevels
housings

## Slide 26: Table saws
Safe practice:
When using table saws, always set up the machine and extraction for safe operation.
Pictured is a feather board, which maintains pressure on the material – pushing it into the fence.
The removable hook is called a push stick. It enables the user to push the stock through without hands coming within 15cm (6 inches) of the blade.

## Slide 27: Table saws
Dimension saw
This saw is designed to cut (rip) timber along its length, as well as cutting sheet materials.
With its sliding table and adjustable fences, this is a versatile machine capable of producing square, bevelled and tapered cuts.

## Slide 28: Rip saws
This saw is designed to cut (rip) large timber stock along its length.
With its adjustable fence and large ripping blade, this is a machine capable of ripping most lengths and types of timber.
Normally three phase, as the motor needs to be powerful.

## Slide 29: Blades: crosscut blade
  This type of blade reduces breakout by cutting the fibres. A negative hook angle can tend to push the timber away from the saw blade.
  However, it also makes a stronger tooth point which can withstand the rigours of cutting across the grain of the timber.

## Slide 30: Blades: ripping blade
  This type of blade is designed to separate the fibres. The positive angle of hook teeth should only be used for ripping along the grain.
  The teeth tend to drive and bite progressively into the timber and may snatch when cross cutting.

## Slide 31: Blades: combination blade
This type of blade takes the characteristics of crosscut and rip blades and combines them into one blade.
A number of variations are available that can be used for cutting different materials.

## Slide 32: Kerf
  The kerf is produced by bending each tooth over in alternate directions as with a traditional hand saw.
  This type of set is known as ‘spring set’ and is used on parallel blades
Kerf: the total width of the saw cut

## Slide 33: TCT
  Tungsten carbide tipped (TCT) saw blades have a piece of tungsten brazed onto each tooth which is replaceable.
  The shape of the tungsten gives the saw blade its clearance (set).
  Most saw blades today use this type of cutting material on the tooth tips.
  It is a hard material that lasts longer and stays sharper
Kerf provided by the width of the tungsten carbide tips
TCT tips

## Slide 34: Gullet
The gullet is the gap between the saw blade teeth that removes the chips created by cutting the timber.
The image below shows different types of gullets and the different feed rates that can be applied to pushing timber through the saw
Smaller gullet
Less chip removal
Slower feed rate
Larger gullet
More chip removal
Quicker feed rate

## Slide 35: Chip limiter
    This reduces the amount that each tooth can cut and hence reduces the risk of kickback (material being forced back towards the operator).
Limits the amount each tooth can move
Anti-kickback safety feature
Tungsten carbide tipped

## Slide 36: Jigsaws and reciprocating saws
These saws use a fixed straight blade that moves in and out (and backwards and forwards in a pendulum action the case of jigsaws) to cut materials.
Jigsaws can be used to cut wood and metal and are designed for cutting curves.
Reciprocating saws are designed for the removal of old frames and fixings and can cut through wood and metal with ease.
Jigsaws also have a tilting bed allowing compound cuts.
Blades can bend making cuts out of square so not ideal for square cuts on thick timber.

## Slide 37: Routers
Components
Fine depth adjustment
Chuck and collet
Depth stop
Speed setting. This is reduced when using large diameter cutters
Trigger and safety switch
Handle
Body
Fence
Base
Fine adjustment for fence
Handle
Adjustable turret or castellation

## Slide 38: Routers
Routers are a very versatile power tool and have many uses.
They are a great power tool for carpenters and joiners.
Some possible uses are:
  cutting rebates
  cutting mouldings
  trimming and shaping timber products
  cutting curves
  notching mortices and housings.

## Slide 39: Router cutters
Ovolo cutter Rebate cutter Chamfer cutter Bullnose cutter V cutter
Dovetail cutter Trimming cutter Flute cutter Ogee cutter Cove cutter

## Slide 40: Power planers
Power planers are planes that can quickly and efficiently remove timber to a good finish.
They have removable knives or cutters, set in a spindle which rotates rapidly.
The front section of the baseplate is height adjustable, so the user can alter the depth of cut.
Take care to keep the bed flat and level, and to use the handles only. Most planers have belts, often with access gaps that can pinch fingers. As with all power tools, you must wait for the cutters to stop before putting it down.

## Slide 41
Any questions?