## Slide 1: PowerPoint 13: Mouldings
PowerPoint presentation
Unit 108: Wood occupations

## Slide 2: Mouldings
Types of mouldings include:
  architrave
  skirting board
  cornice
  pelmet
  dado rail
  picture rail
  plinth block
  staff and glazing bead.

## Slide 3: Mouldings
Dado rail
Cornice
Picture rail
Architrave
Plinth blocks
Skirting board

## Slide 4: Mouldings
Mouldings come in various shapes called profiles, defined by the silhouette showing the moulded front face.
These are machined by joiners or wood machinists using a spindle moulder.
6706_l2u209_Powerpoint_5
Ogee mould on a length of softwood architrave
Length of hardwood architrave with a torus mould

## Slide 5: Mouldings
Some other profiles are:
Ovolo
Lamb’s tongue
Reeded
Bullnosed
Pencil round
Chamfer
Splay
Button

## Slide 6: Scribing skirting
A scribe refers to cutting one piece of timber to the profile of another.
In this case the profile of one piece of skirting has been cut to follow the profile of another.
Skirting can also be scribed along its length into an uneven floor or wall by feathering the back or bottom edge.

## Slide 7: Direct scribe
Scribes can also be made by butting the two surfaces together and using a pair of compasses or scribing block to follow the profile of the surface being scribed to. This is a common method when scribing kitchen end panels to uneven walls.
Care must be taken to keep the scribe point and pencil level to the surface being scribed to, to maintain the correct height or position of the scribe detail.

## Slide 8: Cutting scribes from internal mitres
Scribes can be cut by cutting an internal mitre and following the profile of the cut with a coping saw or jigsaw.
This method requires two cuts and does not allow for the flooring or walls being out of level.

## Slide 9: Mitred mouldings
Mitred joints are two pieces cut at 45º to make a 90º or square corner.
They can be marked and cut diagonally across the face of the moulding, as in a picture frame or architrave, or across the depth of the moulding as with skirting boards.
Compound mitre saws are the most accurate, efficient and safe way to cut these joints on site.

## Slide 10: Architrave
The margin can be between 3mm and 12mm, depending on the width of the architrave, the depth of the keep for the lock and the depth of the hinges. The wider the architrave, the bigger the margin.
The margin should remain an equal distance around the lining and can be marked prior to installation with a pencil and combination square.
Architraves are pinned into the lining through the front of the mould, which is fragile and leaves a weak joint. The back of the architrave is therefore often fixed to the wall with mastic.
Standard size range
6mm to 9mm margin

## Slide 11
Any questions?