## Slide 1: PowerPoint 13: Application methods and techniques when applying plaster systems
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Types of plastering work
Heritage and conservation plastering work
Restoration plastering work
Modern plastering work
Maintenance work

## Slide 3: Traditional and modern materials
Advantages and disadvantages
Loose plastering materials
Factory batched materials
Pre-blended plastering materials

## Slide 4: Applying plastering systems
The type of plastering that can be carried out on internal walls within buildings will be restricted by the background’s surface.
Internal solid plastering can be classed as one, two or three coat work.
However, some surfaces will require additional plaster application .

## Slide 5: Plastering process
Pricking up coat on EML and timber lath
Dubbing out coat around stone/slate crevices
Scratch coat on uneven background surface
Floating coat is a backing coat for the finish
Finishing coat known as skim.

## Slide 6: Pricking up coat on to timber lath

## Slide 7: Pricking up coat on to expanded metal lath

## Slide 8: Scratch coat

## Slide 9: Floating coat
The floating process is applied approximately 10mm thick and ruled using one of the following methods:
Two coat work
Dot and screed
Box or broad screed
Free hand ruling.

## Slide 10: Ruling and devil floating
Applying, ruling and devil floating, preparing for the finishing plaster surface.

## Slide 11: Preparing floated walls
Floated wall surfaces need to be prepared by:
removing snots
cutting back at angles and ceiling lines
checking and cleaning and controlling suction.

## Slide 12: Applying and finishing plasters
Plasterers apply two applications of setting plaster.
Process of applying setting coats on plasterboard.

## Slide 13: One coat plaster
Although one coat work is generally related to the application of the setting coat, there are pre-mixed plasters that can be applied approximately 10mm thick and finished in one application.
This plaster is known as one coat plaster and it can also be applied by a spray machine.
Advantages.
Disadvantages.

## Slide 14: Defected plaster surfaces
Poor workmanship can lead to the following faults arising in the plastering work:
Surface staining
Blemishes
Blistering
Grinning
Snots
Shrinkage cracks
Hairline cracks
Efflorescence.

## Slide 15
Any questions?