## Slide 1: Session 3: Traditional and modern plastering materials: binders, aggregates, reinforcement and additives
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Traditional and modern plastering materials:
Binders
Aggregates
Additives
Reinforcements
Beads
Notes: Set Worksheet 9

## Slide 3: Sand
Sand is used as the aggregate to bulk the mix. Well-graded sand will have a uniform mix of small, medium and large grains and be angular in shape. Silt will prevent the cement from binding with the sand and cause the mix to be weak.
Types of sand
Dredged sand.
Pit sand.
Coarse sand/crushed aggregate.
Sea sand contains impurities such as shells, and is badly graded.

## Slide 4: Cement-based backing plasters
Cement is a binder that provides a faster set but also provides strength in the mix. The introduction of cement in undercoat mixes meant that building and plastering work would have faster setting times.
Cement mixed with sand and water will begin to set after 45 minutes and is normally completely set by the next day.
Brittle
Shrinkage
Curing

## Slide 5: Additives
Additives are designed to give the plaster a different characteristic and improve its performance. Additives can be liquid or powder form and include:
plasticisers
waterproofer
frostproofer/accelerators
retarders
bonding agents.
Always follow the manufacturer's instructions when using additives.

## Slide 6: Gypsum pre-blended plasters
Gypsum pre-mixed plasters have many advantages over traditional plastering materials, because they have been designed with speciﬁc application in mind.
Modern pre-mixed plasters are a mixture of gypsum and lightweight aggregates (vermiculite and perlite). There is a range of undercoat and setting coat plasters designed to be applied to different backgrounds.

## Slide 7: Gypsum pre-blended plasters
These plasters have many benefits:
They will set hard in under two hours, allowing several applications within the same day.
Their bonding capabilities are far greater than traditional plasters, which makes them more versatile.
Setting coat plasters are made to provide an excellent surface finish that can be trowelled smooth for decoration. This type of plaster finish can be applied on sand and cement undercoats, plasterboard and gypsum pre-mixed undercoat plaster.

## Slide 8: Cement and lime pre-mixed backing plaster
This undercoat plaster is a mixture of cement, lime, perlite
and synthetic ﬁbres that are added during manufacture to
improve its strength and binding ability and to help reduce
shrinkage.
This type of plaster is used on renovation work after a
chemical damp course has been installed or if moisture has
been a persistent presence in the background.
Like lime mortar mixes, this plaster allows walls to naturally
breathe, allowing trapped moisture to dry out from within
the masonry.

## Slide 9: Lime-based plasters
Lime mixes are mainly used in restoration of heritage and conservation work.
Non-hydraulic lime (or lime putty, pure lime, air lime, high calcium lime)
Sand is coarse/sharp aggregate
Reinforcements
Pozzolan additives
Earth pigments for colouring.
Finish coat: lime putty, ﬁne silica sand as ﬁller or ﬁne aggregate.
Notes: Set Worksheet 11
What are the advantages and disadvantages of using lime-based plasters?

## Slide 10: Types of beads
There is a range of different beads used for interior surfaces.
Standard angle beads.
Thin coat angle beads.
Stop beads.
Expansion beads.
Timber P beads (used on lime plaster)
Beads and trims are made from galvanised steel or plastic and come in standard lengths of 2.4mm.

## Slide 11: Reinforcements
Reinforcements are used to strengthen weak surfaces or improve the strength of mixes. They include:
fibres
EML
timber laths
self-adhesive scrim.

## Slide 12: Timber lath background

## Slide 13: Expanded metal lath

## Slide 14: Plasterboard
Plasterboard is a rectangular sheet manufactured from a Gypsum core, sandwiched between lining paper on both sides. It is used as a background surface in new and traditional buildings to form a dry construction background known as ‘dry lining’.
Used as a replacement to lath and plaster.
Pre-made dry product that only requires ﬁnishing by applying a setting coat.
Edges are either tapered or have a square edge.
Can be standard or performance rated.
Fixed with screws, nails or dabs.

## Slide 15: Performance plasterboard
Fire line
Moisture resistant
Vapour check
Sound check
Thermal laminate

## Slide 16: Storage of materials
Plastering materials need to be stored away from moisture and frost. You need to consider the following.
Loose material storage.
Bagged materials storage.
Containers.
Beads.
‘Use-by’ dates.
Stock rotation.
Contamination.
Corrosion.

## Slide 17: Casting plaster
Notes: Set Worksheet 12

## Slide 18
Any questions?