## Slide 1: PowerPoint 5: Understand how to prepare mixing and work areas for plastering
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Plan for plastering work
When setting up a mixing area you need to consider:
storage
clean water
dust extraction
electricity
mixing equipment
disposing of waste.

## Slide 3: Mixing pre-blended plaster

## Slide 4: Power tools
Mixing equipment loose materials

## Slide 5: Mixing traditional materials

## Slide 6: Setting up the work area

## Slide 7: Setting up the work area

## Slide 8: Access equipment
Access equipment is used to provide a safe means of working at height, reducing the risks of falls which can cause serious injury.
Notes: Set Worksheet 17

## Slide 9: Preparing surfaces
Key: how rough or smooth the background surface is.
Adhere/adhesion: how well plaster sticks or grips to the
background surface.
Suction: the rate of absorption from the background.
Low suction: a background that has little or no absorption.
Notes: Set Worksheet 18

## Slide 10: Laying trowels
A good plasterer will have several types of laying trowels: one for applying undercoats and another trowel for applying the ﬁnishing.

## Slide 11: Hawks/handboard
Hawks were traditionally made from timber, but today modern hawks are made from polyurethane or aluminium.

## Slide 12: Trowels
Bucket trowel
Pointing trowel
Gauging trowel

## Slide 13: Corner tools
Internal corner tool External corner tool

## Slide 14: Scratchers
A comb scratcher is used for keying undercoats.
A scarifier is used for keying lightweight undercoats.
A lath scratcher is used for lime backing plaster.

## Slide 15: Straight edges
Feathered edge straight edge
Box rule
Derby

## Slide 16: Spatula and sponge floats
Tools used for flattening and finishing plaster surfaces.

## Slide 17: Snips
Snips are used for cutting various types of trims, such as angle beads, stops and rolled EML before it is fixed onto the wall plate.

## Slide 18: Float
Used for consolidating undercoat surfaces to form either a plain smooth finish or a key, preparing for the setting coat. These floats are generally made from polyurethane.

## Slide 19: Spirit level
A spirit level can be used on its own or with a straight edge, which extends its length.
It is used for plumbing and levelling surfaces such as standard angle beads to window openings and returns.

## Slide 20: Water brushes
Used to apply water when finishing setting plaster.
Used to clean internal angles and frames.

## Slide 21: Small tools
Used in tight, difficult angles. The types shown here are leaf and square.
Notes: Set Worksheet 20

## Slide 22: Advantages of planning plastering work
Work is completed on time to the schedule.
Work is completed without distraction and interruptions.
Work is completed to budget.
Work is completed to the required standard.
Work is completed safely.

## Slide 23
Any questions?