## Slide 1: PowerPoint 7: Methods of preparing backgrounds
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Preparation of backgrounds
Plasterers must be able to identify different backgrounds and recognise the following characteristics of different background surfaces when applying plaster and fixing sheet materials:
strong and weak surfaces
poorly-keyed surfaces
high-suction surfaces
timber and metal backgrounds.

## Slide 3: Background characteristics
Key terms you need to know include the following.
Compatibility: the plaster materials used are the right strength for the background they are applied to.
Key: how rough or smooth the background surface is. Creating a rough surface on a background helps the plaster adhere to it.
Mechanical key: Mechanical scabbling tools are used on dense smooth surfaces to create a rough area that will result in a good key.
Expanded Metal Lathing (EML): Another good way of providing a background with reinforcement and key.
Suction: the rate at which a background absorbs moisture.

## Slide 4: Assessing backgrounds
One of the responsibilities of a plasterer is to examine and assess the surface characteristics of different backgrounds before applying plaster, to ensure the plaster adheres.
Checking the suction will tell you if the background is dry and porous.
No or low suction can indicate that the background is hard or dense.
High-suction backgrounds will absorb moisture from the plaster mix and may cause it to dry too quickly when applied.
Notes: Set Worksheet 26

## Slide 5: Hollow and solid blocks
Newly-constructed buildings that have block walling will need very little preparation before you apply plaster to their surface, because they have medium to adequate key.

## Slide 6: Lightweight aerated blocks
These blocks are lightweight and weak with an adequate key. This type of block has high-suction levels.
Cement-based mixes are not compatible with this background.

## Slide 7: Ceiling joists
There are several different types of plasterboard used in the industry, but they are all made with a plaster core within an outer skin of paper.
Timber ceiling joists
Check centres
Check they are linable

## Slide 8: Timber stud partitions
Timber stud walls to be covered with plasterboard:
centres of studs
sole plate
head
stud.

## Slide 9: Timber lath background
Laths were traditionally used on timber backgrounds. This type of background is still used in restoration of traditional and listed buildings.
It can be a time-consuming process to prepare, fix and plaster this surface.

## Slide 10: Existing solid plaster
This type of surface is common with solid walls that require a makeover.
Over-skim makeovers enhance the appearance of a wall by re-skimming the surface without removing the old plaster from the background.

## Slide 11: Clay bricks
Clay bricks were very popular at one time and can be found in all types of buildings. A common fault with clay bricks is that they shell their face, causing the plaster to ‘blow’.

## Slide 12: Concrete bricks
These bricks are made from coarse aggregate mixed with cement. This surface is smooth and hard, which means the key is poor and the suction is minimal.

## Slide 13: Engineering bricks
This is a hard, dense surface with poor key and no absorption rate. The face of the brick has a glossy surface that makes it difficult to prepare for plastering.

## Slide 14: Stone and slate backgrounds
Stone backgrounds can have rough or smooth surfaces. Due to their irregular shape and size, this background is very uneven and will require additional layers to dub out.

## Slide 15: Concrete lintels and pad stones
This surface is generally flat and hard with minimal suction. Concrete is used to make lintels and pad stones, which provide load-bearing surfaces above openings such as windows and doorways.

## Slide 16: Timber sheets or wall plates
This background generally has low suction and no key. Timber can move and twist with moisture contact.
Notes: Set Worksheet 27

## Slide 17: Plasters
Materials used for internal plastering range from traditional
loose ingredients to modern pre-blended bagged plaster in which only requires water. The main materials used are:
traditional lime-based plaster
traditional cement-based plaster
gypsum backing and finishing plasters.

## Slide 18: Sheet materials/plasterboard
Sheet materials and plasterboard are used more commonly today and have mostly replaced lath and plaster due to their increased performance, including:
fire resistance
insulation benefits
moisture resistance
impact resistance
soundproofing.
Notes: Set Worksheet 28

## Slide 19
Any questions?