## Slide 1: PowerPoint 10: Understand how to calculate quantities of plastering materials
PowerPoint presentation
Unit 109: Plastering and interior systems

## Slide 2: Good planning can save on costs
Being organised in advance with the correct labour, quantities of materials and resources means it will be less likely that problems occur. A disorganised workforce can be costly in the long run.
Risk assessments and method statements need to be produced before the work starts.
Materials and resources must be ordered in advance of the scheduled work to ensure deadlines are met.
Plastering materials need to be stored correctly to avoid damage.

## Slide 3: Aims
Understand how to calculate different formulas for measuring internal plastering and sheet materials using:
Linear
Perimeter
Area
Volume.

## Slide 4: Calculating quantities of materials
As a plasterer you will be required to measure and calculate a range of plastering materials for a contract.
This can include: loose sand, cement, lime, pre-mixed plasters, beads, sheet materials, additives, EML, fixings, reinforcements etc.
When tendering for plastering contracts, it is important to calculate accurately and not underestimate the quantity of materials as this can be very costly.
Allowances must be made for waste when calculating quantities.

## Slide 5: Units of measurements
When calculating for quantities of plastering materials, the following units are used for measuring:
Units | Materials
Linear measurements | Angle beads
Square metres | Plasterboard
Cubic metres | Three coat work
Litres | Additives/bonding agents
Kilograms | Cement
Tonnes | Sand

## Slide 6: Calculating
When calculating for plastering materials, we use the following basic operations:
Addition +
Subtraction -
Multiplication x
Division ÷

## Slide 7: Percentages %
An easy way to calculate the percentage (%) of a number is to divide the number by 100 and multiply it by the percentage figure you require.
20% is the number added for VAT on materials.
5% - 10% is a number used for adding waste when calculating quantities of materials for a contract.
Example: To increase 19m by 12%:
19 ÷ 100 = 0.19
0.19 × 12 = 2.28
19 + 2.28 = 21.28m
Total required 21.28m.

## Slide 8: Linear measurements
Linear measurements are how long an item measures.
Metal trims are measured by linear.
When fixing EML strips to wall plates we measure the quantity required by linear metres.
Plasterboard coving is another plastering material measured by linear.
When measuring a room for plasterboard coving we first measure the perimeter (four sides).
To find the linear measurement, add the length of all four walls and divide by the length of coving.
Notes: Set Worksheet 37

## Slide 9: Areas
To measure how much plaster or plasterboard material is required to cover a surface area of a wall or ceiling you need to calculate the area.
To find the area you multiply the length by its width (L x W).
Example
A standard plasterboard measures 2.4m long x 1.2m wide therefore there are 2.88m in every whole sheet used.

## Slide 10: Areas
Irregular shaped areas can be broken down into sections and then added together.
Side 6: 2.1m
Side 4
Side 2: 3.2m
Side 1
Side 5: 2.8m
Side 3: 2.5m
Step 1
Divide the area into two parts, and then calculate the area of each part. The easiest way to do this is to divide it into two smaller sections:
Section A Section B
Side 6: 2.1m
Side 5: 2.8m
Side 1
Side 4
Side 2: 3.2m
Side 3: 2.5m
Step 2
Work out the areas of section A and section B: section A = 2.1 × 2.8 = 5.88m²
section B = 2.5 × 3.2 = 8m²
Step 3
Add the areas of section A and section B together: section A + section B = total floor area
5.88 + 8 = 13.88m²
The total floor area is 13.88m².
Notes: Set Worksheet 38

## Slide 11: Perimeters and areas of circles
There are 3.142 diameters in one complete revolution

## Slide 12: Cube volume
The volume of an object is the total space it takes up. e.g. a container of plasticiser, a foundation or the capacity of a concrete mixer.
volume = length × width × height
Example 3
A joiner has a tin of preservative and needs to know its volume. The tin has a diameter of 250mm and a height of 700mm.
πr²h (π×r²×h) = volume
The radius (r) is half the diameter: 250 ÷ 2 = 125mm
3.142 × 0.125² × 0.700 = 0.034m³
The volume of the tin of paint is 0.034m³.
250mm
700mm
Notes: Set Worksheet 39

## Slide 13: Ratios
Ratios are often referred too when mixing different ingredients together to make a cement or lime-based plastering mix.
A typical ratio for a mix would be written as: 6:1:1 sand, cement and lime
6 represents the sand
1 represents the cement
1 represents the lime.
These would be mixed with equal gauge measures to ensure the correct proportion of each material to ensure the plaster mix is consistent in strength.

## Slide 14
Any questions?
Notes: Set Worksheet 40